## Slide 1
GPU Memory Optimization
Tiling and Recomputation in Modern Deep Learning Systems
1

## Slide 2
PART I
GPU Memory Architecture
Fundamentals
2

## Slide 3
Why Different Memories Have Different Speeds
SRAM (Shared Memory, Cache)
6 transistors per bit
(bistable latch — two cross-coupled inverters)
• Data stored as logic state, no charge
• Pure transistor switching → extremely fast
• No refresh needed
• 6T cell is large → low density, expensive
DRAM (HBM, DDR — Main Memory)
1 transistor + 1 capacitor per bit
(charge stored on capacitor)
• Capacitor leaks → needs periodic refresh
• Charge/discharge slower than switching
• 1T1C cell is tiny → high density, cheap
• Same area stores ~5× more bits than SRAM
Key: speed difference comes from physics: transistor switching (ns) vs capacitor charge/discharge (tens of ns)
3

## Slide 4
H100 Memory Hierarchy
Level | Type | Capacity | Bandwidth | Latency
Registers | SRAM | 256 KB/SM | — | ~0 cycles
Shared Mem / L1 | SRAM (6T) | 228 KB/SM | ~33 TB/s (agg.) | ~20–30 cyc
L2 Cache | SRAM | 50 MB | ~12 TB/s | ~200 cyc
HBM3 (VRAM) | 3D DRAM | 80 GB | 3.35 TB/s | ~400–500 cyc
CPU DRAM | DDR5 | ~hundreds GB | ~64 GB/s | ~100K cyc
HBM3 = DRAM + 3D Stacking + Wide Data Path
Cell-level speed is still DRAM (slow latency). Bandwidth boost comes from: (1) stacking 8 DRAM dies vertically via Through-Silicon Vias (TSV); (2) 1024-bit interface per stack vs ~384-bit for GDDR6. H100: 5 stacks × 1024-bit = 5120-bit total bus → 3.35 TB/s.
Interconnect Comparison
PCIe Gen5: 128 GB/s total (64 GB/s per direction)
NVLink 4.0 (GPU↔GPU): 900 GB/s total → 7× PCIe Gen5
NVLink-C2C (Grace↔Hopper): 900 GB/s, cache-coherent
Even NVLink is ~4× slower than HBM. CPU DRAM is always the slowest link.
4
Table 1. H100 memory hierarchy — capacity, bandwidth, and latency by level.

## Slide 5
H100 Physical Structure
GH100 die + 5 HBM3 stacks on a CoWoS-S silicon interposer (6 stack positions, 1 unused in H100)
HBM3 16 GB
HBM3 16 GB
HBM3 16 GB
HBM3 16 GB
HBM3 16 GB
(unused)
GH100 Die
814 mm² · TSMC 4N · 80 B transistors
132 SMs · 228 KB SRAM/SM · 50 MB L2
4th-gen Tensor Cores · TMA · WGMMA
TMA — Tensor Memory Accelerator
Dedicated HW unit for async HBM ↔ Shared Memory transfers.
Key properties
• Single thread issues request via copy descriptor
• HW handles address calc, bounds, transfer
• Fully async — other threads keep computing
• Frees registers & CUDA cores
→ Foundation for FA3's pipeline
5
Figure 1. H100 die + 5× HBM3 stacks on a CoWoS-S interposer.

## Slide 6
PART II
The Core Problem
+ Two Solution Strategies
6

## Slide 7
The Problem: Working Set > Memory Size
Standard self-attention: O = softmax(QKᵀ/√d) · V
Seq Length N | S = QKᵀ size (FP16) | H100 SRAM/SM | Ratio
4,096 | 32 MB | 228 KB | 140×
128K (GPT-4) | 32 GB | 228 KB | 140,000×
The N×N intermediate matrix cannot fit in SRAM → must be stored in HBM → 3 round-trips of O(N²) HBM reads/writes. Attention is memory-bound: Tensor Cores spend most time waiting for data.
Tiling
Break data into blocks that fit fast memory.
Compute block-by-block.
(Cache blocking / loop tiling)
Recomputation
Drop intermediate values to free memory.
Recompute them when needed.
(Trade compute for memory)
7
Table 2. Working set vs on-chip SRAM — the N×N attention matrix dwarfs SRAM.

## Slide 8
PART III
Tiling:
FlashAttention → FlashAttention-3
8

## Slide 9
Tiling: Two Layers of Benefit
A roadmap for this section — tiling helps on two distinct time scales
Layer 1 — Spatial Benefit (FA1 / FA2)
Break large data into blocks → working set fits SRAM → eliminate HBM round-trips
• S, P matrices never materialized in HBM (kernel fusion)
• HBM IO reduced from O(N²) to O(N²d²/M)
• A100 result: ~70% peak utilization
Layer 2 — Temporal Benefit (FA3)
Tiling creates a block loop → exposes pipeline parallelism across iterations
• Within one iteration: load → matmul → softmax (serial)
• Across iterations: load(i+1) ‖ matmul(i) ‖ softmax(i−1) (parallel!)
• No tiling → no loop → no pipeline opportunity
• H100 result: 35% → 85% peak utilization
9

## Slide 10
Standard Attention: Three Separate Kernels
Kernel 1
S = Q @ Kᵀ
→ write S (N×N) to HBM
Kernel 2
P = softmax(S)
→ read S from HBM, write P to HBM
Kernel 3
O = P @ V
→ read P from HBM, write O to HBM
Between kernels, data can ONLY communicate through HBM. Each kernel writes its output to HBM, the next kernel reads it back. This is a CUDA programming model constraint.
→ 3× O(N²) HBM round-trips. The S and P matrices are the bottleneck.
10

## Slide 11
FlashAttention: Tiling
FA paper (Dao et al. 2022) has two key techniques: tiling (forward, this slide) + recomputation (backward, Part IV).
Forward (simplified, FA2)
for each Q_block_i:
Load Q_i to SRAM
Init m_i = -∞, ℓ_i = 0, Õ_i = 0
for each K_block_j, V_block_j:
Load K_j, V_j to SRAM
S_ij = Q_i @ K_j.T # in SRAM
m_new = max(m_i, rowmax(S_ij))
P̃_ij = exp(S_ij − m_new)
ℓ_i = e^(m_i−m_new)·ℓ_i + rowsum(P̃_ij)
Õ_i = e^(m_i−m_new)·Õ_i + P̃_ij·V_j
m_i = m_new
O_i = Õ_i / ℓ_i # divide ONCE
Write O_i, L_i = m_i + log(ℓ_i) to HBM
Tiling (forward)
Block Q, K, V to fit SRAM. Fuse the 3 kernels into 1.
Online softmax keeps a running max + sum, so S, P never live in HBM.
Output O_i is divided by ℓ_i only once at the end of each Q block — minimizes non-matmul FLOPs.
HBM memory: O(N²) → O(N) HBM IO: Θ(N²d²/M) FLOPs: same O(N²d)
Result: A100 ~70%, H100 ~35% (motivates FA3 →)
11

## Slide 12
Online Softmax: Derivation
Block 1 = [x₁, x₂] Block 2 = [x₃, x₄] m₁ = max(B1) m₂ = max(B2) m = max(m₁, m₂)
shift by global max m
split by blocks
substitute local max m₁, m₂
Execution · track numerator & denominator separately, divide only at the end
After Block 1:
o₁ =
red = never computed · green = stored separately
Block 2 arrives, m = max(m₁,m₂):
o₂ =
12
Figure 4. Online softmax derivation — split by blocks then substitute local maxes.

## Slide 13
Online Softmax: Numerical Example
Scores = [1, 3, 2, 4] Block 1 = [1, 3] (m₁ = 3) Block 2 = [2, 4] (m₂ = 4)
m = 4
After Block 1 (m₁ = 3):
o₁ =
Block 2 arrives (m₂ = 4), m = 4, correction = e^(3-4) = 0.368:
o₂ =
softmax(x₁) = 0.050 / 1.553 = 0.032 ✓
13
Figure 5. Online softmax numerical example with scores [1, 3, 2, 4].

## Slide 14
FlashAttention-3: Three-Way Async Pipeline
Warp Specialization: Producer (TMA) + Consumer (WGMMA + MUFU) with circular SMEM buffer
Producer
(TMA load)
Consumer
(WGMMA)
Softmax
(MUFU)
Time →
T1
T2
T3
T4
T5
Load K₁V₁
Load K₂V₂
Load K₃V₃
Load K₄V₄
QK₁ᵀ GEMM
QK₂ᵀ GEMM
P₁V₁ GEMM
P₂V₂ GEMM
softmax₁
softmax₂
All 3 units active
Why this matters: H100 matmul = 989 TFLOPS, but exp (softmax) = 3.9 TFLOPS — 256× gap. Serial = idle HW.
setmaxnreg: producer warps donate registers to consumer → larger GEMM tiles
Circular SMEM buffer: classic OS producer-consumer + ring buffer (double/triple buffering)
14
Figure 2. FlashAttention-3 three-way async pipeline — TMA producer + WGMMA consumer + MUFU softmax.

## Slide 15
FlashAttention Performance Comparison
Implementation | H100 TFLOPS | Utilization | vs FA2
FlashAttention-2 (baseline) | ~350 | ~35% | 1.0×
FlashAttention-3 BF16 | ~840 | ~85% | 2.4×
FlashAttention-3 FP8 | ~1,300 | — | 3.7×
FA3 nearly doubles utilization on H100 by adding the temporal pipeline (Layer 2). FP8 squeezes out another 1.5× on top.
15
Table 3. FlashAttention performance comparison on H100 (BF16/FP8).

## Slide 16
PART IV
Recomputation:
FlashAttention Backward + Gradient Checkpointing
16

## Slide 17
FlashAttention Backward: Recomputation
Don't store the N×N attention matrices — regenerate them on-chip during the backward pass.
Standard backward
Forward stores S, P (each N×N) in HBM.
Backward reads them back to compute gradients.
Memory: O(N²) per layer
FA backward (recomputation)
Forward stores only the log-sum-exp L_i (size N).
Backward recomputes S, P block-by-block from Q, K, V.
Memory: O(N) per layer
How is recompute so cheap?
Because L_i = m_i + log(ℓ_i) was already computed and saved in forward. So in backward:
1. S_ij = Q_i @ K_j.T (one matmul, on-chip)
2. P_ij = exp(S_ij − L_i) (one elementwise op — no re-doing online softmax!)
3. Use S, P with dO to compute dQ, dK, dV — all in SRAM, no HBM reads of N×N matrices.
The numbers (FA1 paper, GPT-2 medium on A100, seq 1024, batch 64):
Standard → 66.6 GFLOPs, 40.3 GB HBM IO, 41.7 ms
FlashAttention → 75.2 GFLOPs (+13%), 4.4 GB HBM IO (9× less), 7.3 ms (5.7× faster)
→ Attention is memory-bound. Trading +13% FLOPs for 9× less HBM IO is a huge win.
17

## Slide 18
Gradient Checkpointing (1/2): The Activation Problem
Forward pass must store every layer's activation for backward — activation memory scales with depth L.
Why activations dominate memory (not weights)
Weights
Fixed size. Shared across all inputs.
7B model FP16:
= 14 GB (always, regardless of batch)
Does NOT grow with:
• batch size
• sequence length
Activations
Per-sample × per-layer intermediate state.
7B, batch=8, seq=2048:
≈ 32 layers × ~1.3 GB/layer ≈ 40 GB
GROWS linearly with:
• batch × sequence × layers
14 GB vs 40 GB
Activations are ~3× larger than weights and grow with batch / seq. With long context they can exceed 10× the weight memory.
18

## Slide 19
Gradient Checkpointing (2/2): The √L Solution
Don't store everything. Store one checkpoint every √L layers. Recompute the rest during backward.
Standard: store all activations
[L1]→[L2]→[L3]→[L4]→[L5]→[L6]
✓ ✓ ✓ ✓ ✓ ✓
Memory: O(L)
Checkpointed: store every √L
[L1]→ x →[L3]→ x →[L5]→ x
✓ free ✓ free ✓ free
Memory: O(√L)
Why √L? Minimize total memory: L/k checkpoints + k layers buffered during recompute
Trade-off: ~33% extra compute (one extra forward pass during backward) OS analogy: swap / demand paging
from torch.utils.checkpoint import checkpoint; x = checkpoint(self.attn, x, use_reentrant=False)
19

## Slide 20
PART V
Summary
20

## Slide 21
Same Ideas, Different Hardware
These memory-management problems are not new — they appear across the systems stack
GPU Technique | Mechanism | Related Idea in OS / Systems
Tiling Strategy (working set > SRAM) |  | 
FA tiling | Compute on blocks that fit SRAM | Cache blocking / loop tiling
FA3 warp specialization | Producer-consumer with ring buffer | Async I/O pipelines, DMA double-buffering
Recomputation Strategy (working set > HBM) |  | 
FA recomputation (backward) | Drop S, P; recompute from Q, K, V on-chip | Trade compute for memory (within attention)
Gradient Checkpointing | Drop activations, recompute in backward | Same idea, applied at layer granularity
Memory hierarchies have always been about fast-but-small vs. slow-but-large. GPUs just made the gap more extreme.
21
Table 4. GPU memory techniques and their analogues in classical OS/systems design.

## Slide 22
Thank You
22