## Slide 1: CSC6032 – Advanced Operating Systems Distributed Shared Memory (DSM)
Prof. Yeh-Ching Chung
School of Data Science
Chinese University of Hong Kong, Shenzhen

## Slide 2: Shared Memory
On-Chip Memory
extension
CPU
Memory
Chip package
Address and data lines Connecting the CPU to the memory
A single-chip computer
CPU1
Memory
CPU4
CPU2
CPU3
A hypothetical shared-memory Multiprocessor

## Slide 3: Bus-Based Multiprocessors
CPU
CPU
CPU
Memory
Bus
A multiprocessor
CPU
Cache
CPU
CPU
Cache
Cache
Memory
Bus
A multiprocessor with caching

## Slide 4: Write Through Protocol
Event | Action taken by a cache in response to its own CPU’s operation | Action taken by a cache in response to a remote CPU’s operation
Read miss | Fetch data from memory and store in cache | no action
Read hit | Fetch data from local cache | no action
Write miss | Update data in memory and store in cache | no action
Write hit | Update memory and cache | invalidate cache entry

## Slide 5: Write Once Protocol
This protocol manages cache blocks, each of which can be in one of the following three states
  INVALID: This cache block does not contain valid data.
  CLEAN: Memory is up-to-date; the block may be in other caches.
  DIRTY: Memory is incorrect; no other cache holds the block.
The basic idea of the protocol is that a word that is being read by multiple CPUs is allowed to be present in all their caches. A word that is being heavily written by only one machine is kept in its cache and not written back to memory on every write to reduce bus traffic.

## Slide 6: Example (1)
A
B
W1
C
W1
CLEAN
Memory is correct
Initial state – word W1 containing
value W1 is in memory and is also
cached by B.
CPU
A
B
W1
C
W1
W1
CLEAN
CLEAN
Memory is correct
(b) A reades word W and gets W1. B does
not respond to the read, but the memory
does.

## Slide 7: Example (2)
A
B
W1
C
W2
W1
A
B
W1
C
W3
W1
DIRTY
INVALID
DIRTY
INVALID
Memory is correct
(c) A write a value W2, B snoops on the bus, sees the write and invalidates its entry. A’s copy is marked DIRTY.
Not update memory
Memory is correct
(d) A write W again. This and subsequent writes by A are done locally, without any bus traffic.

## Slide 8: Example (3)
A
B
W1
C
W3
W1
INVALID
INVALID
DIRTY
W3
(e) C reads or writes W. A sees the request by snooping on the bus, provides the value, and invalidates its own entry. C now has the only valid copy.
Not update memory

## Slide 9: Ring-Based Multiprocessors - Memnet
CPU
CPU
CPU
CPU
CPU
CPU
CPU
Private memory
MMU
Cache
Home
memory
Memory management unit
Location
Interrupt
Home
Exclusive
Valid
0
1
2
3
The block table

## Slide 10: Protocol (1)
Read
  When the CPU wants to read a word from shared memory, the memory address to be read is passed to the Memnet device, which checks the block table to see if the block is present. If so, the request is satisfied. If not, the Memnet device waits until it captures the circulating token, puts a request onto the ring. As the packet passes around the ring, each Memnet device along the way checks to see if it has the block needed. If so, it puts the block in the dummy field and modifies the packet header to inhibit subsequent machines from doing so.
  If the requesting machine has no free space in its cache to hold the incoming block, to make space, it picks a cached block at random and sends it home. Blocks whose Home bit are set are never chosen because they are already home.

## Slide 11: Protocol (2)
Write
  If the block containing the word to be written is present and is the only copy in the system (i.e., the Exclusive bit is set), the word is just written locally.
  If the needed block is present but it is not the only copy, an invalidation packet is first sent around the ring to force all other machines to discard their copies of the block about to be written. When the invalidation packet arrives back at the sender, the Exclusive bit is set for that block and the write proceeds locally.
  If the block is not present, a packet is sent out that combines a read request and an invalidation request. The first machine that has the block copies it into the packet and discards its own copy. All subsequent machines just discard the block from their caches. When the packet comes back to the sender, it is stored there and written.

## Slide 12: Switched Multiprocessors
Two approaches can be taken to attack the problem of not enough bandwidth
  Reduce the amount of communication. E.g. Caching.
  Increase the communication capacity. E.g. Changing topology.
One method is to build the system as a hierarchy. Build the system as multiple clusters and connect the clusters using an intercluster bus. As long as most CPUs communicate primarily within their own cluster, there will be relatively little inter-cluster traffic. If still more bandwidth is needed, collect a bus, tree, or grid of clusters together into a supercluster, and break the system into multiple superclusters.

## Slide 13: Dash (1)
A Dash consists of 16 clusters, each cluster containing a bus, four CPUs, 16M of the global memory, and some I/O equipment. Each CPU is able to snoop on its local bus, but not on other buses.
The total address space is 256M, divided up into 16 regions of 16M each. The global memory of cluster 0 holds addresses 0 to 16M, and so on.

## Slide 14: Dash (2)
C
C
C
M
C
C
C
M
C
C
C
M
Three clusters connected by
an intercluster bus to form one
supercluster.
Cluster
Interacluster bus
Intercluster bus

## Slide 15: Supercluster
C
C
C
M
C
C
C
M
C
C
C
M
C
C
C
M
C
C
C
M
C
C
C
M
Supercluster bus
CPU with cache
Global memory
Connect 2 clusters via supercluster bus

## Slide 16: Caching
Caching is done on two levels: a first-level cache and a larger second-level cache.
Each cache block can be in one of the following three states:
UNCACHED—The only copy of the block is in this memory.
CLEAN—Memory is up-to-date; the block may be in several caches.
DIRTY—Memory is incorrect; only one cache holds the block.

## Slide 17: NUMA Multiprocessors (1)
Like a traditional UMA (Uniform Memory Access) multiprocessor, a NUMA machine has a single virtual address space that is visible to all CPUs. When any CPU writes a value to location a, a subsequent read of a by a different processor will return the value just written.
The difference between UMA and NUMA machines lies in the fact that on a NUMA machine, access to a remote memory is much slower than access to a local memory.

## Slide 18: NUMA Multiprocessors (2)
CPU
M
I/O
Local bus
Cluster
CPU
M
I/O
CPU
M
I/O
Inter-cluster bus
Local memory
Microprogrammed MMU
Connection machine (CM2)

## Slide 19: NUMA Multiprocessors (3)
7
10
0
1
2
3
4
.5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
.5
6
8
9
11
12
13
14
15
Switch
BNN Butterfly

## Slide 20: Properties of NUMA Multiprocessors
Access to remote memory is possible
Accessing remote memory is slower than accessing local memory
Remote access times are not hidden by caching

## Slide 21: NUMA Algorithms
In NUMA, it matters a great deal which page is located in which memory. The key issue in NUMA software is the decision of where to place each page to maximize performance.
A page scanner running in the background can gather usage statistics about local and remote references. If the usage statistics indicate that a page is in the wrong place, the page scanner unmaps the page so that the next reference causes a page fault.

## Slide 22: Comparison of Shared Memory Systems (1)
Single-bus
multi-processor
Switched
multi-
processor
NUMA
machine
Page-
based
DSM
Shared-
variable
DSM
Object-
based
DSM
Cache
block
Cache
block
Page
Page
Data structure
Object
Loosely coupled
Tightly coupled
Transfer unit
Sequent
Firefly
Dash
Alewife
Cm*
Butterfly
Ivy
Mirage
Munin
Midway
Linda
Orca
Remote access in hardware
Remote access in software
Managed by MMU
Managed by OS
Managed by language
runtime system
Hardware-controlled caching
Software-controlled caching

## Slide 23: Comparison of Shared Memory Systems (2)
Item | Single bus | Switched | NUMA | Page based | Shared variable | Object based
Linear, shared virtual address space? | Yes | Yes | Yes | Yes | No | No
Possible operations | R/W | R/W | R/W | R/W | R/W | General
Encapsulation and methods? | No | No | No | No | No | Yes
Is remote access possible in hardware? | Yes | Yes | Yes | No | No | No
Is unattached memory possible? | Yes | Yes | Yes | No | No | No
Who converts remote memory accesses to messages? | MMU | MMU | MMU | OS | Runtime system | Runtime system
Transfer medium | Bus | Bus | Bus | Network | Network | Network
Data migration done by | Hardware | Hardware | Software | Software | Software | Software
Transfer unit | Block | Block | Page | Page | Shared variable | Object
Multiprocessors
DSM

## Slide 24: Consistency Models
Strict Consistency - Any read to a memory location x returns the value stored by the most recent write operation to x
Strict consistency
P1: W(x)1
P2: R(x)1
Not strict consistency
P1: W(x)1
P2: R(x)0 R(x)1

## Slide 25: Sequential Consistency (1)
The result of any execution is the same as if the operations of all processors were executed in some sequential order, and the operations of each individual processor appear in this sequence in the order specified by its program.

## Slide 26: Sequential Consistency (2)
P1: W(x)1 P1: W(x)1
P2: R(x)0 R(x)1 P2: R(x)1 R(x)1
Two possible results of running the same program
a=1; b=1; c=1;
print(b,c); print(a,c); print(a,b);
Three parallel processes: P1, P2, P3.
P1P2P3: 00 00 00 is not permitted.
P2P2P3: 00 10 01 is not permitted.
All processes see all shared accesses in the same order.

## Slide 27: Causal Consistency (1)
Writes that are potentially causally related must be seen by all processes in the same order. Concurrent writes may be seen in a different order on different machines.
P1: W(x)1 W(x)3
P2: R(x)1 W(x)2
P3: R(x)1 R(x)3 R(x)2
P4: R(x)1 R(x)2 R(x)3
This sequence is allowed with causally consistent memory, but not with sequentially consistent memory or strictly consistent memory.

## Slide 28: Causal Consistency (2)
P1: W(x)1
P2: R(x)1 W(x)2
P3: R(x)2 R(x)1
P4: R(x)1 R(x)2
A violation of causal memory
P1: W(x)1
P2: W(x)2
P3: R(x)2 R(x)1
P4: R(x)1 R(x)2
A correct sequence of events in causal memory
All processes see all casually-related shared accesses in the same order.

## Slide 29: PRAM Consistency
Writes done by a single process are received by all other processes in the order in which they were issued, but writes from different processes may be seen in a different order by different processes.
P1: W(x)1
P2: R(x)1 W(x)2
P3: R(x)1 R(x)2
P4: R(x)2 R(x)1
A valid sequence of events for PRAM consistency but not for the above stronger models.

## Slide 30: Processor Consistency
Processor consistency is PRAM consistency + memory coherence. That is, for every memory location, x, there be global agreement about the order of writes to x. Writes to different locations need not be viewed in the same order by different processes.

## Slide 31: Weak Consistency (1)
The weak consistency has three properties
Accesses to synchronization variables are sequentially consistent.
No access to a synchronization variable is allowed to be performed until all previous writes have completed everywhere.
No data access (read or write) is allowed to be performed until all previous accesses to synchronization variables have been performed.

## Slide 32: Weak Consistency (2)
P1: W(x)1 W(x)2 S
P2: R(x)1 R(x)2 S
P3: R(x)2 R(x)1 S
A valid sequence of events for weak consistency.
P1: W(x)1 W(x)2 S
P2: S R(x)
An invalid sequence for weak consistency.
P2 must get 2 instead of 1 because it is already synchronized.
Shared data can only be counted on to be consistent after a synchronization is done.

## Slide 33: Release Consistency
Release consistency provides acquire and release accesses. Acquire accesses are used to tell the memory system that a critical region is about to be entered. Release accesses say that a critical region has just been exited.
P1: Acq(L) W(x)1 W(x)2 Rel(L)
P2: Acq(L) R(x)2 Rel(L)
P3: R(x)1
A valid event sequence for release consistency. P3 does not acquire, so the result is not guaranteed.

## Slide 34: Lazy Consistency
Shared data are made consistent when a critical region is exited.
In lazy release consistency, at the time of a release, nothing is sent anywhere. Instead, when an acquire is done, the processor trying to do the acquire has to get the most recent values of the variables from the machine or machines holding them.

## Slide 35: Entry Consistency
Shared data pertaining to a critical region are made consistent when a critical region is entered.
Formally, a memory exhibits entry consistency if it meets all the following conditions:

## Slide 36: Page-Based Distributed Shared Memory
These systems are built on top of multicomputers, that is, processors connected by a specialized message-passing network, workstations on a LAN, or similar designs. The essential element here is that no processor can directly access any other processor’s memory.

## Slide 37: Chunks of Address Space Distributed (1)
0
2
5
9
1
3
6
8
4
7
11
12
13
15
10
14
CPU1
CPU2
CPU3
CPU4
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Shared global address space
Memory

## Slide 38: Chunks of Address Space Distributed (2)
0
2
5
9
1
3
6
8
4
7
11
12
13
15
10
14
CPU1
CPU2
CPU3
CPU4
Situation after CPU 1 References Chunk 10

## Slide 39: Chunks of Address Space Distributed (3)
0
2
5
9
1
3
6
8
4
7
11
12
13
15
10
14
CPU1
CPU2
CPU3
CPU4
10
Situation if chunk 10 is read only and replication is used

## Slide 40: Replication
One improvement to the basic system that can improve performance considerably is to replicate chunks that are read only.
Another possibility is to replicate not only read-only chunks, but all chunks. No difference for reads, but if a replicated chunk is suddenly modified, special action has to be taken to prevent having multiple, inconsistent copies in existence.

## Slide 41: Granularity
when a nonlocal memory word is referenced, a chunk of memory containing the word is fetched from its current location and put on the machine making the reference. An important design issue is how big should the chunk be? A word, block, page, or segment (multiple pages).

## Slide 42: False sharing
A
B
A
B
Code using A
Code using B
Processor 1
Processor 2
Shared
page
Two
unrelated
shared
variables

## Slide 43: Finding the Owner (1)
The simplest solution is by doing a broadcast, asking for the owner of the specified page to respond.
  Drawback: broadcasting wastes network bandwidth and interrupts each processor, forcing it to inspect the request packet.
Another solution is to designate one process as the page manager. It is the job of the manager to keep track of who owns each page. When a process P wants to read or write a page it does not have, it sends a message to the page manager. The manager sends back a message telling who the owner is. Then P contacts the owner for the page.

## Slide 44: Finding the Owner (2)
An optimization is to let manager forwards the request directly to the owner, which then replies directly back to P.
Drawback: heavy load on page manager.
Solution: having more page managers. Then how to find the right manager? One solution is to use the low-order bits of the page number as an index into a table of managers. Thus with eight page managers, all pages that end with 000 are handled by manager 0, all pages that end with 001 are handled by manager 1, and so on. A different mapping is to use a hash function.

## Slide 45: Finding the Owner (3)
Page manager
Owner
P
1. Request
2. Reply
3. Request
4. Reply
Page manager
Owner
P
1. Request
2.Request forwarded
3. Reply

## Slide 46: Find the Copies
The first is to broadcast a message giving the page number and ask all processors holding the page to invalidate it. This approach works only if broadcast messages are totally reliable and can never be lost.
The second possibility is to have the owner or page manager maintain a list or copyset telling which processors hold which pages. When a page must be invalidated, the old owner, new owner, or page manager sends a message to each processor holding the page and waits for an acknowledgement. When each message has been acknowledged, the invalidation is complete.

## Slide 47: Page Replacement (1)
If there is no free page frame in memory to hold the needed page, which page to evict and where to put it?
  Use traditional virtual memory algorithms, such as LRU.
  In DSM, a replicated page that another process owns is always a prime candidate to evict because another copy exists.
  The second best choice is a replicated page that the evicting process owns. Pass the ownership to another process that owns a copy.
  If none of the above, then a nonreplicated page must be chosen. One possibility is to write it to disk. Another is to hand it off to another processor.

## Slide 48: Page Replacement (2)
Choosing a processor to hand a page off to can be done in several ways
  1. Send it to home machine which must accept it.
  2. The number of free page frames could be piggybacked on each message sent, with each processor building up an idea of how free memory was distributed around the network.

## Slide 49: Synchronization
In a DSM system, as in a multiprocessor, processes often need to synchronize their actions. A common example is mutual exclusion, in which only one process at a time may execute a certain part of the code. In a multiprocessor, the TEST-AND-SET-LOCK (TSL) instruction is often used to implement mutual exclusion. In a DSM system, this code is still correct, but is a potential performance disaster.

## Slide 50: Shared-Variable in Distributed Shared Memory
share only certain variables and data structures that are needed by more than one process.
Two examples of such systems are Munin and Midway.

## Slide 51: Munin
Munin is a DSM system that is fundamentally based on software objects, but which can place each object on a separate page so the hardware MMU can be used for detecting accesses to shard objects.
Munin is based on a software implementation of release consisency.

## Slide 52: Release Consistency in Munin
a, b, c
a, b, c
Process 1
Process 2
Process 3
Network
Lock(L);
a=1;
b=2;
c=3;
Unlock(L);
Changes to
shared
variables
Get exclusive access to this critical region
Critical region

## Slide 53: Use of Twin Pages in Munin
Word 4
6->8
6
6
8
6
8
6
6
Page
Read-only mode
Originally
After write
trap
After write
has completed
At release
R
Twin
RW
Twin
RW
Twin
RW
Message sent

## Slide 54: Directories
Munin uses directories to locate pages containing shared variables.
Root
P1
P2
P3
P4
P1
P1
P1
P2
P2
P2
P3
P4
P4
P1
P3
P4
P1

## Slide 55: Midway
Midway is a distributed shared memory system that is based on sharing individual data structures. It is similar to Munin in some ways, but has some interesting new features of its own.
Midway supports entry consistency

## Slide 56: Object-based Distributed Shared Memory
In an object-based distributed shared memory, processes on multiple machines share an abstract space filled with shared objects.
Process
Object space
Object

## Slide 57: Linda (1)
Tuple Space - A tuple is like a structure in C or a record in Pascal. It consists of one or more fields, each of which is a value of some type supported by the base language.
For example,
(“abc”,2,5)
(“matrix-1”,1,6,3.14)
(“family”,”is-sister”,”Carolyn”,”Elinor”)

## Slide 58: Linda (2)
Operations on Tuples
Out, puts a tuple into the tuple space. E.g. out(“abc”,2,5);
In, retrieves tuple from the tuple space.
In(“abc”,2,?j);
If a match is found, j is assigned a value.

## Slide 59: Linda (3)
A common programming paradigm in Linda is the replicated worker model. This model is based on the idea of a task bag full of jobs to be done. The main process starts out by executing a loop containing
Out(“task-bag”,job);
In which a different job description is output to the tuple space on each iteration. Each worker starts out by getting a job description tuple using
In(“task-bag”,?job);
Which it then carries out. When it is done, it gets another. New work may also be put into the task bag during execution. In this simple way, work is dynamically divided among the workers, and each worker is kept busy all the time, all with little overhead.

## Slide 60: Orca
Orca is a parallel programming system that allows processes on different machines to have controlled access to a distributed shared memory consisting of protected objects.
These objects are a more powerful form of the Linda tuple, supporting arbitrary operations instead of just in and out.
Orca has a fork statement to create a new process on a user-specified processor, i.e., for I in 1.. n do fork foobar(s) on I