## Slide 1: KVM VIRTUALIZATION: LEVERAGING I/O VIRTUALIZATION ON QorIQ PLATFORMS FOR VNFS
PUBLIC USE
BHARAT BHUSHAN PRINCIPAL STAFF ENGINEER DIANA CRĂCIUN
SOFTWARE ENGINEER
FTF-NET-N1844 MAY 2016

## Slide 2: Software Products and Services
1 EXTERNAL USE
Integration Services
Solutions Reference
Development Tools Runtime Products
Visit us in the Tech Lab – #247
Deliver Commercial Software, Support, Services and Solutions
Create Success!
Simplify Software
Engagement with NXP
Find us online at www.nxp.com/networking-services
Accelerate Customer Time-to-Market
Security
Consulting
Hardened Linux
IOT
Gateway
OpenWRT+
CodeWarrior
VortiQa Software Solutions
Linux® Services
Commercial
Support
Performance Tuning

## Slide 3: AGENDA
2 PUBLIC USE #NXPFTF
PUBLIC USE #NXPFTF
2
Virtualization Overview
I/O Virtualization
Direct Assignment
VirtIO
Conclusions

## Slide 4: VIRTUALIZATION OVERVIEW

## Slide 5: NFV and VNFs
I/O device
IOMMU
Hardware
Memory
Accelerators
CPU
Virtual network infrastructure (Virtual Switch, Service Chain)
KVM, Docker, Ceph
Host OS (Standard Linux distro)
Virtualization
VNF1
VNF3
VNF2
Guest OS
kernel
User space
Guest OS
kernel
User space
Guest OS
kernel
User space
Management & Orchestration

## Slide 6: NXP virtualization solutions
KVM
Linux ® Hypervisor
Resource Virtualization/oversubscription
Open source
Qemu user space emulation used
Multicore Hardware
Linux
KVM
VM
App App
OS
OS Virtualization
Lightweight Overhead
Isolation and Resource Control in Linux ®
Decreased Isolation (Kernel sharing)
Cont C
Multicore Hardware
LXC
App
VM
App App
OS
App App
Cont B
Cont A
LXC
Linux
Docker
Docker
App App
App App
App App

## Slide 7: KVM/QEMU
Multicore Hardware
Linux
KVM
App
Virtual Machine 1
QEMU
App
OS
Virtual Machine 2
QEMU
App
OS
KVM/QEMU– open source virtualization technology based on the Linux® kernel
KVM is a Linux kernel module
QEMU is a user space emulator that uses KVM for acceleration
Run virtual machines alongside Linux applications
No or minimal OS changes required
Virtual I/O capabilities
Direct/pass thru I/O – assign I/O devices to VMs

## Slide 8: Linux Containers
OS level virtualization / process level virtualization
Single kernel for host and guests, virtualized userspace instances – OS appears isolated
Low overhead, lightweight, secure partitioning of Linux
applications into different domains
Per domain resource utilization control – CPU, memory, I/O bandwidth
Multiple resource instances – namespaces
− Process – process trees
− Network – network stack (netdevs, socket families, FDBs)
Based on a collection of technologies including kernel components (cgroups, namespaces), and user space tools (LXC, libvirt, Docker)
Multicore Hardware
App
Container 1
App
Container 2
App
Linux

## Slide 9: I/O VIRTUALIZATION

## Slide 10: Device Usage in Virtual Environments
Hardware/software access Hypercalls
Traps
Direct Access
Fastest native performance
Direct access to hardware
I/O
Hypervisor
OS
I/O
OS
Driver
Full emulation
Driver in Hypervisor
Emulation in Hypervisor
Unmodified Drivers in Guest
I/O
OS
Driver
Driver
Emulation
OS
Driver
Para-Virtualized
Driver in Hypervisor
Modified Drivers in Guest
I/O
OS
Custom Driver
Driver
OS
Custom
Driver
Hardware support
Hardware partitioned
One hardware block
Hypervisor
I/O
OS
Driver
OS
Driver

## Slide 11: Device Usage in KVM/Linux
QEMU
I/O device
IOMMU
User-space
Kernel
Hardware
VM
Guest OS
Device driver
MMIO
IRQ
DMA
MMU
KVM
VFIO
VFIO (simplified view)
Virtio (simplified view)
VM
Guest OS
Virtio frontend
QEMU
Virtio backend
I/O device
User-space
Kernel
Hardware
KVM

## Slide 12: Device Usage in Containers
Drivers
generic iface
DPNI
DPMAC
DPMUX
Netdevs
eth
ni
veth
vlan macvlan
bridge
Netns 1
Netns 2
Host
C1
C2
Each container (userspace instance) has a net namespace
− Multiple containers can share the same netns
Each netdev belongs to a net namespace
The netdev can be:
− Physical: has an associated HW device or abstraction
− Virtual: entirely SW (veth, vlan, bridge, etc.)
Virtual netdev overhead is low – differences arise from
technology specifics
− Bridge: kernel switching
− MACVLAN: MAC level VLAN
− VETH: IP level SW pairs
Mix and match

## Slide 13: DIRECT ASSIGNMENT

## Slide 14: Introduction to VFIO
VFIO (Virtual Function IO)
− Linux user space driver
infrastructure
− Enforces IOMMU protection
VFIO Provides
− Device access (mmap() device
MMIO regions)
− IOMMU programming interface
− High performance interrupt support
Bus support
− PCI, platform devices, LS2 MC bus
MMIO IRQ DMA
Control
QEMU
I/O Device (PCI, Platform, LS2-MC Bus)
Hardware
User-space
Kernel
VM
KVM
VFIO
I/O Device Drivers
IOMMU
QEMU VFIO
VM Memory

## Slide 15: PCI Device Direct Assignment to VM
QEMU
Hardware
User-space
Kernel
VM
KVM
VFIO PCI
PCI Bus Driver
SMMU
QEMU VFIO
(PCI Emulation)
VM Memory
PCI-SRIOV
PCI Device Driver
VF
(Virtual Function)
PF
(Physical Function)
VF
VF
MMIO IRQ DMA
Control

## Slide 16: DPAA2 Enables Secure Direct Assignment
Management Complex (MC) is optimized for resource assignment to various software contexts through Management Complex
  Linux MC bus
  Resource management tool
IOMMU translation and protection for user-
space (DPDK and QEMU)
  ICID (StreamID)
  MC bus integration with VFIO
  Device reset
DPAA secured with Authorization Tables
DPAA 2
ACC
GPP
Memory
MMU
IOMMU
ICID
ICID
ICID
ICID
ICID
ICID
ID
P P
ID
PID
I
CID
I
CID
ICID
ICID
ICID ICID
Authorize
Q/BMan

## Slide 17: DPAA2 Device Direct Assignment to VM
QEMU
Hardware
User-space
Kernel
VM
KVM
VFIO FSL-MC
FSL MC Bus Driver
SMMU
QEMU VFIO
(FSL MC Emulation)
VM Memory
LS2-MC (DPAA2.0)
Eth Driver DPAA2
DPAA2
Crypto-Driver
MMIO IRQ DMA
Control

## Slide 18: DPAA2 Device Pass-through to DPDK in VM
QEMU
Hardware
User-space
Kernel
VM
KVM
VFIO FSL-MC
SMMU
QEMU VFIO
(FSL MC Emulation)
VM Memory
LS2-MC (DPAA2.0)
DPDK
DPDK applications
DPAA Drivers
Kernel
User-space
VFIO FSL-MC
FSL MC Bus
Driver
MMIO IRQ DMA
Control

## Slide 19: Platform devices direct assignment
I/O device
User-space
Kernel
Hardware
QEMU
VM
KVM
VFIO
I/O Device Drivers
IOMMU
QEMU VFIO
VM Memory
MMIO IRQ DMA
Control

## Slide 20: VIRTIO DETAILS

## Slide 21: Virtual I/O Device
Virtio family of devices
Found in virtual environments
By design they look like physical devices
Use guest standard drivers and discovery mechanisms
Specification defined by OASIS technical committee
Virtio specification purpose
Straightforward - use normal bus mechanisms of interrupts and DMA
Efficient - rings of descriptors for both input and output, laid out to avoid cache effects
Standard - makes no assumptions about guest environment beyond supporting MMIO, Channel I/O or PCI bus transports.
Extensible - devices contain feature bits acknowledged by the guest OS
Virtio device facilities
Device status field
Feature bits
Device Configuration space
One or more virtqueues
Guest
Host
virtio- console
virtio- blk
virtio- net
virtio- pci
virtio- scsi
virtio | 
transport | 
virtio back-end driver | 

## Slide 22: Virtio-net: Vhost back-end in user space
DPAA
Hardware
VM
virtio-net Drivers
Networking Stack
Network Application
Kernel
User-space
KVM
VFIO
vhost-user application(s)
DPDK/ODP
DPAA Drivers
vhost-user
Host User-space
Host kernel space

## Slide 23: Virtio-net: DPDK-OVS backend
DPAA Drivers
Hardware
VM
virtio-net Drivers
Networking Stack
Network Application
Kernel
User-space
KVM
VFIO
DPDK/ODP
OVS
IF
IF
vhost-user
DPAA Drivers
Host User-space
Host kernel space

## Slide 24: Virtio-net: DPDK in guest using virtio-net
DPAA Drivers
Hardware
VM
virtio-net Drivers
DPDK Network Application
User-space Kernel
KVM
VFIO
DPDK/ODP
OVS
IF
IF
vhost-user
DPAA Drivers
Host User-space
Host kernel space

## Slide 25: Virtio-block dataplane
Block device 1
Hardware
QEMU
VM
VFS
Frontend driver
Host User-space
Host kernel space
IO Thread 1
IO Thread 2
Block layer
libaio
Block device 2

## Slide 26: CONCLUSIONS

## Slide 27: Conclusions
26
Efficiency, performance and flexibility in I/O virtualization solutions are important ingredients for network function virtualization
KVM provides VirtIO and direct assignment offering NFV system designers the possibility to choose the best suited solution for their applications.

## Slide 29: ATTRIBUTION STATEMENT
28
NXP, the NXP logo, NXP SECURE CONNECTIONS FOR A SMARTER WORLD, CoolFlux, EMBRACE, GREENCHIP, HITAG, I2C BUS, ICODE, JCOP, LIFE VIBES, MIFARE, MIFARE Classic, MIFARE DESFire, MIFARE Plus, MIFARE FleX, MANTIS, MIFARE ULTRALIGHT, MIFARE4MOBILE, MIGLO, NTAG, ROADLINK, SMARTLX, SMARTMX, STARPLUG, TOPFET, TrenchMOS, UCODE, Freescale,
the Freescale logo, AltiVec, C 5, CodeTEST, CodeWarrior, ColdFire, ColdFire+, C Ware, the Energy Efficient Solutions logo, Kinetis, Layerscape, MagniV, mobileGT, PEG, PowerQUICC, Processor Expert, QorIQ, QorIQ Qonverge, Ready Play, SafeAssure, the SafeAssure logo, StarCore, Symphony, VortiQa, Vybrid, Airfast, BeeKit, BeeStack, CoreNet, Flexis, MXC, Platform in a Package, QUICC Engine, SMARTMOS, Tower, TurboLink, and UMEMS are trademarks of NXP B.V. All other product or service names are the property of their respective owners. ARM, AMBA, ARM Powered, Artisan, Cortex, Jazelle, Keil, SecurCore, Thumb, TrustZone, and μVision are registered trademarks of ARM Limited (or its subsidiaries) in the EU and/or elsewhere. ARM7, ARM9, ARM11, big.LITTLE, CoreLink, CoreSight, DesignStart, Mali, mbed, NEON, POP, Sensinode, Socrates, ULINK and Versatile are trademarks of ARM Limited (or its subsidiaries) in the EU and/or elsewhere. All rights reserved. Oracle and Java are registered trademarks of Oracle and/or its affiliates. The Power Architecture and Power.org word marks and the Power and Power.org logos and related marks are trademarks and service marks licensed by Power.org. © 2015–2016 NXP B.V.