## Slide 1: HSAemu
NTHU HSA Course

## Slide 2: Review Virtual Machines

## Slide 3: VM overview
Why do we prefer something virtual than real?
  Why Virtual memory?
  Why Java Virtual Machine?
  Why Virtual I/O?
  Why Virtual Private Network (VPN) ?

## Slide 4: VM overview
Why Virtual Memory?
  Sharing, protection, large address space, …
Why Java virtual machine?
  Interoperability, application sharing, protection,
Why Virtual I/O?
  NIC: flexibility, low cost sharing, better management
  Disk storage: disk expansion and shrinking
Why Virtual Private Network (VPN) ?
  Secure communication over unsecure (public) network
  QoS – bandwidth guarantee

## Slide 5: Virtual is better than Real
So virtualization is often related to the following:
  Resource Sharing
  Protection, Security, Safety
  Flexibility
  Interoperability, Platform Independence
  Portability
  Emulation

## Slide 6: Virtualization
Process virtualization: language level (Java, .Net) OS-level (Solaris Zone), Cross-ISA (Apple Rosetta, IA32EL, FX!32)
Device virtualization: VLAN, VPN, RAID
System virtualization: VMware ESX, Xen, KVM, MS Hyper-V, OKL4 Microvisor

## Slide 7: VM overview
Why are virtual machines interesting?
  They allow transcending of standard interfaces (which often seem to be an obstacle to innovation)
  They enable innovation in flexible, adaptive software & hardware, security, network computing (and others)
  They involve computer architecture in a pure sense

## Slide 8: Transcending of standard interfaces
Well-defined interfaces allow design tasks to be decoupled, e.g. ISA, system calls, API
  Examples: IA-32 (x86) ISA, Linux, OpenGL
  Such interfaces can also be confining: subsystems and components designed to specification for one interface will not work with those designed for another.
  Examples: x86 binary does not run on PowerPC, Linux based apps do not run on Windows
Diversity in ISA, OS, and PL lead to innovations. However, it also leads to reduced interoperability.
  The trend of ISA consolidation, for example, limits innovations in computer architectures.

## Slide 9: Enable innovation in flexible, adaptive software & hardware, security, network computing
Many OS are developed for a specific system architecture and are designed to manage hardware resources directly. This limits the flexibility of the system, in terms of available application software, security and failure isolation.
Example:
  Can you run iPhone’s applications on Gphone?
  One rogue application could crash a complete system
  Virus, worms, and malicious attacks

## Slide 10: VM overview
Virtual machines have been investigated and built by
  OS IBM VM/CMS,VmWare, Xen
  Language designers JVM, P-code
  Compiler developers MS .Net/CIL, Dynamo, Aries
  Hardware designers Crusoe, Intel VT, AMD-V, ARM virtualization extension (hyp mode + others)
This course tries to look at underlying concepts and technologies that are common across the spectrum of virtual machines
This is a cross-disciplinary (inter-disciplinary) course!

## Slide 11: VM overview
Virtualization will be a key part of future computer systems
  Due to the network computing environment
  A fourth major discipline? (with HW, System SW, Application SW)

## Slide 12: Abstraction
Computer systems are built on levels of abstraction
Higher level of abstraction hide details at lower levels
Example: files are abstraction of a disk

## Slide 13: Machines (defined by ISA)
For OS developers, a machine is defined by ISA (Instruction Set Architecture)
Major division between Hardware and software

## Slide 14: Machines (defined by ABI)
For Compiler developers, a machine is defined by ABI (Application Binary Interface)
ABI User level ISA + OS System Calls

## Slide 15: Machines (defined by API)
For Application developers, a machine is defined by API (Application Programming Interface)
API User level ISA + Library Calls (such as Clib, OpenGL)

## Slide 16: Virtual Machines
Add Virtualizing Software to a Host platform and support Guest process or system on a Virtual Machine (VM)

## Slide 17: Process Virtual Machines
Execute applications with an ISA different from the HW platform
Couple at ABI level via runtime system
Usually not persistent

## Slide 18: Process Virtual Machines
Guest processes may intermingle with host processes
As a practical matter, guest OS and host OS are often the same
Example: IA-32 EL, FX!32, Aries, Rosetta
Same ISA dynamic optimizer is a special case
Example: Dynamo, Adore
Dynamic binary instrumentation
Example: PIN, Valgrind, DynamoRIO

## Slide 19: Cross-Platform Portability
PowPC
programs
x86-32
or x86-64
Rosetta
(Apple)
x86 programs
DEC
Alpha
FX!32
(DEC)
x86-32 programs
IA-64
(Itanium)
IA-32EL
(Intel)
HP –PA
programs
IA-64
(Itanium)
Aries
(HP)

## Slide 20: Crossa-Platform Portability
ARM
x86 programs
DEC
Alpha
FX!32
IA-64
(Itanium)
IA-32EL
PowerPC
Sun
Sparc
ARM
Is there a way to make it more portable?
Virtual PC

## Slide 21: HLL Virtual Machines
Java and MS CLI (Common Language Infrastructure) are current examples
Binary class files are distributed
“ISA” is part of binary class format
OS interaction via API (part of VM platform)

## Slide 22: Another Possibility
Byte
code
C
ARM
x86 programs
DEC
Alpha
IA-64
PowerPC
Sun
Sparc
LLVM IR
LLBT

## Slide 23: System Virtual Machines
Provide a system environment
Constructed at ISA level
Allow multiple OS environments, or support time sharing.
Examples: IBM VM/360, VMware, Xen KVM, OKL4
Virtual network communication

## Slide 24: System Virtual Machines
IA-32 Physical Machine
VMM or Hypervisor
Windows Apps
MS Windows
Linux Apps
Linux

## Slide 25: Hosted System VMs
Virtualization SW is built on top of an existing OS
Installation process is similar to the installation of an APP
Let the host OS to provide device drivers and other low-level services
Linux Apps
IA-32 Physical Machine
Windows Apps
MS Windows
Linux

## Slide 26: System Virtual Machines
Past: Early IBM VMs
  Large main frames are shared by many groups, and each group may want different OS
  As a convenient way to implement time sharing OS for multiple single user OS
Current:
  Server consolidation
  Secure partitioning
  Multiple OS environments
  Fault isolation
  Support software development and deployment
  Cloud computing

## Slide 27: Co-designed Virtual Machines
Perform both translation and optimization
VM provides interface between standard ISA software and implementation ISA software
Primary goal is performance or power efficiency
Use proprietary implementation ISA
Example: Transmeta Crusoe and IBM Daisy

## Slide 28: Taxonomy
Pin, Valgrind

## Slide 29: GPU Virtualization
Enable GPU to be shared by multiple graphics applications
  More like system VM, or server virtualization
Graphics VISA (Virtual-ISA)
  Graphics applications are translated into IR (Intermediate Representations) such as PTX (Parallel Thread Execution) or HSAIL (Heterogeneous Systems Architecture Intermediate Language). At runtime, such IR code can be translated for the underlying graphics devices.
  More like HLL VM

## Slide 30: Review Virtualization Technology

## Slide 31: Common terms
Guest and Host
  Guest: Environment that is being supported by underlying platform
  Host: Underlying platform that provides guest environment
  Example: Emulating a Android(ARM) on PC(Intel), Android is the Guest, PC is the Host
Ways of implementing emulation
  Interpretation: instructions at-a-time
  Binary Translation: block-at-a-time optimized for repeated instruction executions. (block could be a trace, or even a procedure)

## Slide 32: Interpretation
Source ISA and Target ISA
  Source ISA: Original instruction set or binary
  Target ISA: Instruction set being executed by processor
  Source/Target refer to ISAs; Guest/Host refer to platforms
Hold complete source architecture state in the interpreter’s data memory
Code
Data
Stack
Interpreter Code
Program counter
Condition codes
Register 0
Register 1
……..
Register N
Architecture State

## Slide 33: Decode-Dispatch Interpretation
while (!halt && !interrupt)
{
inst = code (PC);
opcode = extract (inst, 31, 6);
switch (opcode) {
case LoadWord: LoadWord (inst);
case ALU: ALU (inst);
case Branch: Branch (inst);
. . .
}
LoadWord(inst)
{
RT = extract (inst,25,5);
RA = extract (inst,20,5);
offset = extract (inst,15,16);
source = regs[RA];
address = source + offset ;
regs[RT] = data[address];
PC = PC + 4;
}
Source
ISA
code
PC

## Slide 34: Decode-Dispatch: Low efficiency
Executing an instruction
  Approximately 20 target instructions
  Several loads/stores
  Several shift and mask steps

## Slide 35: Binary Translation
Generate custom code for every source instruction. For example, a load instruction in source code could be translated into a respective load instruction in native code.
Get rid of repeated parsing, decoding, and jumping overhead.
Compiled emulation is an early form of binary translation.
x86 Source Binary
addl %edx,4(%eax)
movl 4(%eax),%edx
add %eax,4
PowerPC Target
addi r16,r4,4 ; add 4 to %eax, r16=r4+4
lwzx r17,r2,r16 ; load operand from memory
add r7,r17,r7 ; perform add of %edx
stwx r7,r2,r16 ; store %edx into memory
mr r4,r16 ; move update value into %eax
addi r3,r3,9 ;

## Slide 36: Dynamic Translation
First Interpret
  And perform code discovery as a byproduct
Translate Code
  Place translated blocks into Code Cache
  Save source PC to target PC mapping in an Address Lookup Table
Emulation process
  Execute translated block to end, Lookup next source PC in table. If translated, jump to target PC, else interpret and translate

## Slide 37: Dynamic Translation
Source Binary
Interpreter
Translator
Code cache
SPC to TPC
Look-up Table
Emulation
Manager
1
3
2
4
5
6
hit
miss

## Slide 38: Flow of Control
Control flows between translated block and emulation manager
Emulation
Manager
Translation Block
Translation Block
Translation Block
Context switch

## Slide 39: Translation Chaining
Jump from one translation directly to next. Avoid switching back to emulation manager
Emulation
Manager
Translation Block
Translation Block
Translation Block
Translation Block

## Slide 40: Review QEMU

## Slide 41: QEMU Overview
QEMU - Quick EMUlator
Processor emulator relies on Binary translation Using a Tiny Code Generator(TCG)
Free and open source
KVM support
Support process VM and system VM
Support same ISA and cross ISA emulation
  This slide focuses on system VM and cross ISA emulation

## Slide 42: Basic Background: POSIX thread
mutual exclusion lock/unlock
  If current thread already has mutex, than lock same mutex again. It will cause dead lock condition
  If current thread does not have mutex but unlock it which is very dangerous
condition wait
  Before use condition wait, current thread must have mutex already
  When current thread use condition wait, it will unlock mutex first, then wait until another thread signals it
  If current thread wake up, it must get the mutex again before execute codes
condition signal/broadcast
  Condition signal will wake 1 thread up at random
  Before use condition broadcast, make sure all of thread (which should be waiting) already in waiting state

## Slide 43: QEMU Main Control Flow
QEMU only create 1 thread which be called “vCPU thread”to represent vCPUs (no matter how many vCPU) and main thread finally becomes“IO thread”
QEMU use global mutex lock to achieve vCPUs and IO communication
vCPU thread execute TCG in the infinite loop
IO thread wait IO and execute IO in the infinite loop
When IO happened, vCPU thread must stop until IO thread finish job

## Slide 44: QEMU TCG
Tiny Code Generator
  A generic backend for a C compiler. It was simplified to be used in QEMU
Translation Block(TB)
  A TCG "basic block" corresponds to a list of instructions terminated by a branch instruction
Prologue/Epilogue
  Load/store all vCPU registers in stack
TB use page as unit to be maintained (guest physic page)
prologue
epilogue
Code cache
TB
CPU_EXEC
TB

## Slide 45: TCG Intermediate Representations
Intermediate Representation is Virtual-ISA, like LLVM IR, PTX(Parallel Thread Execution). At runtime, such IR code can be translated
DEC Alpha | IA-64 | IBM PowerPC | Sun Sparc | ARM | x86
TCG IR
DEC Alpha | IA-64 | IBM PowerPC | Sun Sparc | ARM | x86
Source ISA
Target ISA

## Slide 46: Execution flow
Find_fast
CPU_EXEC
Find_slow
Gen_code
Not found
Not found
found
Exec
Tb_link
found
Chain the TB
Using current virtual PC
Search in a cached hash table
Using current phy-addr
Search in a hash table
Unlink the TB when CPU need to stop

## Slide 47: Exception and interrupt
Find_fast
CPU_EXEC
Find_slow
Gen_code
Not found
Not found
found
exec
Tb_link
found
TB1
TB2
TB3
TB4
Exception or
Interrupt

## Slide 48: Code block Chaining
jmp_next[0]
jmp_next[1]
jmp_first
struct TranslationBlock {
struct TranslationBlock *jmp_next[2];
struct TranslationBlock *jmp_first;
};
QEMU uses the last two bits of the pointer to TranslationBlock to encode
the direction of block chaining:
  0 -> branch taken
  1 -> branch not taken
  2 -> EOF

## Slide 49: Example (insert)
TB2
TB1
TB3
TB1 -> jmp_next = TB2 | 2
TB3 -> jmp_next = TB2->jmp_first = TB1 | 0
struct TranslationBlock
QEMU code cache
TB2 -> jmp_first = TB1 | 0
TB2 -> jmp_first = TB3 | 0

## Slide 50: Example (remove)
TB2
TB1
TB3
jmp_next = NULL
jmp_next = TB2 | 2
jmp_first = TB1 | 0
jmp_first = TB3 | 0
jmp_next = TB1 | 0
struct TranslationBlock
QEMU code cache

## Slide 51: Example (remove)
TB2
TB1
TB3
jmp_next = NULL
jmp_next = TB2 | 2
jmp_first = TB1 | 0
struct TranslationBlock
QEMU code cache

## Slide 52: Address
Guest Virtual Address (GVA)
Guest Physic Address (GPA)
Host Virtual Address (HVA)
Host Physic Address (HPA)
GVA
GPA
HVA
HPA
guest OS+softmmu
offset
host OS+HW

## Slide 53: HSAemu Introduction

## Slide 54: What Is HSAemu
HSAemu is a full system emulator that supports the following HSA features
  Shared virtual memory between CPU and GPU
  Memory based signaling and synchronization
  Multiple user level command queues
  Preemptive GPU context switching
  Concurrent execution of CPU threads and GPU threads
  HSA runtime
  Finalizer
A Project Sponsored by MediaTek (MTK)
Currently, it supports simple HSA platform simulation
  Functional-accurate simulation
  Cycle-accurate simulation

## Slide 55: Architecture of HSAemu
HSAemu consists of 6 components
  HSA Runtime
  CPU Simulation Module
  GPU Task Dispatcher
  Functional-Accurate GPU Simulator (Fast-GPU Simulator)
  Cycle-Accurate GPU Simulator (Mult2sim)
  GPU Helper Functions

## Slide 56: HSAemu Runtime
User Mode Queue
  Store AQL packets
AQL Queue Manager
  Manage AQL packets in User Mode Queue
AQL Command Dispatcher
  Launch the execution of kernel jobs on HSAemu
Support OpenCL runtime

## Slide 57: CPU Simulation Module (1)
PQEMU – Perform multicore CPU simulation
HSA Signal Handler – Receive AQL command from HSA Runtime and launch GPU simulation

## Slide 58: CPU Simulation Module (2)
PQEMU
  A parallel system emulator based on QEMU
  Tow efficient synchronization models (UCC/SCC)
  Dynamic binary translation (DBT) technique
  A project sponsored by MTK
Agent code, HSA runtime, and operating system are run on PQEMU
Code Cache
CPU
CPU
CPU
CPU
DBT
DBT
DBT
DBT
Unified Code Cache (UCC) Model
“PQEMU: A Parallel System Emulator Based on QEMU” (ICPADS 2011)

## Slide 59: GPU Task Dispatcher (1)
AQL Command Monitor
  Receive signal from HSA Signal Handler
  Copy AQL packets from User Mode Queue to HW AQL Queue
  Launch AQL Packet Worker
AQL Packet Worker
  Dequeue AQL packets from HW AQL Queue
  Parse AQL packet
  Dispatch kernel jobs to Fast-GPU Simulator or M2S-GPU Simulator according to the kernel information

## Slide 60: GPU Task Dispatcher (2)
Execution Flow
Signal from
HSA Signal Handler
Copy AQL Packets from
User Mode Queue to
HW AQL Queue
Launch
AQL Packet Worker
to Parse AQL Packet
Launch Fast-GPU
Simulator
Launch M2S-GPU
Simulator

## Slide 61: Fast-GPU Simulator
A functional-accurate simulator for generic GPU model simulation
  HSAIL Translator
    Act as a Finalizer
    Use static binary translation technique to translate BRIG file to host executable binary file (x86) based on LLVM
    Host SSE instruction optimization
  GPU Thread Scheduler
    Simulate a generic GPU model

## Slide 62: HSAIL Translator
Read BRIG File And
Launch LLVM
HSAIL Translator
Construct
The Control Flow
Graph of HSAIL
Program
Translate HSAIL
To LLVM IR
Translate LLVM IR
to Host Executable
Object File (x86)
Load Host Executable
Object File
Link to GPU
Helper Functions
Store The Host Executable
Binary to GPU Code Cache
Architecture of HSAIL Translator

## Slide 63: GPU Thread Scheduler
Simulate a generic GPU model
  GPU Thread Scheduler assigns work groups to free CU threads in the GPU Thread Pool
  Each CU thread executes all work items in a work group
  The maximum number of CU threads is limited by host operating system

## Slide 64: M2S-GPU Simulator (1)
A cycle-accurate simulator for AMD Southern Islands GPU model simulation
  HSAIL Translator
    Translate BRIG file to GPU binary
  M2S Bridge
    Bridge Multi2Sim GPU Model to HSAemu
  M2S GPU Module
    Simulate a cycle-accurate GPU model

## Slide 65
HSAIL Translator
  Act as a Finalizer
  Translate HSAIL to AMD Southern Islands GPU binary (under development)
  Use static binary translation technique based on LLVM
M2S-GPU Simulator (2)

## Slide 66: M2S-GPU Simulator (3)
M2S Bridge : An interface to launch M2S GPU Module
  Initialize the data structures used by AMD Southern Islands GPU, including a memory register for AMD Southern Islands GPU to access the shared system memory in HSAemu
  Invoke M2S GPU Module (the AMD Southern Islands GPU module in Multi2Sim)

## Slide 67: M2S-GPU Simulator (4)
M2S GPU Module
  A cycle-accurate AMD Southern Islands GPU simulator in Multi2Sim
Memory access is performed by HSAemu memory helper function to comply the hUMA model

## Slide 68: GPU Helper Functions (1)
Memory Helper Function
  A soft-mmu of GPU with a page table worker and a TLB to enable hUMA model
  Support the redirect access of a local segment memory to a non-shared private memory in GPU
Kernel Information Helper Function
  Collect and return information of GPU simulation and current execution state
  Retrieve kernel information such as working item ID, work group size, etc, from AQL packet

## Slide 69: GPU Helper Functions (2)
Mathematic Helper Function
  Simulate special mathematical instructions such as trigonometric instructions by calling the corresponding mathematical functions in standard library
Synchronization Helper Function
  Barrier synchronization implementation for generic GPU model simulation

## Slide 70: hUMA Model in HSAemu
Unified coherent address space
  GPU can access a virtual memory page allocated by CPU
Soft-mmu is simulated for GPU
  TLB hit/miss events can be traced
Memory segment access
  Global memory segment access is handled by memory helper function
  Group memory segment access is handled by host ld/st instructions

## Slide 71: Recall: Hardware Simulation of HSAemu
HSA hardware components simulated
  Multicore CPU: A parallel multicore CPU model simulation
  Functional-Accrate GPU: A generic GPU model simulation
  Cycle-Accurate GPU: AMD Southern Islands GPU model simulation
  hUMA: A unified address space between CPU and GPU simulation
  Synchronization Primitive: Barrier instruction simulation
  Hardware AQL Queue: A HW dispatch queue for GPU simulation

## Slide 72: Recall: Software Utilities of HSAemu
HSA software utilities designed
  HAS Runtime: HSA runtime library (OpenCL runtime)
  Topology Discovery: Discover the current platform topology
  User Mode Queue: A queue for each user application
  Signal Event: Notify GPU to work
  HSAIL Generator: A PTX to HSAIL source level translator
  BRIG Generator: Generate a binary format from a Kernel file
  HSAIL Translator: Translate HSAIL to host executable binary
  GPU Code Cache: store translated host binaries

## Slide 73: Experimental Evaluation
Guest OS | Linux-3.5.0-1-linaro-vexpress
Guest | ARM Vexpress-A9
Host OS | Ubuntu 12.04
Host | Dell PowerEdge
Benchmark: AMD APP SDK v2.8 | 
Binary Search | Fast Walsh Transform
Prefix Sum | Bitonic Sort
Discrete Wavelet Transform | Floyd Warshall (shortest path)
NBody | Reduction (parallel summation)
Matrix Transpose | 

## Slide 74: N-Body Simulation by Fast-GPU Simulator
N-Body Simulation
All of host physical CPUs are running

## Slide 75: Reference
rednoah“VM & QEM”2010/04/09
徐慰中 “Introduction to Virtual Machines and Virtualization Technology” 2012/09/17
臧傑晧 “Introduction to VM” 2012/07/26
郭舟東 “QEMU” 2012/07/25
陳韋任 “qemu - 韋任的維基百科” http://people.cs.nctu.edu.tw/~chenwj/dokuwiki/doku.php?id=qemu