## Slide 1: GPU simulation Technology
GPGPU-sim, Gem5-gpu, GPUWattch

## Slide 2: Outline
GPGPU-Sim
  functional/timing GPU simulator
Gem5-gpu
  Merge Gem5 and GPGPU-Sim.
  Case study: GPU MMU design
GPUWattch
  Add power model for GPGPU-Sim

## Slide 3: What GPGPU-Sim Simulates
Functional model for PTX/SASS
  PTX = Parallel Thread eXecution
    Virtual ISA defined by Nvidia
  SASS = Native ISA for Nvidia GPUs
Timing model for the compute part of a GPU
  Not for CPU or PCIe
  Only model micro-architecture timing relevant to GPU compute.

## Slide 4: Functional Model (PTX)
Low-level, data-parallel virtual machine by Nvidia
  Instruction level
  Unlimited registers
  Parallel threads running in blocks; barrier synchronization instruction
Intermediate representation in CUDA tool chain:
.cu
.cl
NVCC
OpenCL Drv
PTX
ptxas
G80
GT200
Fermi
Kepler

## Slide 5: Functional Model (SASS)
SASS = Native ISA for Nvidia GPUs
  Better correlation with HW GPU
  “SASS” is what NVIDIA’s cuobjdump calls it.
For simplicity GPGPU-Sim uses assembly syntax that can represent both SASS and PTX. Called PTXPlus.
SASS mapped into PTXPlus instructions.
CUDA
Executable
cuobjdump
SASS
conversion
PTXPlus

## Slide 6: Timing Model for Compute Parts of a GPU
GPGPU-Sim models timing for:
  SIMT Core (SM, SIMD Unit)
  Caches (Texture, Constant, …)
  Interconnection Network
  Memory Partition
  Graphics DRAM
It does NOT model timing for:
  CPU, PCIe
  Graphics Specific HW (Rasterizer, Clipping, Display… etc.)
GPU
PCIe
Interconnect
Gfx DRAM
Mem Part.
SIMT Cores
Cache
Raster…
Gfx HW
CPU

## Slide 7: Timing Model for GPU Micro-architecture
GPGPU-Sim is a detailed cycle-level simulator:
  Cycle-level model for each part of the microarchitecture
  Research focused
    Ignoring rare corner cases to reduce complexity
  In most cases we can only guess at details. Guesses “informed” by studying patents and microbenchmarking.
  CUDA manual provides some hints. NVIDIA IEEE Micro articles provide other hints.

## Slide 8: GPU Microarchitecture Overview
SIMT Core
Interconnection Network
Clock Domains
Memory Partition
Figure from: http://gpgpu-sim.org/manual/images/2/21/Overall-arch.png

## Slide 9: Inside a SIMT Core (3.0)
Design Model
  Fetch + Decode
  Instruction Issue
  Scoreboard
  SIMT Stack
  Operand collector
  ALU
  Memory unit
SIMT Front End
SIMD Datapath
ALU
ALU
ALU
I-Cache
Decode
I-Buffer
Score
Board
Issue
Operand
Collector
MEM
ALU
Fetch
SIMT-Stack
Done (WID)
Valid[1:N]
Branch Target PC
Pred.
Active
Mask
Scheduler 1
Scheduler 2
Scheduler 3

## Slide 10: Memory Partition
Service memory request (Load/Store/AtomicOp)
  Contains L2 cache bank, DRAM timing model
Figure from:http://gpgpu-sim.org/manual/index.php5/File:Mempart-arch.png

## Slide 11: Accuracy
Chart: RODINIA Benchmark Suite Quadro FX5800 SASS GPGPU-Sim 3.1.0 – Correlation: 98.37%
Similarity Score
copyChunks_kernel()
Back Propagation
bpnn_layerforward_CUDA()
HotSpot
calculate_temp()

## Slide 12: Accuracy
Chart: RODINIA Benchmark Suite Tesla C2050 (Fermi) SASS GPGPU-Sim 3.1.0 – Correlation: 97.35%

## Slide 13: Gem5-gpu
Gem5 simulator
  Full-system simulation
  Multiple ISA support(arm, x86…etc)
  detailed, event-driven memory system
Gem5-gpu merges 2 popular simulators:
  gem5 and gpgpu-sim.
Support detail timing simulation of CPU, GPU and memory hierarchy.

## Slide 14: Gem5-gpu: Gem5 + GPGPU-Sim
CudaCore
  Wrapper for GPGPU-Sim shader_core_ctx
  Sends instruction, global and const memory requests to Ruby cache hierarchy.
CudaGPU
  Acts as gem5 structure for organizing the GPU hardware
Shader TLB
  Manages GPU memory space page table
  If flag “--access-host-pagetable” is set, GPU will use CPU page table for translations.
  Const latency for each event(hit, miss…)
Figure from:https://gem5-gpu.cs.wisc.edu/wiki/_detail/current_gem5-gpu_architecture_1_31_2013-cropped.png?id=cur-arch

## Slide 15: Case study: GPU MMU design
Related paper:
  Topic: Address translation(VA->PA) on GPU
    Supporting x86-64 address translation for 100s of gpu lanes(HPCA '14)
      Jason Power(gem5-gpu author), Mark D. Hill , David A. Wood (University of Wisconsin–Madison )

## Slide 16: Target simulation architecture
Simulate GPU TLB, MMU behavior
Assign constant delay latency for each event(hit, miss...)

## Slide 17: MMU design for HSA
IOMMU in HSA architecture
  Use Device ID, PASID ID to separate different device process.
  Walk page table to find physical address.
Figure from HSA hardware specification
Problem
  The overhead of address translation mechanism.
  Unlike a simple IO device, GPU issues much more memory requests than accesses to I/O.

## Slide 18: Discussion of GPU MMU design
The fundamental problems
  Low temporal locality, increase TLB miss.
  GPU has hundreds of cores.
  Memory instructions dispatch on several lanes at the same time.
  Some memory instructions will hit and others will miss in TLB.
  What is the frequency of TLB miss or page fault?
Simulation target platform

## Slide 19: Paper’s observation 1: global memory access
Frequently global memory access
  Every 1000 cycles
    Average 602 mem inst.
    268 global instructions.
    Coalescing can reduce global inst to 39 accesses.
  Solution: Use coalescer to reduce global memory access.
Memory instructions every 1000 cycles

## Slide 20: Paper’s observation 2: memory bandwidth
Average 60 page table walks are active at that CU.
Worst workload averages 140 concurrent PTW.
observation:
  90% page walks issued within 500 cycles of previous PTW.
  Solution: shared multi-threaded page table walker(PTW) (up to 32 threads).
Log scale

## Slide 21: Paper’s observation 3:TLB miss rate
High TLB miss rate
  Average 29%, the highest is 67%.
  Solution: Add page walk cache to reduce PTW latency.

## Slide 22: Paper’s proposed architecture
Coalescer for global memory accesses
multi-threaded page table walker
page walk cache

## Slide 23: MMU performance
Design 1: Coalescer
Design 2: Coalescer + multi-threaded PTW
Design 3: Coalescer + multi-threaded PTW + PTW cache

## Slide 24: GPUWattch

## Slide 25: Power Model: GPUWattch
GPGPU-Sim introduces such a power model
  Cycle-accurate: Integrates GPGPU-Sim v3.1.2 with McPAT v0.8
  Configurable: GPGPU-Sim/McPAT configuration files
  Fine-grained: Performance/event counter driven. McPAT: Circuit level implementation
  Extensible: Can model new components or add more fine-grained per-component metrics
  Validated: Rigorously validated against NVIDIA GTX480 and Quadro Fx 5600 GPUs
Enables the exploration of new energy-efficiency optimizations for GPGPU research

## Slide 26: GPUWattch: GPGPU-Sim with McPAT
Modified McPAT
Modifications: Specific micro-architectural components
GPGPU-Sim
Modifications: Add required performance counters
A Comprehensive Framework for Performance and Energy Optimization Research
Interface
Interface
Static Power
Dynamic Power
Detailed Power Stats
Detailed Performance Stats
Feedback-driven Optimizations
Performance counters

## Slide 27: Modeling Bottom Up: McPAT Modifications
Baseline McPAT
  Multi-core CPU power simulator
  Detailed models for CPU microarchitectural blocks
Modified McPAT to account for GPU specific microarchitectural components
Some of the main components that were added/modified:
  SM Pipeline
  Register File
  Caches
  Shared Memory
  Execution Units
  Main Memory

## Slide 28: Modeling: Bottom Up: GPGPU-Sim modifications
Added performance counters required by McPAT
Structures added to manage performance counters
Files added to interface with McPAT
Existing timing model not affected by any GPGPU-Sim modifications

## Slide 29: Modeling: Bottom Up: GPGPU-Sim modifications
Current version utilizes 30 performance counters
Main Component | Performance Counters | Main Component | Performance Counters
Instruction cache | Read hit | L2 Data cache | Read hit
 | Read miss |  | Read miss
L1 Data cache | Read hit |  | Write hit
 | Read miss |  | Write miss
 | Write hit | Memory | Reads
 | Write miss |  | Writes
Texture cache | Read hit |  | Precharges
 | Read miss | Register file | Reads
Constant cache | Read hit |  | Writes
 | Read miss |  | Non-register file operand

## Slide 30: Modeling: Bottom Up: GPGPU-Sim modifications
Current version utilizes 30 performance counters
Main Component | Performance Counters | Main Component | Performance Counters
Decoding/Scheduling | Total # instructions | Shared Memory | Accesses
 | FP_INT instructions |  | 
Pipeline dutycycle | Fraction of committed instructions per cycle | Execution Units | SP accesses
Idle core | Number of cycles each SM is idle |  | SFU accesses
Interconnect | # of flits from SIMT cores to Memory Partition |  | 
 |  |  | FPU accesses
 | # of flits from Memory Partition to SIMT cores |  | 

## Slide 31: Accuracy (Average Power)
Chart: NVIDIA GTX 480

## Slide 32: Status
Gem5-gpu
GPUWattch
CPU power model
Different GPGPU-Sim version

## Slide 33: Reference
Slides p3~p12, p25~p31 are from gpgpusim tutorial at MICRO 2012.
  Following pages are used:
    1-Tutorial-Intro: 21,22
    2-GPGPU-Sim-Overview: 4,5,7,10,12
    4-Microarchitecture: 9,47
    5c-GPUWattch: 5,9,13,15,19~21
Slides p13~p23 are mainly from
  Gem5-gpu simulator(http://gem5-gpu.cs.wisc.edu)
  Supporting x86-64 address translation for 100s of gpu lanes(HPCA '14)