## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Computer
Desktop computers
  Designed to deliver good performance to a single user at a low cost.
  Usually executing third-party software.
  Usually incorporating a graphics display, a keyboard and a mouse.

## Slide 3: Other Classes of Computers
Servers
  Used to run larger program for multiple users simultaneously, typically accessed only via a network, with a greater emphasis on dependability and (often) security.
Supercomputers
  A high performance, high-cost class of servers with a large number of processors, huge memory and storage that are used for high-end scientific and engineering applications.
Embedded computers (microprocessors)
  A computer within another system with a dedicated function or application.

## Slide 4: Supercomputers
Sunway TaihuLight
  Fastest supercomputer in the world (as of June 2017)
  Over 10 million CPU cores
  Power: 15 MW
  Speed: 93 PFLOPS
http://www.nsccwx.cn/wxcyw/

## Slide 5: Automotive Embedded Systems
https://dcvizcayno.wordpress.com/2015/08/28/the-future-of-technology-privacy-security-and-risks-part-3-of-5/

## Slide 6: Post-PC Era
Personal Mobile Devices
  Battery-operated devices with wireless connectivity.
Warehouse-Scale Computers
  Datacenter containing hundreds of thousands of servers providing software as a service (SaaS).

## Slide 7: Embedded vs. Desktop

## Slide 8: Evolution of Computer Hardware (1)
1st transistor invented by John Bardeen, Walter Brattain, and William Shockley at Bell Labs in 1947.
UNIVAC I (UNIVersal Automatic Computer I): 1st commercial computer sold in US in 1951.

## Slide 9: Evolution of Computer Hardware (2)
1st integrated circuit invented by Jack Kilby of Texas Instruments in 1958.
IBM System/360: 1st family of computers in 1964 with a range of performance but with the same instruction set.

## Slide 10: Evolution of Computer Hardware (3)
Intel 4004: 1st commercially available microprocessor by Intel in 1971.
https://en.wikipedia.org/wiki/Intel_4004

## Slide 11: IC Manufacturing Process
Yield: proportion of working dies per wafer.

## Slide 12: Intel Core i7 Wafer
300-mm wafer, 280 dies at 100% yield (32-nm technology).

## Slide 13: Integrated Circuit Cost
Nonlinear relation to defect rate and die area
  Wafer cost and wafer area are fixed
  Defect rate is determined by manufacturing process
  Die area is determined by architecture and circuit design

## Slide 14: Impacts of Advancing Technology
Processor
  Logic capacity: increases about 30% per year
  Performance: 2× every 1.5 years
Memory
  DRAM capacity: 4× every 3 years, about 60% per year
  Memory speed: 1.5× every 10 years
  Cost per bit: decreases about 25% per year
Storage
  Capacity: increases about 60% per year

## Slide 15: Moore’s Law
http://www.itrs2.net/

## Slide 16: International Technology Roadmap for Semiconductors
Year | 2013 | 2015 | 2017 | 2019 | 2021 | 2023 | 2025 | 2028
Logic half pitch (nm) | 40 | 32 | 25 | 20 | 16 | 13 | 10 | 7
Gate Density (gates/mm2) | 4M | 6.4M | 10M | 16M | 25.5M | 40M | 64M | 128M
Double the circuitry in the same space
or
Same circuitry in half the space
equals
Same capability, half the die size

## Slide 17: Clock Rate and Power
Pentium 4 had a dramatic jump in clock rate and power.
Core 2 reverts to simpler pipeline, lower clock rates and multiple processors per chip.

## Slide 18: Power Wall
Pdynamic = 0.5 × CL × Vdd2 × fswitching
Example:
  For a simple processor, if capacitive load is reduced by 15%, voltage is reduced by 15%, frequency is reduced by 15%, how much power consumption can be reduced?

## Slide 19: From Uniprocessors to Multiprocessors
Power limit forced a dramatic change in microprocessor design.
Since 2002, the response time improvement has slowed from 1.5× per year to 1.2× per year.
As of 2006, all computer companies are shipping microprocessors with multiple processors per chip (called “multicore microprocessors”).

## Slide 20: Intel Core i7
http://www.intel.com/

## Slide 21: Major Components of a Computer

## Slide 22: Computer Organization
Components
  Processor (control, datapath)
  Input (keyboard, mouse)
  Output (display, printer)
  Memory (cache, SRAM, disk drive, CD/DVD)
  Network
Our main focus
  The processor (control and datapath) and its interaction with memory systems
  Implemented using hundreds of millions of transistors; impossible to understand by looking at each transistor

## Slide 23: Machine Organization
Capabilities and performance characteristics of the principal functional units (e.g., registers, ALU, shifters, logic units).
Ways in which these components are interconnected
Logic and means by which such information flow is controlled
Instruction Set Architecture (ISA)
Register Transfer Level (RTL) description

## Slide 24: Processor Organization (1)
Control needs to have circuitry to
  Decide which is the next instruction and input it from memory
  Decode the instruction
  Issue signals that control the way information flows between datapath components
  Control what operations the datapath’s functional units perform

## Slide 25: Processor Organization (2)
Datapath needs to have circuitry to
  Execute instructions – functional units (e.g., adder) and storage locations (e.g., register)
  Interconnect the functional units so that the instructions can be executed as required
  Load data from and store data to memory

## Slide 26: System Software
Operating System
  Supervising program that interfaces the user’s program with the hardware (e.g., Linux, iOS, Windows)
  Handles basic input and output operations
  Allocates storage and memory
  Provides for protected sharing among multiple applications
Compiler
  Translate high-level language programs (e.g., C, Java) into instructions that the hardware can execute
Application Software
System Software
Hardware

## Slide 27: High-Level Languages
Allow the programmer to think in a more natural language and for their intended use (Fortran for scientific computation, Cobol for business programming, Lisp for symbol manipulation, Java for web programming, etc.).
Improve programmer productivity – more understandable code that is easier to debug and validate.
Improve program maintainability.
Allow programs to be independent of the computer on which they are developed (compilers and assemblers can translate high-level language programs to the binary instructions of any machine).
Emergence of optimizing compilers that produce very efficient assembly code optimized for the target machine.
As a result, very little programming is done today at the assembly level.

## Slide 28: Below the Program
High-level language program (in C)
swap (int v[], int k) {
int temp;
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
Assembly language program (for MIPS)
swap: sll $2, $5, 2
add $2, $4, $2
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
jr $31
Machine (object) code (for MIPS)
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
one-to-many
one-to-one
C Compiler
Assembler

## Slide 29: Code Input to Device
Memory
Processor
Devices
Network
Input
Output
Control
Datapath
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000
Object Code

## Slide 30: Code Stored in Memory
Memory
Processor
Devices
Network
Input
Output
Control
Datapath
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000

## Slide 31: Code Fetch from Memory
Memory
Processor
Devices
Network
Input
Output
Control
Datapath
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000

## Slide 32: Decoding Code
Processor
Devices
Network
Input
Output
Control
Datapath
000000 00100 00010 0001000000100000
Memory

## Slide 33: Executing Code
Control decodes the instruction to determine what to execute
Datapath executes the instruction as directed by control
Processor
Devices
Network
Input
Output
Control
Datapath
Memory
Add Reg #4 and Reg #2, put result in Reg #2
000000 00100 00010 0001000000100000

## Slide 34: The Cycle
Processor fetches the next instruction from memory
How does it know which location in memory to fetch from next?
Fetch
Decode
Execute

## Slide 35: Data Output to Device
Memory
Processor
Devices
Network
Input
Output
Control
Datapath
00000100010100000000000000000000
00000000010011110000000000000100
00000011111000000000000000001000

## Slide 36: Instruction Set Architecture (ISA)
ISA, or simply architecture – the abstract interface between the hardware and the lowest level software that includes all the information necessary to write a machine language program, including instructions, registers, memory access, I/O, etc.
Enables implementations of varying cost and performance to run identical software.
The combination of the basic instruction set (the ISA) and the operating system interface is called the Application Binary Interface (ABI).
  The user portion of the instruction set plus the operating system interfaces used by application programmers.
  Define a standard for binary portability across computers.

## Slide 37: MIPS ISA
Instruction Categories
  Load/Store
  Computational
  Jump and Branch
  Floating Point
  Memory Management
  Special
3 instruction formats: all 32-bit wide
R0–R31
PC
HI
LO
Registers
OP
rs
rt
rd
sa
funct
OP
rs
rt
immediate
OP
jump target

## Slide 38: Computer Architecture
Coordination of many levels of abstraction
Under a rapidly changing set of forces
Design, measurement, and evaluation
Circuit Design
Digital Design
Datapath & Control
Memory System
Processor
I/O System
Network
Applications
Operation System
Compiler
Firmware
Instruction Set Architecture