## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
    CPI < 1, so use Instructions Per Cycle (IPC)
  E.g., 4 GHz 4-way multiple-issue
    16 BIPS, peak CPI = 0.25, peak IPC = 4
  But dependencies reduce this in practice
Computer Architecture: A Quantitative Approach

## Slide 3: Multiple Issue
Static multiple issue (at compile time)
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue (during execution)
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 4: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome, execute instructions after branch
    Roll back if path taken is different
  Speculate on store that precedes load does not refer to same address
    Roll back if location is updated

## Slide 5: Compiler or Hardware Speculation
Compiler can reorder instructions
  e.g., move load before branch
  Compiler inserts “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed (written to the registers or memory)
  Flush buffers on incorrect speculation

## Slide 6: Speculation and Exceptions
What if exception occurs on a speculatively executed instruction?
Static speculation
  Can add ISA support for deferring exceptions
Dynamic speculation
  Can buffer exceptions until instruction completion (which may not occur)

## Slide 7: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations  Very Long Instruction Word (VLIW)

## Slide 8: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary

## Slide 9: MIPS with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop

## Slide 10: MIPS with Static Dual Issue

## Slide 11: Hazards in the Dual-Issue MIPS
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now cannot use ALU result in load/store in same packet
    add $t0, $s0, $s1 load $s2, 0($t0)
  Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required

## Slide 12: Scheduling Example
Schedule this for dual-issue MIPS
Loop: lw $t0, 0($s1) # $t0=array element addu $t0, $t0, $s2 # add scalar in $s2 sw $t0, 0($s1) # store result addi $s1, $s1,–4 # decrement pointer bne $s1, $zero, Loop # branch $s1!=0
IPC = 5/4 = 1.25 (c.f. peak IPC = 2)

## Slide 13: Loop Unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Compiler applies “register renaming” to eliminate all data dependencies that are not true data dependencies

## Slide 14: Unrolled Code Example
lp: lw $t0,0($s1) # $t0=array element lw $t1,-4($s1) # $t1=array element lw $t2,-8($s1) # $t2=array element lw $t3,-12($s1) # $t3=array element addu $t0,$t0,$s2 # add scalar in $s2 addu $t1,$t1,$s2 # add scalar in $s2 addu $t2,$t2,$s2 # add scalar in $s2 addu $t3,$t3,$s2 # add scalar in $s2 sw $t0,0($s1) # store result sw $t1,-4($s1) # store result sw $t2,-8($s1) # store result sw $t3,-12($s1) # store result addi $s1,$s1,-16 # decrement pointer bne $s1,$0,lp # branch if $s1 != 0

## Slide 15: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at cost of registers and code size

## Slide 16: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 17: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s4, $s4, $t3 slti $t5, $s4, 20
Can start sub while addu is waiting for lw

## Slide 18: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Preserves dependencies
Hold pending operands
Reorders buffer for register (memory) writes
Can supply operands for issued instructions

## Slide 19: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 20: Does Multiple Issue Work?
Yes, but not as much as we’d like:
  Programs have real dependencies that limit ILP
  Some dependencies are hard to eliminate
  Some parallelism is hard to expose
  Memory delays and limited bandwidth, hard to keep pipelines full
  Speculation can help if done well

## Slide 21: Power Efficiency
Complexity of dynamic scheduling and speculations requires power
Multiple simpler cores may be better