## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Introduction
Goal: connecting multiple computers to get higher performance
  Multiprocessors
  Scalability, availability, power efficiency
Job-level (process-level) parallelism
  High throughput for independent jobs
Parallel processing program
  Single program run on multiple processors
Multicore microprocessors
  Chips with multiple processors (cores)

## Slide 3: Hardware and Software
Sequential/concurrent software can run on serial/parallel hardware
  Challenge: making effective use of parallel hardware

## Slide 4: Parallel Programming
Parallel software is the problem
Need to get significant performance improvement
  Otherwise, just use a faster uniprocessor, since it’s easier!
Difficulties
  Partitioning, load balancing
  Coordination, synchronization
  Communications overhead
  Sequential dependencies

## Slide 5: Amdahl’s Law (1)
=

## Slide 6: Amdahl’s Law (2)
To achieve 90x speed-up using 100 processors
fimprovable = 0.999  funimprovable = fsequential = 0.1%
Sequential part can limit speed-up

## Slide 7: Scaling Example
Calculate sum of 10 scalars, and sum of two 10×10 matrices
Single processor:
  ttotal = (10 + 100) × tadd = 110 tadd
10 processors:
  ttotal = 10 × tadd + (100/10) × tadd = 20 tadd
  Speed-up = 110/20 = 5.5 (55% of ideal)
100 processors:
  ttotal = 10 × tadd + (100/100) × tadd = 11 tadd
  Speed-up = 110/11 = 10 (10% of ideal)

## Slide 8: Scaling Example (cont’d)
What if matrix size is 100 × 100?
Single processor:
  ttotal = (10 + 10000) × tadd = 10010 tadd
10 processors:
  ttotal = 10 × tadd + (10000/10) × tadd = 1010 tadd
  Speed-up = 10010/1010 = 9.9 (99% of ideal)
100 processors:
  ttotal = 10 × tadd + (10000/100) × tadd = 110 tadd
  Speed-up = 10010/110 = 91 (91% of ideal)

## Slide 9: Strong vs Weak Scaling
Strong scaling
  Speed-up achieved on a multiprocessor without increasing the size of the problem.
Weak scaling
  Speedup achieved on a multiprocessor while increasing the size of the problem proportionally to the increase in the number of processors.

## Slide 10: Multithreading
Difficult to continue to extract instruction-level parallelism (ILP) from a single sequential thread of control
Many workloads can make use of thread-level parallelism (TLP)
  TLP from multiprogramming (run independent sequential jobs)
  TLP from multithreaded applications (run one job faster using parallel threads)
Multithreading uses TLP to improve utilization of a single processor

## Slide 11: Examples of Threads
A web browser
  One thread displays images
  One thread retrieves data from network
A word processor
  One thread displays graphics
  One thread reads keystrokes
  One thread performs spell checking in the background
A web server
  One thread accepts requests
  When a request comes in, separate thread is created to service
  Many threads to support thousands of client requests

## Slide 12: Multithreading on a Chip
Find a way to “hide” true data dependency stalls, cache miss stalls, and branch stalls by finding instructions (from other process threads) that are independent of those stalling instructions
Hardware multithreading – increase the utilization of resources on a chip by allowing multiple processes (threads) to share the functional units of a single processor
  Processor must duplicate the state hardware for each thread – a separate register file, PC, instruction buffer, and store buffer for each thread
  The caches, Translation Look-aside Buffers (TLBs), Branch History Table (BHT), Branch Target Buffer (BTB), Register Update Unit (RUU) can be shared (although the miss rates may increase if they are not sized accordingly)
  The memory can be shared through virtual memory mechanisms
  Hardware must support efficient thread context switching

## Slide 13: Types of Multithreading
Fine-grained multithreading
  Switch threads after each cycle
  Interleave instruction execution
  If one thread stalls, others are executed
Coarse-grained multithreading
  Only switch on long stall (e.g., L2-cache miss)
  Simplifies hardware, but does not hide short stalls
  Also has pipeline start-up costs

## Slide 14: Simultaneous Multithreading (SMT)
In multiple-issue dynamically scheduled processor
  Schedule instructions from multiple threads
  Instructions from independent threads execute when function units are available
  Within threads, dependencies handled by scheduling and register renaming
Example: Intel Pentium-4 HyperThreading
  Two threads: duplicated registers, shared function units and caches

## Slide 15: Threading on a 4-way SS Processor Example

## Slide 16: The Big Picture: Where are We Now?
Multiprocessor – a computer system with at least two processors
  Can deliver high throughput for independent jobs via job-level parallelism or process-level parallelism
  And improve the run time of a single program that has been specially crafted to run on a multiprocessor – a parallel processing program

## Slide 17: Multicores Now Universal
Power challenge has forced a change in microprocessor design
  Since 2002 the rate of improvement in the response time of programs has slowed from a factor of 1.5 per year to less than a factor of 1.2 per year
Today’s microprocessors typically contain more than one core – Chip Multicore microProcessors (CMPs) – in a single IC
Product |  | AMD Barcelona | Intel Nehalem | IBM Power 6 | Sun Niagara 2
Cores per chip |  | 4 | 4 | 2 | 8
Clock rate |  | 2.5 GHz | ~2.5 GHz? | 4.7 GHz | 1.4 GHz
Power |  | 120 W | ~100 W? | ~100 W? | 94 W

## Slide 18: Shared Memory Multiprocessor
SMP: shared memory multiprocessor
  Hardware provides single physical address space for all processors
  Synchronize shared variables using locks
  Memory access time
    UMA (uniform) vs. NUMA (nonuniform)

## Slide 19: Shared Address Space Example
Add 100,000 numbers in shared memory using 100 processors (P0–P99)
sum[Pn] = 0; for (i = 1000*Pn; i < 1000*(Pn+1); i += 1) sum[Pn] += A[i]; /*sum the assigned areas*/
Gather the partial sums (reduction)
half = 100; /*100 processors in multiprocessor*/ do synch(); /*wait for partial sum completion*/ if (half%2 != 0 && Pn == 0) sum[0] += sum[half–1]; half = half/2; if (Pn < half) sum[Pn] += sum[Pn+half]; while (half > 1);

## Slide 20: Reduction

## Slide 21: Message Passing
Each processor has private physical address space
Hardware sends/receives messages between processors

## Slide 22: Sum Reduction (1)
Sum 100,000 on 100 processors
First distribute 100 numbers to each
The do partial sums
sum = 0; for (i = 0; i<1000; i = i + 1) sum += AN[i];
Reduction
  Half the processors send, other half receive and add
  The quarter send, quarter receive and add, …

## Slide 23: Sum Reduction (2)
Given send() and receive() operations
limit = 100; half = 100;/* 100 processors */ do half = (half+1)/2; /* send vs. receive dividing line */ if (Pn >= half && Pn < limit) send(Pn - half, sum); if (Pn < (limit/2)) sum = sum + receive(); limit = half; /* upper limit of senders */ while (half > 1); /* exit with final sum */
Send/receive also provide synchronization
Assumes send/receive take similar time to addition (which is unrealistic)

## Slide 24: Message Passing Multiprocessors

## Slide 25: Pros and Cons of Message Passing
Message sending and receiving is much slower than addition
But message passing multiprocessors are much easier for hardware designers to design
  Don’t have to worry about cache coherency for example
The advantage for programmers is that communication is explicit, so there are fewer “performance surprises” than with the implicit communication in cache-coherent SMPs.
However, its harder to port a sequential program to a message passing multiprocessor since every communication must be identified in advance.
  With cache-coherent shared memory the hardware figures out what data needs to be communicated