## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Review: Major Components of a Computer

## Slide 3: Review: Instruction Set Architecture (ISA)
The interface description separating the software and hardware
Instruction Set Architecture
Software
Hardware

## Slide 4: Analog vs. Digital
Analog Signal
  Vary in a smooth way over time
  Analog data are continuously valued
Example: audio, video
Digital Signal
  Maintains a constant level then changes to another constant level (generally operate in one of the two states)
  Digital data are discretely valued
Example: computer data

## Slide 5: Radix or Base
An ordered set of symbols, called digits, with relations defined for addition, subtraction, multiplication and division
Radix or base of the number system is the total number of digits allowed in the number system

## Slide 6: Decimal, Binary, Octal and Hexadecimal
System Name | Decimal | Binary | Octal | Hexadecimal
Radix | 10 | 2 | 8 | 16
 | 0 | 0000 | 0 | 0
 | 1 | 0001 | 1 | 1
 | 2 | 0010 | 2 | 2
 | 3 | 0011 | 3 | 3
 | 4 | 0100 | 4 | 4
 | 5 | 0101 | 5 | 5
 | 6 | 0110 | 6 | 6
 | 7 | 0111 | 7 | 7
 | 8 | 1000 | 10 | 8
 | 9 | 1001 | 11 | 9
 | 10 | 1010 | 12 | A
 | 11 | 1011 | 13 | B
 | 12 | 1100 | 14 | C
 | 13 | 1101 | 15 | D
 | 14 | 1110 | 16 | E
 | 15 | 1111 | 17 | F
 | 16 | 10000 | 20 | 10

## Slide 7: Number Systems
Decimal numbers
Binary numbers
1000’s column
100’s column
10’s column
1’s column
five
thousands
three
hundreds
seven
tens
four
ones
8’s column
4’s column
2’s column
1’s column
one
eight
one
four
zero
two
one
one

## Slide 8: Powers of Two
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 =128
28 = 256
29 = 512
210 = 1024
211 = 210 × 21 = 2048
212 = 210 × 22 = 4096
216 = 210 26 = 65536
…
220 = 210 × 210 = 1048576
Handy to memorize up to 210

## Slide 9: Decimal vs Binary Numbers
Binary to decimal conversion:
  Convert 100112 to decimal
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
Decimal to binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112
N-digit decimal number
  How many values? 10N Range: [0, 10N−1]
  Example: 3-digit decimal number:
  103 = 1000 possible values Range: [000, 999]
N-digit binary number
  How many values? 2N Range: [0, 2N−1]
  Example: 3-digit binary number:
  23 = 8 possible values Range: [0002, 1112]
  [ 0 , 7 ]

## Slide 10: Hexadecimal Numbers
Hexadecimal to binary conversion
  4AF16 (or 0x4AF)
  0100 1010 11112
Hexadecimal to decimal conversion
  4AF16 (or 0x4AF)
  162×4 + 161×10 + 160×15 = 119910

## Slide 11: Exercise L02-1
Ex 1: Convert 368 to binary
Ex 2: Convert 3610 to binary
Notes: 368=011 1102
3610=1001002

## Slide 12: Unsigned and Signed Numbers
Hexadecimal | Binary | Decimal (Unsigned) | Decimal (2’s Complement)
0x8F | 0111 1111 | 127 | 127
0x8E | 0111 1110 | 126 | 126
… | … | … | …
0x02 | 0000 0010 | 2 | 2
0x01 | 0000 0001 | 1 | 1
0x00 | 0000 0000 | 0 | 0
0xFF | 1111 1111 | 28−1 = 255 | −1
0xFE | 1111 1110 | 254 | −2
… | … | … | …
0x82 | 1000 0010 | 130 | −126
0x81 | 1000 0001 | 129 | −127
0x80 | 1000 0000 | 128 | −128
1000 0000
1000 0001
Complement all bits
Then add 1
0000 0001
0000 0010
Complement all bits
Then add 1

## Slide 13: Exercise L02-2
Ex 3: For a n-bit 2’s complement signed binary numeral system, what’s the largest positive number and the smallest negative number?

## Slide 14: Digital Circuits
Digital circuits generally contain two parts
  Combinational logic
  Sequential logic
Combinational circuits consist of logic gates with inputs and outputs
  The outputs at any instance of time depend only on the combination of the input values based on logic operations such as AND, OR, etc.
Sequential circuits, in addition to inputs and outputs also have storage elements, therefore the output depends on both the current inputs as well as the stored values

## Slide 15: Digital Signal Representation
Active High
  High voltage activates/enables the pin
Active Low
  Low voltage activates/enables the pin

## Slide 16: Logic Levels

## Slide 17: Logic Gates
OR
NOR
AND
NAND
buffer
NOT (inverter)
XOR
XNOR

## Slide 18: Exercise L02-3
Ex 4: What is the schematic view of a NOR gate?
Notes: 368=011 1102
3610=1001002

## Slide 19: Truth Table
A tool for describing how the output of a logic circuit depends on the logic levels presented at the inputs
The number of input combinations will equal 2N for an N-input truth table
Logic Circuit
A
B
Z
A | B | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Inputs
Output

## Slide 20: Exercise L02-4
Ex 5: Draw the truth table of a 3-input AND gate.
Notes: 368=011 1102
3610=1001002

## Slide 21: Combinational Circuits
In combinational circuits, the output at any time is a direct function of the applied external inputs
Combinational Circuits
…
Input X
…
Output Z
Z = F(X)

## Slide 22: Design Procedure of Combinational Circuits
Circuit Specification
Truth Table
(How many input/output?)
Minimization
(K-maps, algebraic manipulation, CAD tools)
Logic Diagram

## Slide 23: Exercise L02-5
Ex 6: Implement AB+CD using NAND gates only

## Slide 24: Propagation Delay
The delay when the signal arrives at the input of a circuit, and when the output of the circuit changes, is called the propagation delay.
A circuit is considered to be fast, if its propagation delay is small (ideally as close to 0 as possible).
X
Y
Z
Delay between input (X, Y) and change in output Z.

## Slide 25: Timing Diagram
The inputs to a circuit can be changed over time.
The timing diagram shows the values of the input signals to a circuit with the passage of time, in the form of a waveform.
It also shows a waveform for the output.
X
Y
Z
Inputs
Output
Time
Propagation delay =
τ

## Slide 26: Fan-in
Fan-in of a gate is the number of inputs to the gate.
For a 3-input OR gate, the fan-in = 3.
There is a limitation on the fan-in for any gate.
In CMOS IC technology, higher fan-in implies slower gates (higher propagation delays).

## Slide 27: Fan-out
Fan-out is the number of gates that can be driven by a driver gate.
The driven gate is called the load gate.
There is a limit to the number of load gates that can be driven by a driver gate.
Fan-out = 3

## Slide 28: Buffers
Buffers have a single input and a single output, where output = input.
Buffers help increase the driving capability of a circuit by increasing the fan-out.
Drive strength: how much load a gate can drive.
Greater drive strength, load gates are (dis)charged more quickly.

## Slide 29: Decoders (1)
Information is represented by binary codes.
Circuits that perform decoding are called decoders.
A decoder is a minterm generator.
Minterm: product that includes all input variables
  ABC, ABC, ABC
̅
̅
̅

## Slide 30: Decoders (2)
N inputs, 2N outputs
One-hot outputs: only one output HIGH at once
Binary 2-to-4 Decoder
Note: “x” denotes don’t care.

## Slide 31: Decoders (3)
2-to-4 Decoder Logic Diagram

## Slide 32: Decoder Applications
Decode 3-bit opcodes:
Home automation:
op0
op1
op2
ADD
SUB
AND
XOR
NOT
LOAD
STORE
JUMP
C0
C1
Light
A/C
Door
TV

## Slide 33: Decoders as Binary Adder

## Slide 34: Multiplexers
Directs one of 2n input to the output, basically a data selector.
Input to output direction is done based on a set of n select bits.
…
2n-to-1 MUX
2n inputs
1 output
n select bits

## Slide 35: Sequential Circuits
Give sequence to events
Have memory (short-term)
Use feedback from output to input to store information
The state of a circuit influences its future behavior
State elements store state
  Latch
  Flip-flop

## Slide 36: Bistable Circuit
Fundamental building block of other state elements
  Two outputs: Q, Q
  No inputs
Consider the two possible cases:
  Q = 0: then Q = 1, Q = 0 (consistent)
  Q = 1: then Q = 0, Q = 1 (consistent)
Stores 1 bit of state in the state variable, Q (or Q).
But there are no inputs to control the state.
̅
̅
̅
̅

## Slide 37: SR (Set/Reset) Latch
SR Latch
Consider the four possible cases:
  S = 1, R = 0
  S = 0, R = 1
  S = 0, R = 0
  S = 1, R = 1

## Slide 38: SR Latch Analysis（1）
  S = 1, R = 0:
    then Q = 1 and Q = 0
  S = 0, R = 1:
    then Q = 0 and Q = 1
̅
̅

## Slide 39: SR Latch Analysis （2）
S = 0, R = 0:
  then Q = Qprev
  Memory
S = 1, R = 1:
  then Q = 0, Q = 0
  Invalid (Q = Q)
̅
̅

## Slide 40: SR Latch Symbol
SR (Set/Reset) Latch
  Stores one bit of state (Q)
Control what value is being stored with S, R inputs
  Set: Make the output 1 (S = 1, R = 0, Q = 1)
  Reset: Make the output 0 (S = 0, R = 1, Q = 0)
Must do something to avoid invalid state (when S = R = 1)

## Slide 41: Gated D Latch
Two inputs: CLK, D
  CLK: controls when the output changes.
  D (data input): controls what the output changes to.
Function
  When CLK = 1, D passes through to Q (transparent).
  When CLK = 0, Q holds its previous value (opaque).
Avoids invalid case when Q ≠ NOT Q.
̅

## Slide 42: Gated D Latch Internal Circuit

## Slide 43: Master-Slave D Flip-Flop
Two back-to-back latches (L1 and L2) controlled by complementary clocks.
When CLK = 0
  L1 is transparent
  L2 is opaque
  D passes through to Y
When CLK = 1
  L1 is opaque
  L2 is transparent
  Y passes through to Q
Thus, on the edge of the clock (when CLK rises from 01), D passes through to Q.
Y

## Slide 44: Edge-Triggered D Flip-Flop
Inputs: CLK, D
Function
  Samples D on rising edge of CLK
    When CLK rises from 0 to 1, D passes through to Q
    Otherwise, Q holds its previous value
  Q changes only on rising edge of CLK
Called edge-triggered.
Activated on the clock edge.

## Slide 45: Latch and Flip-Flop
Latch is level-sensitive.
Flip-flop is edge-triggered.

## Slide 46: Registers
A register is a simple memory device that is composed of a series of flip-flops wired together so that they share a common clock pulse.
Registers come in various sizes and types.
The size of a register is closely tied to the structure of the microprocessor, e.g. 8-bit registers for microprocessor architecture with 8-bit wide data.

## Slide 47: 4-Bit Register
A simple 4-bit register can be made with 4 D-FF
Common Clock
  At each positive-edge, 4 bits are loaded in parallel
  Previous data is overwritten
Common Clear
  Asynchronous clear
  When Clear = 0, all FFs are cleared; i.e. 0 is stored.

## Slide 48: Shift Registers
Serial-in, serial-out: A register which can shift its stored bits laterally in one or both directions is called a shift registers.
Common Clock
  At each positive-edge, 4 bits are loaded in parallel
  Previous data is overwritten
Which direction is this registering shifting?

## Slide 49: Bidirectional Shift Register with Parallel Load