## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Two Key Principles of Machine Design
Instructions are represented as (binary) numbers and, as such, are indistinguishable from data.
Programs are stored in alterable memory (that can be read from or written to) just like data.
Memory
Accounting Program (machine code)
C Compiler (machine code)
Accounting Data
Source Code (text file)

## Slide 3: Stored-Program Concept
Programs can be shipped as files of binary numbers – binary-code compatibility.
Computers can inherit ready-made software provided they are compatible with an existing ISA – leads industry to align around a small number of ISAs.

## Slide 4: Assembly Language Instructions
The language of the machine
  Want an ISA that makes it easy to build the hardware and the compiler while maximizing performance and minimizing cost.
Our target: the MIPS ISA
  Similar to other ISAs developed since the 1980’s
  Used by Broadcom, Cisco, NEC, Nintendo, Sony, etc.
Design Goals:
  Maximize performance, minimize cost, reduce design time (time-to-market), minimize memory space (embedded systems), minimize power consumption (mobile systems).

## Slide 5: CISC vs. RISC
Complex Instruction Set Computer (CISC)
  Lots of instructions of variable size, very memory optimal, typically less registers.
  Intel x86
Reduced Instruction Set Computer (RISC)
  Instructions, all of a fixed size, more registers, optimized for speed.
  Usually called a “Load/Store” architecture.
  MIPS, Sun SPARC, HP PA-RISC, IBM PowerPC

## Slide 6: RISC – Reduced Instruction Set Computer
RISC Philosophy
  fixed instruction lengths
  load-store instruction sets
  limited number of addressing modes
  limited number of operations
Instruction sets are measured by how well compilers use them as opposed to how well assembly language programmers use them.

## Slide 7: MIPS (RISC) Design Principles
Simplicity favors regularity
  fixed size instructions
  small number of instruction formats
  opcode always the first 6 bits
Smaller is faster
  limited instruction set
  limited number of registers
  limited number of addressing modes
Make the common case fast
  arithmetic operands from the registers (load-store machine)
  allow instructions to contain immediate operands
Good design demands good compromises
  three instruction formats

## Slide 8: MIPS ISA
Instruction Categories
  Load/Store
  Computational
  Jump and Branch
  Floating Point
  Memory Management
  Special
3 instruction formats: all 32-bit wide
R0–R31
PC
HI
LO
Registers
OP
rs
rt
rd
shamt
funct
OP
rs
rt
immediate
OP
jump target
R format
I format
J format

## Slide 9: MIPS Registers (1)
Holds thirty-two 32-bit registers
Two read ports
One write ports

## Slide 10: MIPS Registers (2)
Registers are
  Faster than main memory
    But registers with more locations are slower
    Read/write port increase impacts speed quadratically
  Easier for a complier to use
    E.g., (A*B) – (C*D) – (E*F) can do multiplications in any order vs. stack
  Can hold variables
    so that code density improves (since register are named with fewer bits than a memory location).

## Slide 11: MIPS Register Convention
Name | Register Number | Usage | Preserved on call?
$zero | 0 | Constant value 0 | N/A
$at | 1 | (Reserved for assembler) | No
$v0–$v1 | 2–3 | Returned values | No
$a0–$a3 | 4–7 | Arguments | No
$t0–$t7 | 8–15 | Temporaries | No
$s0–$s7 | 16–23 | Saved values | Yes
$t8–$t9 | 24–25 | Temporaries | No
$k0–$k1 | 26–27 | (Reserved for OS) | No
$gp | 28 | Global pointer | Yes
$sp | 29 | Stack pointer | Yes
$fp | 30 | Frame pointer | Yes
$ra | 31 | Return address | Yes

## Slide 12: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
  add a, b, c # a gets b + c
  All arithmetic operations have this form
Design Principle 1: Simplicity favors regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost

## Slide 13: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1
Using registers (f–j are stored in $s0–$s4):
add $t0, $s1, $s2 # $t0 = g + h add $t1, $s3, $s4 # $t1 = i + j sub $s0, $t0, $t1 # f = $t0 - $t1

## Slide 14: Register Operands
Arithmetic instructions use register operands
MIPS has 32 × 32-bit registers
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names (convention)
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables

## Slide 15: Memory Operands
Design Principle 2: Smaller is faster
  (main memory: millions of locations)
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4
MIPS is Big Endian

## Slide 16: Big Endian / Little Endian
Big Endian: The leftmost byte stores at the starting address of a word
  IBM 360/370, Motorola 68k, MIPS, Sparc, HP PA
Little Endian: The rightmost byte stores at the starting address of a word
  Intel 80x86, DEC Vax, DEC Alpha
Example: 0x1234abcd
Memory | Big-Endian | Little-Endian
0x0000 | 0x12 | 0xcd
0x0001 | 0x34 | 0xab
0x0002 | 0xab | 0x34
0x0003 | 0xcd | 0x12

## Slide 17: Memory Operand Example (1)
C code
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code
  Index 8 requires offset of 32 (4 bytes × 8 words)
lw $t0, 32($s3) # load word add $s1, $s2, $t0
Offset
Base register

## Slide 18: Memory Operand Example (2)
C code
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code
  Index 8 requires offset of 32 (4 bytes × 8 words)
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word

## Slide 19: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 20: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
addi $s2, $s1, -1

## Slide 21: The Constant Zero
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
add $t2, $s1, $zero

## Slide 22: Binary Integers
Unsigned Binary Integers
  Range: 0 to 2n – 1
  32 bit: 0 to 4,294,967,295
2’s-Complement Signed Integers
  Range: –2(n – 1) to +2(n – 1) – 1
  32 bits: –2,147,483,648 to +2,147,483,647
  Bit 31 is sign bit: 1 is negative, 0 is positive
  Some specific numbers
    0: 0000 0000 … 0000
    –1: 1111 1111 … 1111
    Most-negative: 1000 0000 … 0000
    Most-positive: 0111 1111 … 1111

## Slide 23: Sign Extension
Representing a number using more bits
  Preserve the numeric value
In MIPS instruction set
  addi: extend immediate value
  lb, lh: extend loaded byte/halfword
  beq, bne: extend the displacement
Replicate the sign bit to the left
  compare unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110

## Slide 24: MIPS ISA
Instruction Categories
  Load/Store
  Computational
  Jump and Branch
  Floating Point
  Memory Management
  Special
3 instruction formats: all 32-bit wide
R0–R31
PC
HI
LO
Registers
OP
rs
rt
rd
shamt
funct
OP
rs
rt
immediate
OP
jump target
R format
I format
J format

## Slide 25: MIPS Instruction Fields
MIPS fields are given names to make them easier to refer to.
op: 6-bit opcode that specifies the operation
rs: 5-bit the first register source operand
rt: 5-bit the second register source operand
rd: 5-bit the register destination operand
shamt: 5-bit shift amount
funct: 6-bit function code that selects specific variant of the operation
6 | 5 | 5 | 5 | 5 | 6
op | rs | rt | rd | shamt | funct

## Slide 26: R-format Example
op | rs | rt | rd | shamt | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
0 | $s1 | $s2 | $t0 | 0 | 32
add $t0, $s1, $s2
$t0  R8
$s1  R17
$s2  R18
0 | 17 | 18 | 8 | 0 | 32
000000 | 10001 | 10010 | 01000 | 00000 | 100000
0000 0010 0011 0010 0100 0000 0010 00002 = 0232402016

## Slide 27: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: (–215) to (+215 – 1)
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op | rs | rt | constant or address
6 bits | 5 bits | 5 bits | 16 bits

## Slide 28: Load/Store (I-format)
lw $t0, 24($s3)
op | rs | rt | constant or address
6 bits | 5 bits | 5 bits | 16 bits
35 | 19 | 8 | 24
$s3 = 0x12004094
$s3 + 24 = 0x12004094 + 0x18
= 0x120040AC
$t0 = data[0x120040AC]
Memory | 
 | 0xFFFFFFFF
 | 0x120040AC
 | 0x12004094
 | 0x0000000C
 | 0x00000008
 | 0x00000004
 | 0x00000000
Data | Address
$s3
$t0  R8
$s3  R19
$t0

## Slide 29: MIPS Instruction Encoding
Instruction | Format | op | rs | rt | rd | shamt | funct | address
add | R | 0 | reg | reg | reg | 0 | 32 | 
sub | R | 0 | reg | reg | reg | 0 | 34 | 
addi | I | 8 | reg | reg |  |  |  | constant
lw | I | 35 | reg | reg |  |  |  | address
sw | I | 43 | reg | reg |  |  |  | address
reg: 0–31
constant/address: 16-bit

## Slide 30: Translating C Code to Machine Code (1)
C code:
A[300] = h + A[300];
  h in $s2, base address of A in $t1
Compiled MIPS code:
lw $t0, 1200($t1) # $t0 = A[300] add $t0, $s2, $t0 # $t0 = h + A[300] sw $t0, 1200($t1) # A[300] = $t0
Machine code:
op | rs | rt | address rd shamt funct |  | 
35 | 9 | 8 | 1200 |  | 
0 | 18 | 8 | 8 | 0 | 32
43 | 9 | 8 | 1200 |  | 

## Slide 31: Translating C Code to Machine Code (2)
Machine code (decimal)
Machine code (binary)
op | rs | rt | address rd shamt funct |  | 
35 | 9 | 8 | 1200 |  | 
0 | 18 | 8 | 8 | 0 | 32
43 | 9 | 8 | 1200 |  | 
100011 | 01001 | 01000 | 0000 0100 1011 0000 |  | 
000000 | 10010 | 01000 | 01000 | 00000 | 100000
101011 | 01001 | 01000 | 0000 0100 1011 0000 |  | 

## Slide 32: Logical Operations
Instructions for bitwise manipulation
Useful for extracting and inserting groups of bits in a word
Operation | C | Java | MIPS
Shift Left | << | << | sll
Shift Right | >> | >>> | srl
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise NOT | ~ | ~ | nor

## Slide 33: Shift Operations
shamt: how many positions to shift
Shift Left Logical (sll):
  Shift left and fill with bit 0
  sll by i bits equals multiplication by 2i
Shift Right Logical (srl):
  Shift right and fill with bit 0
  srl by i bits equals division by 2i (for unsigned numbers)
op | rs | rt | rd | shamt | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits

## Slide 34: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
$t2 | 0000 0000 0000 0000 0000 1101 1100 0000
$t1 | 0000 0000 0000 0000 0011 1100 0000 0000
$t0 | 0000 0000 0000 0000 0000 1100 0000 0000

## Slide 35: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
$t2 | 0000 0000 0000 0000 0000 1101 1100 0000
$t1 | 0000 0000 0000 0000 0011 1100 0000 0000
$t0 | 0000 0000 0000 0000 0011 1101 1100 0000

## Slide 36: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT (a OR b)
nor $t0, $t1, $zero
$t1 | 0000 0000 0000 0000 0011 1100 0000 0000
$t0 | 1111 1111 1111 1111 1100 0011 1111 1111

## Slide 37: MIPS Logical Operations
There are a number of bit-wise logical operations in the MIPS ISA
R-format
  and $t0, $t1, $t2 # $t0 = $t1 & $t2 or $t0, $t1, $t2 # $t0 = $t1 | $t2 nor $t0, $t1, $t2 # $t0 = not($t1 | $t2)
I-format
  andi $t0, $t1, 0xFF00 # $t0 = $t1 & 0xFF00 ori $t0, $t1, 0xFF00 # $t0 = $t1 | 0XFF00

## Slide 38: Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1
j L1
  unconditional jump to instruction labeled L1

## Slide 39: Compiling If Statements
C code:
if (i == j) f = g + h; else f = g – h;
  f in $s0, g in $s1, h in $s2
Compiled MIPS code:
bne $s3, $s4, Else # go to Else if i≠j add $s0, $s1, $s2 # f=g+h (skipped if i≠j) j Exit # go to Exit Else: sub $s0, $s1, $s2 # f=g-h (skipped if i=j) Exit: ...
Assembler calculates addresses

## Slide 40: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 # $t1 = i * 4 add $t1, $t1, $s6 # $t1 = addr of save[i] lw $t0, 0($t1) # $t0 = save[i] bne $t0, $s5, Exit # Exit if save[i]≠k addi $s3, $s3, 1 # i = i+1 j Loop # go to Loop Exit: ...

## Slide 41: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization

## Slide 42: More Conditional Operations
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L

## Slide 43: Branch Instruction Design
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  Combining with branch involves more work per instruction, requiring a slower clock
  All instructions penalized!
beq and bne are the common case
This is a good design compromise

## Slide 44: Signed vs. Unsigned
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example:
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0000
slt $t0, $s0, $s1 # signed
  $s0 = −1, $s1 = 0, $s0 < $s1  $t0 = 1
sltu $t0, $s0, $s1 # unsigned
  $s0 = +4,294,967,295, $s1 = 0, $s0 > $s1  $t0 = 0

## Slide 45: Bounds Check Shortcut
Treating signed numbers as if they were unsigned gives a low cost way of checking if 0 ≤ x < y (index out of bounds for arrays)
sltu $t0, $s1, $t2 # $t0 = 0 if # $s1 > $t2 (max) # or $s1 < 0 (min) beq $t0, $zero, IOOB # go to IOOB if # $t0 = 0
The key is that negative integers in two’s complement look like large numbers in unsigned notation. Thus, an unsigned comparison of x < y also checks if x is negative as well as if x is less than y

## Slide 46: Procedure Calling
Main routine (caller) places parameters in a place where the procedure (callee) can access them
  $a0–$a3: four argument registers
Caller transfers control to the callee
Callee acquires the storage resources needed
Callee performs the desired task
Callee places the result value in a place where the caller can access it
  $v0–$v1: two value registers for result values
Callee returns control to the caller
  $ra: one return address register to return to the point of origin

## Slide 47: Register Usage
$a0–$a3: arguments (reg 4–7)
$v0, $v1: result values (reg 2 and 3)
$t0–$t9: temporaries
  Can be overwritten by callee
$s0–$s7: saved
  Must be saved/restored by callee
$gp: global pointer for static data (reg 28)
$sp: stack pointer (reg 29)
$fp: frame pointer (reg 30)
$ra: return address (reg 31)

## Slide 48: Procedure Call Instructions
Procedure call: jump and link (jal)
  jal ProcedureLabel
  Address of following instruction is put in $ra
  Jumps to target address
Procedure return: jump register (jr)
  jr $ra
  Copies $ra to program counter

## Slide 49: Leaf Procedure Example（1）
C code:
int leaf_example (int g, int h, int i, int j) { int f; f = (g + h) – (i + j); return f; }
  Arguments g–j in $a0–$a3
  f in $s0 (hence, need to save $s0 on stack)
  Result in $v0

## Slide 50: Leaf Procedure Example（2）
MIPS code:
leaf_example: addi $sp, $sp, -4 sw $s0, 0($sp) add $t0, $a0, $a1 add $t1, $a2, $a3 sub $s0, $t0, $t1 add $v0, $s0, $zero lw $s0, 0($sp) addi $sp, $sp, 4 jr $ra
Save $s0 on stack
Procedure body
Result
Restore $s0 from stack
Return

## Slide 51: Stack Layout
 | Memory
0xFFFFFFFF | 
$sp  | 
0x00000000 | 
Address | Data
 | Memory
0xFFFFFFFF | 
$sp  | $s0
0x00000000 | 
Address | Data
 | Memory
0xFFFFFFFF | 
$sp  | 
0x00000000 | 
Address | Data
Before procedure call
During procedure call
After procedure call

## Slide 52: Non-Leaf Procedures
Procedures that call other procedures
For nested call, caller needs to save on the stack:
  Its return address
  Any arguments and temporaries needed after the call
Restore from the stack after the call

## Slide 53: Non-Leaf Procedure Example (1)
C code:
int fact (int n) { if (n < 1) return f; else return n * fact(n – 1); }
  Arguments n in $a0
  Result in $v0

## Slide 54: Non-Leaf Procedure Example (2)
MIPS code
fact: addi $sp, $sp, -8 sw $ra, 4($sp) sw $a0, 0($sp) slti $t0, $a0, 1 beq $t0, $zero, L1 addi $v0, $zero, 1 addi $sp, $sp, 8 jr $ra L1: addi $a0, $a0, -1 jal fact lw $a0, 0($sp) lw $ra, 4($sp) addi $sp, $sp, 8 mul $v0, $a0, $v0 jr $ra
Adjust stack pointer for 2 items
Save return address
Save argument
Test for n < 1
If so, result is 1
pop 2 items from stack
and return
Else decrement n
Recursive call
Restore original n
and return address
Pop 2 items from stack
Multiply to get result
And return

## Slide 55: Local Data on the Stack
Local data allocated by callee
  e.g., C automatic variables
Procedure frame (activation record)
  Used by some compilers to manage stack storage

## Slide 56: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
  $gp initialized to address allowing ±offsets into this segment
Dynamic data: heap
  e.g., malloc in C, new in Java
Stack: automatic storage

## Slide 57: Character Data
Byte-encoded character sets
  ASCII: 128 characters
    95 graphic, 33 control
  Latin-1: 256 characters
    ASCII, +96 more graphic characters
Unicode: 32-bit character set
  Used in Java, C++ wide characters, …
  Most of the world’s alphabets, plus symbols
  UTF-8, UTF-16: variable-length encodings

## Slide 58: Byte/Halfword Operations
Could use bitwise operations
MIPS byte/halfword load/store
  String processing is a common case
lb rt, offset(rs) lh rt, offset(rs)
  Sign extend to 32 bits in rt
lbu rt, offset(rs) lhu rt, offset(rs)
  Zero extend to 32 bits in rt
sb rt, offset(rs) sh rt, offset(rs)
  Store just rightmost byte/halfword

## Slide 59: 32-bit Constants
Most constants are small
  16-bit immediate is sufficient
For the occasional 32-bit constant
lui rt, constant
  Copies 16-bit constant to left (upper) 16 bits of rt
  Clears right 16 bits of rt to 0
lui $s0, 61
ori $s0, $s0, 2304
0000 0000 0011 1101 | 0000 0000 0000 0000
0000 0000 0011 1101 | 0000 1001 0000 0000

## Slide 60: Branch Addressing
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Forward or backward
  PC-relative addressing
    Target address = PC + offset × 4
    PC already incremented by 4 by this time
op | rs | rt | constant or address
6 bits | 5 bits | 5 bits | 16 bits

## Slide 61: Specifying Branch Destinations
Program Counter (PC) gets updated (PC+4) when fetched.
Branch distance is limited to −215 to +215−1 (word) instructions away.
offset
00
sign-extend
16-bit address
PC
+
+
16
32
32
4
32
32
Branch destination address
32

## Slide 62: Jump Addressing
Jump (j and jal) targets could be anywhere in text segment
  Encode full address in instruction
Pseudodirect jump addressing
op | address
6 bits | 26 bits
PC[31:28] | address | 00
4 bits | 26 bits | 2 bits

## Slide 63: Jump Addressing
Target address must be within the 256-MB region.
address
00
26-bit address
PC
26
32
32
Jump destination address
PC[31:28]
4

## Slide 64: Branching Far Away
If branch target is too far to encode with 16-bit offset, assembler rewrites the code:
beq $s0, $s1, L1
may be replaced by
bne $s0, $s1, L2 j L1 L2: ...

## Slide 65: Addressing Mode Summary

## Slide 66: C Code Translation Hierachy

## Slide 67: MIPS Organization So Far