## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
Floating-point real numbers
  Representation and operations

## Slide 3: MIPS Arithmetic and Logic Unit (ALU)
Must support the Arithmetic/Logic operations of the ISA
  add, addi, addiu, addu
  sub, subu
  mult, multu, div, divu
  sqrt
  and, andi, nor, or, ori, xor, xori
  beq, bne, slt, slti, sltiu, sltu
With special handling for
  sign extend – addi, addiu, slti, sltiu
  zero extend – andi, ori, xori
  overflow detection – add, addi, sub
32
32
32
4
ALU
A
B
result
m (operation)
zero
overflow

## Slide 4: MIPS Arithmetic and Logic Instructions
op
rs
rt
rd
shamt
funct
op
rs
rt
immediate
R format
I format
 | op | funct
add | 000000 | 100000
addu | 000000 | 100001
sub | 000000 | 100010
subu | 000000 | 100011
and | 000000 | 100100
or | 000000 | 100101
xor | 000000 | 100110
nor | 000000 | 100111
 | op | funct
slt | 000000 | 101010
sltu | 000000 | 101011
R-format
I-format
 | op
addi | 001000
addiu | 001001
slti | 001010
sltiu | 001011
andi | 001100
ori | 001101
xori | 001110
lui | 001111

## Slide 5: Design MIPS ALU
Requirements: must support the following arithmetic and logic operations
  add, sub: Two’s complement adder/subtractor with overflow detection
  And, or, nor : Logical AND, logical OR, logical NOR
  slt (set on less than): Two’s complement adder with inverter, check sign bit of result

## Slide 6: Design Approach
Design trick 1: Divide and conquer
  Break the problem into simpler problems, solve them and glue together the solution
Design trick 2: Solve part of the problem and extend
Design trick 3: Take pieces you know (or can imagine) and try to put them together

## Slide 7: Function Specification
ALU Control (ALUop) Function
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-on-less-than
  1100 nor
ALU
32
32
32
A
Result
Overflow
Zero
4
ALUop
CarryOut
B
Notes: Now you remember what binary numbers are, let design an Arithmetic Logic Unit that can perform bitwise AND, bitwise OR, binary add, binary subtract, and et-on-less-than.
The type of operation the ALU perform will be selected by the ALUop bits.
The ALU I am going to show you in class is 4 bits wide (N = 4). The ALU you need to design for the next homework assignment will be 32 bits wide.
I will show you how to implement all these operations except the last one, which is left as your homework assignment.
+1 = 25 min. (Y:05)

## Slide 8: The Diagram of a 32-Bit ALU
ALU31
a31
b31
m
cin
c31
s31
A
B
ALUop
Result
32
32
32
4
Overflow
ALU0
a0
b0
m
cin
co
s0
Zero

## Slide 9: Function Specification
ALU
32
32
32
A
Result
Overflow
Zero
4
ALUop
CarryOut
B
ALU Control (ALUop) Function k
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-on-less-than
  1100 nor
Notes: Now that I have shown you how to build a 1-bit full adder, we have all the major components needed for this 1-bit ALU.
In order to build a 4-bit ALU, we simply connect four 1-bit ALUs in series to feed the CarryOut of one ALU to the CarryIn of the next ALU.
Even though I called this an ALU, I actually lied a little. There is something missing about this ALU. This ALU can NOT perform the subtract operation.
Let see how can we fix this problem.
2 min = 35 min. (Y:15)

## Slide 10: A 1-bit ALU – And, Or, and Add Operations
A
B
1-bit
Full
Adder
CarryOut
Mux
CarryIn
Result
add
and
or
Operation
0
1
2
Notes: Now that I have shown you how to build a 1-bit full adder, we have all the major components needed for this 1-bit ALU.
In order to build a 4-bit ALU, we simply connect four 1-bit ALUs in series to feed the CarryOut of one ALU to the CarryIn of the next ALU.
Even though I called this an ALU, I actually lied a little. There is something missing about this ALU. This ALU can NOT perform the subtract operation.
Let see how can we fix this problem.
2 min = 35 min. (Y:15)

## Slide 11: A 4-bit ALU – And, Or, and Add Operations
1-bit ALU 4-bit ALU
A
B
1-bit
Full
Adder
CarryOut
Mux
CarryIn
Result
Operation
CarryOut3
A0
B0
1-bit
ALU
Result0
CarryIn0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
CarryOut2
A3
B3
1-bit
ALU
Result3
CarryIn3
Operation
Notes: Now that I have shown you how to build a 1-bit full adder, we have all the major components needed for this 1-bit ALU.
In order to build a 4-bit ALU, we simply connect four 1-bit ALUs in series to feed the CarryOut of one ALU to the CarryIn of the next ALU.
Even though I called this an ALU, I actually lied a little. There is something missing about this ALU. This ALU can NOT perform the subtract operation.
Let see how can we fix this problem.
2 min = 35 min. (Y:15)

## Slide 12: Function Specification
ALU Control (ALUop) Function
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-on-less-than
  1100 nor
ALU
32
32
32
A
B
Result
Overflow
Zero
4
ALUop
CarryOut
Notes: Now you remember what binary numbers are, let design an Arithmetic Logic Unit that can perform bitwise AND, bitwise OR, binary add, binary subtract, and et-on-less-than.
The type of operation the ALU perform will be selected by the ALUop bits.
The ALU I am going to show you in class is 4 bits wide (N = 4). The ALU you need to design for the next homework assignment will be 32 bits wide.
I will show you how to implement all these operations except the last one, which is left as your homework assignment.
+1 = 25 min. (Y:05)

## Slide 13: Subtraction Operation
2’s complement: Take inverse of every bit and add 1 (at cin of first stage)
  A + B’ + 1 = A + (B’ + 1) = A + (-B) = A - B
  Bit-wise inverse of B is B’
ALU
A
B’
Result
CarryIn
CarryOut
B
0
1
Mux
Sel
Subtract
(Bnegate)
Operation
Notes: Recalled something you learned from grade school that: A - B is the same as A plus (-B).
Also recall from earlier slides that in order to calculate the 2 complement representation of negative B, we simply take the inverse of very bit and add 1.
The bitwise inverse of B is easy to compute. Just pass them through the inverter.
In order to do the add 1 operation, we simply set the CarryIn to 1.
So for the subtract operation, we simply select the output of the inverter and set CarryIn to 1.
Then we will be adding A to the negative of B and whola, we have the A minus B operation.
+2 = 37 min. (Y:17)

## Slide 14: Revised Diagram
LSB and MSB need to do a little extra
A
B
ALUop
Result
32
32
32
4
Overflow
ALU0
a0
b0
cin
co
s0
ALU31
a31
b31
cin
c31
s31
Supply a 1 on subtraction
?
Zero
Combining the CarryIn and Bnegate

## Slide 15: Function Specification
ALU Control (ALUop) Function
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-on-less-than
  1100 nor
ALU
32
32
32
A
B
Result
Overflow
Zero
4
ALUop
CarryOut
Notes: Now you remember what binary numbers are, let design an Arithmetic Logic Unit that can perform bitwise AND, bitwise OR, binary add, binary subtract, and et-on-less-than.
The type of operation the ALU perform will be selected by the ALUop bits.
The ALU I am going to show you in class is 4 bits wide (N = 4). The ALU you need to design for the next homework assignment will be 32 bits wide.
I will show you how to implement all these operations except the last one, which is left as your homework assignment.
+1 = 25 min. (Y:05)

## Slide 16: Nor Operation
A nor B = (not A) and (not B)
0
Operation
1
0
1
b
2
ALUop
Result
CarryOut
Ainvert
CarryIn
0
1
a
Bnegate
2

## Slide 17: Function Specification
ALU Control (ALUop) Function
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-on-less-than
  1100 nor
ALU
32
32
32
A
B
Result
Overflow
Zero
4
ALUop
CarryOut
Notes: Now you remember what binary numbers are, let design an Arithmetic Logic Unit that can perform bitwise AND, bitwise OR, binary add, binary subtract, and et-on-less-than.
The type of operation the ALU perform will be selected by the ALUop bits.
The ALU I am going to show you in class is 4 bits wide (N = 4). The ALU you need to design for the next homework assignment will be 32 bits wide.
I will show you how to implement all these operations except the last one, which is left as your homework assignment.
+1 = 25 min. (Y:05)

## Slide 18: Set on Less Than (1)
1-bit in ALU (for bits 1-30)
0
3
Operation
1
0
1
b
2
ALUop
Less
(0:bits 1-30)
Result
CarryOut
Ainvert
CarryIn
0
1
a
Bnegate

## Slide 19: Set on Less Than (2)
Sign bit in ALU (bit 31)
Overflow
detection
0
3
Operation
a
1
0
1
b
2
Less
Result
Ainvert
CarryIn
Set
Overflow
Bnegate
0
1

## Slide 20: Set on Less Than (3)
Bit 0 in ALU
0
3
Operation
1
0
1
b
2
ALUop
Set
Result
CarryOut
Ainvert
CarryIn
0
1
a
Bnegate

## Slide 21: (Simplified) 1-bit MIPS ALU
and, or, nor, add, sub, slt

## Slide 22: (Simplified) 32-bit ALU
1-bit ALU

## Slide 23: Overflow

## Slide 24: Overflow Detection
Notes: Recalled from some earlier slides that the biggest positive number you can represent using 4-bit is 7 and the smallest negative you can represent is negative 8.
So any time your addition results in a number bigger than 7 or less than negative 8, you have an overflow.
Keep in mind is that whenever you try to add two numbers together that have different signs, that is adding a negative number to a positive number, overflow can NOT occur.
Overflow occurs when you to add two positive numbers together and the sum has a negative sign. Or, when you try to add negative numbers together and the sum has a positive sign.
If you spend some time, you can convince yourself that If the Carry into the most significant bit is NOT the same as the Carry coming out of the MSB, you have a overflow.
+2 = 41 min. (Y:21)

## Slide 25: Overflow Detection Logic
A0
B0
1-bit
ALU
Result0
CarryIn0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3
Overflow
X
Y
X XOR Y
0
0
0
0
1
1
1
0
1
1
1
0
Overflow = CarryIn[N-1] XOR CarryOut[N-1]
Notes: Recall the XOR gate implements the not equal function: that is, its output is 1 only if the inputs have different values.
Therefore all we need to do is connect the carry into the most significant bit and the carry out of the most significant bit to the XOR gate.
Then the output of the XOR gate will give us the Overflow signal.
+1 = 42 min. (Y:22)

## Slide 26: Dealing with Overflow
Some languages (e.g., C) ignore overflow
  Use MIPS addu, addui, subu instructions
Other languages (e.g., Ada, Fortran) require raising an exception
  Use MIPS add, addi, sub instructions
  On overflow, invoke exception handler
    Save PC in exception program counter (EPC) register
    Jump to predefined handler address
    mfc0 (move from coprocessor reg) instruction can retrieve (copy) EPC value (to a general purpose register), to return after corrective action (by jump register instruction)

## Slide 27: Zero Detection Logic
CarryIn0
A0
B0
1-bit
ALU
Result0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
CarryOut2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3
Zero
Zero Detection Logic is a one BIG NOR gate (support conditional jump)
Notes: Besides detecting overflow, our ALU also needs to indicate if the result is zero.
This is easy to do. All we need is a BIG NOR gate.
Then if any of the Result bit is not zero, then the output of the NOR gate will be low.
The only time the output of the NOR gate is high is when all the result bits are zeroes.
+1 = 43 min. (Y:23)

## Slide 28: Ripple Carry Adder
A0
B0
1-bit
ALU
Result0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3
CarryOut2
CarryIn0
CarryIn
CarryOut
A
B
Design Trick: look for parallelism and throw hardware at it
Carry bit may have to propagate from LSB to MSB => worst case delay: N-stage delay
Notes: The Adder we just built is called a Ripple Carry Adder because: Carry may have to propagate from the least significant bit to the most significant bit.
In other words, the combination of A0, B0, and CarryIn0 may cause CarryOut0 to become 1.
As a result of CarryOut0 going 1, CarryOut1 may become 1 and etc., etc., .... etc and propagate down the carry chain.
Recall the Carry Logic: CarryIn to CarryOut has a 2-gate delay.
So in the worst case, a N-bit ripple carry will have a 2N gate delay.
For a 32-bit adder, this means the worst case delay is 64 gates. This can be a problem.
So after the break, I will show you some faster way of designing an ALU.
+2 = 45 min. (Y:25)

## Slide 29: Carry-Lookahead Adder
a0
b0
c0
s0
c1
s0 = a0  b0  c0
c1 = a0b0 + a0c0 + b0c0
c1 = a0b0 + (a0 + b0)c0
= g0 + p0c0
c3= a2b2 + (a2 + b2)c2
= g2 + p2c2
= g2 + p2g1 + p2p1g0+p2p1p0c0
c2 = a1b1 + (a1 + b1)c1
= g1 + p1c1
= g1 + p1g0 + p1p0c0
Carry-lookahead adder

## Slide 30: Critical Path Delay
Ripple-Carry Adder
Delay = 2n + 1
Carry-Lookahead Adder
Delay = 4

## Slide 31: Multiplication
More complicated than addition
  Can be accomplished via shifting and adding
Double precision product is produced
More time and more area is required
0010
× 1011
0010
00100
000000
0010000
00010110
(multiplicand)
(multiplier)
(partial product array)
(product)

## Slide 32: Multiplication Hardware (1st Version)

## Slide 33: Multiplication Algorithm

## Slide 34: Multiplication Hardware (2nd Version)
32-bit Multiplicand register, 32 -bit ALU, 64-bit Product register (HI & LO in MIPS), (0-bit Multiplier register)

## Slide 35: Multiplication Hardware (2nd Version)
0010 x 0011
Multiplicand Product 0010 0000 0011
0010 0011
0010 0001 0001
0011 0001
0010 0001 1000
0010 0000 1100
0010 0000 0110
1a. Add multiplicand to left half of product and
place the result in left half of Product register
32nd
repetition?
2. Shift Product register right 1 bit
Done
Yes: 32 repetitions
No: < 32 repetitions
1. Test
Product0
Product0 = 0
Product0 = 1
Start

## Slide 36: MIPS Multiplication Instruction
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product  rd

## Slide 37: Divide: Paper & Pencil

## Slide 38: Divide Hardware - Version 1 (1)
Remainder
Quotient
Divisor
64-bit ALU
Shift Right
Shift Left
Write
Control
32 bits
64 bits
64 bits
64-bit Divisor register (initialized with 32-bit divisor in left half), 64-bit ALU, 64-bit Remainder register (initialized with 64-bit dividend), 32-bit Quotient register

## Slide 39
3. Shift Divisor register right 1 bit
No: < 33 repetitions
2b. Restore original value by adding Divisor to Remainder, place sum in Remainder, shift Quotient to the left, setting new least significant bit to 0
Test Remainder
Remainder < 0
Remainder  0
1. Subtract Divisor register from
Remainder register, and place the
result in Remainder register
2a. Shift Quotient register to left, setting new rightmost bit to 1
Done
Yes: 33 repetitions
Start: Place Dividend in Remainder
33rd
repetition?
0111 / 0010
Quot. Divisor Rem.
0000 00100000 00000111 11100111 00000111 0000 00010000 00000111 11110111 00000111 0000 00001000 00000111 11111111 00000111 0000 00000100 00000111 00000011 0001 00000011 0001 00000010 00000011 00000001 0011 00000001 0011 00000001 00000001
Divide Hardware - Version 1 (2)
Notes: Q: 0000 D: 0010 0000 R: 0000 0111  = 1110 0000
1: R = R Q: 0000 D: 0010 0000 R: 1110 0111
2b: +D, sl Q, 0 Q: 0000 D: 0010 0000 R: 0000 0111
3: Shr D Q: 0000 D: 0001 0000 R: 0000 0111  = 1111 0000
1: R = R Q: 0000 D: 0001 0000 R: 1111 0111
2b: +D, sl Q, 0 Q: 0000 D: 0001 0000 R: 0000 0111
3: Shr D Q: 0000 D: 0000 1000 R: 0000 0111  = 1111 1000
1: R = R Q: 0000 D: 0000 1000 R: 1111 1111
2b: +D, sl Q, 0 Q: 0000 D: 0000 1000 R: 0000 0111
3: Shr D Q: 0000 D: 0000 0100 R: 0000 0111  = 1111 1100
1: R = R Q: 0000 D: 0000 0100 R: 0000 0011
2a: sl Q, 1 Q: 0001 D: 0000 0100 R: 0000 0011
3: Shr D Q: 0000 D: 0000 0010 R: 0000 0011  = 1111 1110
1: R = R Q: 0000 D: 0000 0010 R: 0000 0001
2a: sl Q, 1 Q: 0011 D: 0000 0010 R: 0000 0001
3: Shr D Q: 0011 D: 0000 0001 R: 0000 0001
Recommend show 2 comp of divisor, show lines for subtract divisor and restore remainder

## Slide 40: Observations - Version 1
Half of the bits in divisor register always 0 => 1/2 of 64-bit adder is wasted => 1/2 of divisor is wasted
Instead of shifting divisor to right, shift remainder to left?
1st step cannot produce a 1 in quotient bit => switch order to shift first and then subtract => save 1 iteration
Eliminate Quotient register by combining with Remainder register as shifted left

## Slide 41: Divide Hardware - Version 2 (1)
Remainder
(Quotient)
Divisor
32-bit ALU
Write
Control
32 bits
64 bits
Shift Left
32-bit Divisor register, 32 -bit ALU, 64-bit Remainder register, (0-bit Quotient register)

## Slide 42: Divide Hardware - Version 2 (2)
0111 / 0010
Step Remainder Div. 0 0000 0111 0010
1.1 0000 1110
1.2 1110 1110
1.3b 0001 1100
2.2 1111 1100
2.3b 0011 1000 3.2 0001 1000
3.3a 0011 0001
4.2 0001 0001
4.3a 0010 0011
0001 0011
Test Remainder
No: < 32 repetitions
3b. Restore original value by adding Divisor to left half of Remainder, and place sum in left half of Remainder. Also shift Remainder to left, setting the new least significant bit to 0
Remainder < 0
Remainder  0
2. Subtract Divisor register from the left half of Remainder register, and place the
result in the left half of Remainder register
3a. Shift Remainder to left, setting new rightmost bit to 1
1. Shift Remainder register left 1 bit
Done. Shift left half of Remainder right 1 bit
Yes: 32 repetitions
32nd
repetition?
Start: Place Dividend in Remainder
Notes: D: 0010 R: 0000 0111
0: Shl R D: 0010 R: 0000 1110
1: R = R D: 0010 R: 1110 1110
2b: +D, sl R, 0 D: 0010 R: 0001 1100
1: R = R D: 0010 R: 1111 1100
2b: +D, sl R, 0 D: 0010 R: 0011 1000
1: R = R D: 0010 R: 0001 1000
2a: sl R, 1 D: 0010 R: 0011 0001
1: R = R D: 0010 R: 0001 0001
2a: sl R, 1 D: 0010 R: 0010 0011
Shr R(rh) D: 0010 R: 0001 0011

## Slide 43: MIPS Division Instruction
Instruction
div $t1, $t2 # t1 / t2
Quotient stored in Lo, remainder in Hi
mflo $t3 #copy quotient to t3
mfhi $t4 #copy remainder to t4
3-step process
Unsigned division:
divu $t1, $t2 # t1 / t2
  Just like div, except now interpret t1, t2 as unsigned integers instead of signed
  Answers are also unsigned, use mfhi, mflo to access
No overflow or divide-by-0 checking
  Software must perform checks if required

## Slide 44: Signed Divide
Remember signs, make positive, complement quotient and remainder if necessary
Let Dividend and Remainder have same sign and negate Quotient if Divisor sign & Dividend sign disagree,
  e.g., -7 2 = -3, remainder = -1
  -7 - 2 = 3, remainder = -1
  Satisfy Dividend =Quotient x Divisor + Remainder

## Slide 45: Observations: Multiply and Divide
Same hardware as multiply: Just need ALU to add or subtract, and 64-bit register to shift left (multiply: shift right)
Hi and Lo registers in MIPS combine to act as 64-bit register for multiply and divide
Remainder
(Quotient)
Divisor
32-bit ALU
Write
Control
32 bits
64 bits
Shift Left

## Slide 46: Multiply/Divide Hardware
Product/
Remainder
Multiplier/
Quotient
Multiplicand/
Divisor
32-bit ALU
Write
Control
32 bits
64 bits
Shift Left
Shift Right
32-bit Multiplicand/Divisor register, 32 -bit ALU, 64-bit Product/Remainder register, (0-bit Multiplier/Quotient register)

## Slide 47: Floating-Point Numbers
Representation for non-integral numbers
  Include very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
(normalized)
(not normalized)

## Slide 48: Floating-Point Standard
Defined by IEEE 754-1985 standard
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 49: IEEE Floating-Point Format
s
exponent
fraction/mantissa
1 bit
11 bits
52 bits
x = (−1)s × (1+fraction) × 2(exponent−1023)
s
exponent
fraction/mantissa
1 bit
8 bits
23 bits
x = (−1)s × (1+fraction) × 2(exponent−127)
Single-Precision
Double-Precision
exponent | fraction | Value represented
0000 0000 | 0 | 0
1111 1111 | 0 | ±∞
1111 1111 | non-zero | NaN

## Slide 50: Exercise L04-2
Ex-1: What is the IEEE single precision number 0x40C00000 representing in decimal?
Notes: Binary: [0][100 0000 1][100 0000 0000 0000 0000 0000]
Sign: +
Exponent: 129 – 127 = +2
Mantissa: 0b1.1
x = +0b1.1 x 2^(2) = +0b110 = +6

## Slide 51: Exercise L04-3
Ex-2: How to represent –0.5 in IEEE single precision binary floating-point format?
Notes: 0.5 = 0b0.1 = 0b1 x 2^(-1)
Exponent: (-1)+127 = 126 = 0b01111110
Sign = 1
Mantissa: 0000 … 0000
Answer:
1 01111110 000 0000 0000 0000 0000 0000

## Slide 52: Floating-Point Addition (1)
Consider a 4-digit decimal example
  9.999 × 101 + 1.610 × 10–1
1. Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102

## Slide 53: Floating-Point Addition (2)
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625

## Slide 54: FP Adder Hardware (1)
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined

## Slide 55: FP Adder Hardware (2)
Step 1
Step 2
Step 3
Step 4

## Slide 56: FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP ↔ integer conversion
Operations usually takes several cycles
  Can be pipelined

## Slide 57: FP Instructions in MIPS (1)
FP hardware is coprocessor 1
  Adjunct processor that extends the ISA
Separate FP registers
  32 single-precision: $f0, $f1, … $f31
  Paired for double-precision: $f0/$f1, $f2/$f3, …
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  lwc1, ldc1, swc1, sdc1
  e.g., ldc1 $f8, 32($sp)

## Slide 58: FP Instructions in MIPS (2)
Single-precision arithmetic
  add.s, sub.s, mul.s, div.s
  e.g., add.s $f0, $f1, $f6
Double-precision arithmetic
  add.d, sub.d, mul.d, div.d
  e.g., mul.d $f4, $f4, $f6
Single- and double-precision comparison
  c.xx.s, c.xx.d (xx is eq, lt, le, gt, ge)
  Sets or clears FP condition-code bit
  e.g. c.lt.s $f3, $f4
Branch on FP condition code true or false
  bc1t, bc1f
  e.g., bc1t TargetLabel