## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Datapath and Control
Our implementation of the MIPS is simplified
  Memory-reference instructions: lw, sw
  Arithmetic-logical instructions: add, sub, and, or, slt
  Control flow instructions: beq, j
Generic implementation
  Use the program counter (PC) to supply the instruction address and fetch the instruction from memory (and update the PC)
  Decode the instruction (and read registers)
  Execute the instruction
All instructions (except j) use the ALU after reading the registers
Fetch PC=PC+4
Decode
Execute

## Slide 3: Clock Methodology
The clock methodology defines when data in a state element is valid and stable relative to the clock
  State elements: A memory element such as a register
  Edge-triggered: All state changes occur on a clock edge
Typical execution
  Read contents of state elements  send values through combinational logic  write results to one or more state elements
Assumes state elements are written on every clock cycle; if not, need explicit write control signal
  Write occurs only when both the write control is asserted and the clock edge occurs

## Slide 4: Fetch Instructions
Fetch instructions involves
  Read the instruction from the Instruction Memory
  Update the PC value to be the address of the next (sequential) instruction
  PC is updated every clock cycle, so it does not need an explicit write control signal just a clock signal
  Read from the Instruction Memory is a combinational activity. It does not need an explicit read control signal
Fetch PC=PC+4
Decode
Execute

## Slide 5: Decode Instructions
Decode instructions involves
  Send the fetched instruction’s opcode and function field bits to the control unit
  Read two values from the Registers
    Register addresses are contained in the instruction
Fetch PC=PC+4
Decode
Execute

## Slide 6: Read Registers “Just in Case”
Note that both read ports of the Registers are active for all instructions during the decode cycle, using the rs and rt instruction field addresses
  Since haven’t decoded the instruction yet, don’t know what the instruction is
  Just in case the instruction uses values from the Registers do “work ahead” by reading the two source operands

## Slide 7: Executing R Format Operations
R format operations (add, sub, slt, and, or)
  Perform operation (op and funct) on values in rs and rt
  Store the result back into the Registers (into location rd)
  Note that register is not written every cycle (e.g. sw), so we need an explicit write control signal for the Registers
op
rs
rt
rd
shamt
funct
R format
31 25 20 15 10 5 0
Fetch PC=PC+4
Decode
Execute

## Slide 8: Execute Load and Store Operations (1)
Load and store operations have to
  Compute a memory address by adding the base register (in rs) to the 16-bit signed offset field in the instruction
    base register was read from the Registers during decode
    offset value in the low order 16 bits of the instruction, must be sign-extended to create a 32-bit signed value
  Store value, read from the Registers during decode, must be written to the Data Memory
  Load value, read from the Data Memory, must be stored in the Registers
OP
rs
rt
offset
I format
31 25 20 15 0

## Slide 9: Execute Load and Store Operations (2)

## Slide 10: Execute Branch Operations (1)
Branch operations have to
  Compare the operands read from the Registers during decode (rs and rt values) for equality (zero ALU output)
  Compute the branch target address by adding the updated PC to the sign-extended 16-bit offset field in the instruction
    “base register” is the updated PC
    Offset value in the low order 16 bits of the instruction must be sign extended to create a 32-bit signed value and then shifted left 2 bits to turn it into a word address
OP
rs
rt
offset
I format
31 25 20 15 0

## Slide 11: Executing Branch Operations (2)

## Slide 12: Execute Jump Operations
Jump operations have to
  Replace the lower 28 bits of the PC with the lower 26 bits of the fetched instruction shifted left by 2 bits
op
jump target address
J format
31 25 0

## Slide 13: Create a Single Datapath from the Parts
Assemble the datapath segments and add control lines and multiplexors as needed
Single-cycle design – fetch, decode and execute each instructions in one clock cycle
  No datapath resource can be used more than once per instruction, so some must be duplicated (e.g., separate Instruction Memory and Data Memory, several adders)
  Multiplexors needed at the input of shared elements with control lines to do the selection
  write signals to control writing to the Register File and Data Memory
Cycle time is determined by length of the longest path

## Slide 14: Datapath for R-type and Memory Instructions

## Slide 15: Add Branch Instructions

## Slide 16: Our Simple Control Structure
We wait for everything to settle down
  ALU might not produce “right answer” right away
  Read from Memory and Registers are combinational (as are ALU, adders, muxes, shifter, sign-extender)
  Use write signals along with the clock edge to determine when to write to the sequential elements (to the PC, to the Registers and to the Data Memory)
The clock cycle time is determined by the logic delay through the longest path
  We ignore some details like register setup and hold times

## Slide 17: Add the Control
Select the operations to perform (ALU, Register and Memory read/write)
Control the flow of data (multiplexor inputs)
Information comes from the 32 bits of the instruction
Observations
  Op field always in bits 31–26
  Addresses of two registers to be read are always specified by the rs and rt fields (bits 25–21 and 20–16)
  Base register for lw and sw always in rs (bits 25–21)
  Address of register to be written is in one of two places: in rt (bits 20–16) for lw; in rd (bits 15–11) for R-type instructions
  Offset for beq, lw, and sw always in bits 15–0

## Slide 18: Complete Single-Cycle Datapath

## Slide 19: ALU Control (1)
ALU used for
  Load/Store: add
  Branch: subtract (compare in beq)
  R-type: depends on funct field
ALU Control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 20: ALU Control (2)
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
Opcode | ALUOp | Opeation | funct | ALU function | ALU control
lw | 00 | load word | XXXXXX | add | 0010
Sw | 00 | store word | XXXXXX | add | 0010
Beq | 01 | branch equal | XXXXXX | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111

## Slide 21: Design the Main Control Unit
ALUOp |  | Funct field |  |  |  |  |  | Operation
ALUOp1 | ALUOp0 | F5 | F4 | F3 | F2 | F1 | F0 | 
0 | 0 | X | X | X | X | X | X | 0010
X | 1 | X | X | X | X | X | X | 0110
1 | X | X | X | 0 | 0 | 0 | 0 | 0010
1 | X | X | X | 0 | 0 | 1 | 0 | 0110
1 | X | X | X | 0 | 1 | 0 | 0 | 0000
1 | X | X | X | 0 | 1 | 0 | 1 | 0001
1 | X | X | X | 1 | 0 | 1 | 0 | 0111

## Slide 22: The Main Control Unit
Control signals derived from instruction
0
rs
rt
rd
shamt
funct
31:26
25:21
20:16
15:11
10:6
5:0
R-type
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
Load/Store
4
rs
rt
address
31:26
25:21
20:16
15:0
Branch
opcode
always read
read, except for load
write for R-type and load
sign-extend and add

## Slide 23: Complete Single-Cycle Datapath

## Slide 24: Datapath with Control

## Slide 25: R-type Instruction
1
0
0

## Slide 26: Load Instruction
1
0
1

## Slide 27: Branch-on-Equal Instruction
0
0
0
1

## Slide 28: Control Lines
Instruction | RegDst | ALUSrc | MemtoReg | RegWrite | MemRead | MemWrite | Branch | ALUOp
R-type 000000 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 10
lw 100011 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 00
sw 101011 | X | 1 | X | 0 | 0 | 1 | 0 | 00
beq 000100 | X | 0 | X | 0 | 0 | 0 | 1 | 01

## Slide 29: Implement Jumps
Jump uses word address
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
  00
Need an extra control signal decoded from opcode
2
address
31:26
25:0
Jump

## Slide 30: Datapath With Jump Added
0
0
0

## Slide 31: Single-Cycle Implementation Cycle Time
Unfortunately, though simple, the single cycle approach is not used because it is very slow
Clock cycle must have the same length for every instruction
What is the longest path (slowest instruction)?

## Slide 32: Instruction Critical Paths
Calculate cycle time assuming negligible delays (for muxes, control unit, sign extend, PC access, shift left 2, wires) except:
  Instruction and Data Memory (4 ns)
  ALU and adders (2 ns)
  Register File access (reads or writes) (1 ns)
Instruction | I Mem | Reg Rd | ALU Op | D Mem | Reg Wr | Total
R-type | 4 | 1 | 2 |  | 1 | 8
Load |  |  |  |  |  | 
store |  |  |  |  |  | 
beq |  |  |  |  |  | 
jump |  |  |  |  |  | 
4
1
2
4
1
12
4
1
2
4
11
4
1
2
7
4
4

## Slide 33: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction Memory → Registers → ALU → Data Memory → Registers
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast

## Slide 34: Single Cycle Disadvantages & Advantages
Uses the clock cycle inefficiently – the clock cycle must be timed to accommodate the slowest instruction
  Especially problematic for more complex instructions, e.g., floating-point multiplication
May be wasteful of area since some functional units (e.g., adders) must be duplicated since they can not be shared during a clock cycle
But it is simple and easy to understand
lw
sw
Cycle 1
waste
Cycle 2
Clk