## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Outline
Introduction to design a processor
Analyze the instruction set（step 1）
Build the datapath（steps 2 and 3）
A single-cycle implementation
Control for the single-cycle CPU（steps 4 and 5）
  Control of CPU operations
  ALU controller
  Main controller
Add jump instruction

## Slide 3: Introduction
CPU performance factors
  Instruction count
    Determined by ISA and compiler
  CPI (clock cycle per instruction) and cycle time
    Determined by CPU hardware
We will examine two MIPS implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: lw, sw
  Arithmetic/logical: add, sub, and, or, slt
  Control transfer: beq, j

## Slide 4: Instruction Execution
Use the program counter (PC) to supply the instruction address and fetch the instruction from memory
Decode the instruction (and read registers)
Execute the instruction
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch target address
  Access data memory for load/store
  PC  target address or PC + 4
Fetch PC=PC+4
Decode
Execute

## Slide 5: CPU Overview

## Slide 6: Multiplexers
Can’t just join wires together
  Use multiplexers

## Slide 7: Control

## Slide 8: Logic Design Basics
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational element
  Operate on data
  Output is a function of input
State (sequential) elements
  Store information

## Slide 9: Combinational Elements
AND-gate
  Y = A & B
A
B
Y
I0
I1
Y
M u x
S
Multiplexer
  Y = S ? I1 : I0
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)

## Slide 10: Sequential Elements（1）
Register: stores data in a circuit
  Use a clock signal to determine when to update the stored value
  Edge-triggered: update when Clk changes from 0 to 1
D
Clk
Q
Clk
D
Q

## Slide 11: Sequential Elements（2）
Register with write control
  Only updates on clock edge when write control input is 1
  Used when stored value is required later
D
Clk
Q
Write
Write
D
Q
Clk

## Slide 12: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element
  Longest delay determines clock period

## Slide 13: How to Design a Processor
1. Analyze instruction set (datapath requirements)
  The meaning of each instruction is given by the register transfers
  Datapath must include storage element
  Datapath must support each register transfer
2. Select set of datapath components and establish clocking methodology
3. Assemble datapath meeting the requirements
4. Analyze implementation of each instruction to determine setting of control points effecting register transfer
5. Assemble the control logic

## Slide 14: Outline
Introduction to design a processor
Analyze the instruction set (step 1)
Build the datapath (steps 2 and 3)
A single-cycle implementation
Control for the single-cycle CPU
  Control of CPU operations
  ALU controller
  Main controller
Add jump instruction

## Slide 15: Step 1 - Analyze Instruction Set
All MIPS instructions are 32 bits long with 3 formats
  R-type
  I-type
  J-type
The different fields are:
  op: Operation of the instruction
  rs, rt, rd: Source and destination register
  shamt: Shift amount
  funct: Selects variant of the “op” field
  address / immediate
  target address: Target address of jump
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: One of the most important thing you need to know before you start designing a processor is how the instructions look like.
Or in more technical term, you need to know the instruction format. One good thing about the MIPS instruction set is that it is very simple.
First of all, all MIPS instructions are 32 bits long and there are only three instruction formats: (a) R-type, (b) I-type, and (c) J-type.
The different fields of the R-type instructions are:
(a) OP specifies the operation of the instruction.
(b) Rs, Rt, and Rd are the source and destination register specifiers.
(c) Shamt specifies the amount you need to shift for the shift instructions.
(d) Funct selects the variant of the operation specified in the p?field.
For the I-type instruction, bits 0 to 15 are used as an immediate field. I will show you how this immediate field is used differently by different instructions.
Finally for the J-type instruction, bits 0 to 25 become the target address of the jump.
+3 = 10 min. (X:50)

## Slide 16: Our Example: A MIPS Subset
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
address
0
16
21
26
31
6 bits
26 bits
R-Type
  add rd, rs, rt
  sub rd, rs, rt
  and rd, rs, rt
  or rd, rs, rt
  slt rd, rs, rt
Load/Store
  lw rt,rs,imm16
  sw rt,rs,imm16
Immediate operand
  addi rt,rs,imm16
Branch
  beq rs,rt,imm16
Jump
  j target
Notes: In today lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register. (Note that dest is the Rt field!)
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to from the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specified the registers we need to compare.
If these two registers are equal, we will branch to a location offset by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 17: Logical Register Transfer
MEM[ PC ] = op | rs | rt | rd | shamt | funct or = op | rs | rt | Imm16 or = op | Imm26 (added at the end)
Inst Register transfers
ADD R[rd] <- R[rs] + R[rt]; PC <- PC + 4
SUB R[rd] <- R[rs] - R[rt]; PC <- PC + 4
LOAD R[rt] <- MEM[ R[rs] + sign_ext(Imm16)]; PC <- PC + 4
STORE MEM[ R[rs] + sign_ext(Imm16) ] <-R[rt]; PC <- PC + 4
ADDI R[rt] <- R[rs] + sign_ext(Imm16)]; PC <- PC + 4
BEQ if (R[rs] == R[rt]) then PC <- PC + 4 + sign_ext(Imm16)] || 00
else PC <- PC + 4
RTL gives the meaning of the instructions
All start by fetching the instruction, read registers, then use ALU => simplicity and regularity help

## Slide 18: Requirements of Instruction Set
After checking the register transfers, we can see that datapath needs the followings:
  Memory
    Store instructions and data
  Registers (32 x 32)
    Read RS
    Read RT
    Write RT or RD
  PC
  Extender for zero- or sign-extension
  Add and sub register or extended immediate (ALU)
  Add 4 or extended immediate to PC

## Slide 19: Outline
Introduction to design a processor
Analyze the instruction set (step 1)
Build the datapath (steps 2, 3)
A single-cycle implementation
Control for the single-cycle CPU
  Control of CPU operations
  ALU controller
  Main controller
Add jump instruction

## Slide 20: Step 2a - Combinational Components for Datapath
Basic building blocks of combinational logic elements
32
32
A
B
32
Sum
Carry
32
32
A
B
32
Result
ALU control
32
A
B
32
Y
32
Select
Adder
MUX
ALU
CarryIn
Adder
MUX
ALU
4
Notes: Based on the Register Transfer Language examples we have so far, we know we will need the following combinational logic elements.
We will need an adder to update the program counter.
A MUX to select the results.
And finally, an ALU to do various arithmetic and logic operation.
+1 = 30 min. (Y:10)

## Slide 21: Step 2b - Sequential Components for Datapath
Register
  Similar to the D Flip Flop except
    N-bit input and output
    Write Enable input
  Write Enable
    negated (0): Data Out will not change
    asserted (1): Data Out will become Data In
Clk
Data In
Write Enable
N
N
Data Out
Notes: As far as storage elements are concerned, we will need a N-bit register that is similar to the D flip-flop I showed you in class.
The significant difference here is that the register will have a Write Enable input.
That is the content of the register will NOT be updated if Write Enable is not asserted (0).
The content is updated at the clock tick ONLY if the Write Enable signal is asserted (1).
+1 = 31 min. (Y:11)

## Slide 22: Storage Element - Register File
Consists of 32 registers
  Appendix B.8
  Two 32-bit output buses
  busA and busB
  One 32-bit input bus: busW
Register is selected by
  RA selects the register to put on busA (data)
  RB selects the register to put on busB (data)
  RW selects the register to be written via busW (data) when Write Enable is 1
Clock input (CLK)
  The CLK input is a factor ONLY during write operation
  During read, behaves as a combinational circuit
Clk
busW
Write Enable
32
32
busA
32
busB
5
5
5
RW
RA
RB
32-bit
Registers
Notes: We will also need a register file that consists of 32 32-bit registers with two output busses (busA and busB) and one input bus.
The register specifiers Ra and Rb select the registers to put on busA and busB respectively.
When Write Enable is 1, the register specifier Rw selects the register to be written via busW.
In our simplified version of the register file, the write operation will occurs at the clock tick.
Keep in mind that the clock input is a factor ONLY during the write operation.
During read operation, the register file behaves as a combinational logic block.
That is if you put a valid value on Ra, then bus A will become valid after the register file access time.
Similarly if you put a valid value on Rb, bus B will become valid after the register file access time. In both cases (Ra and Rb), the clock input is not a factor.
+2 = 33 min. (Y:13)

## Slide 23: Storage Element - Memory
Clk
Data In
Write Enable
32
32
DataOut
Address
Memory (idealized)
  Appendix B.8
  One input bus: Data In
  One output bus: Data Out
Word is selected by
  Address selects the word to put on Data Out
  Write Enable = 1: address selects the memory word to be written via the Data In bus
Clock input (CLK)
  The CLK input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block
    Address valid => Data Out valid after access time
    No need for read control
Notes: The last storage element you will need for the datapath is the idealized memory to store your data and instructions.
This idealized memory block has just one input bus (DataIn) and one output bus (DataOut).
When Write Enable is 0, the address selects the memory word to put on the Data Out bus.
When Write Enable is 1, the address selects the memory word to be written via the DataIn bus at the next clock tick.
Once again, the clock input is a factor ONLY during the write operation.
During read operation, it behaves as a combinational logic block.
That is if you put a valid value on the address lines, the output bus DataOut will become valid after the access time of the memory.
+2 = 35 min. (Y:15)

## Slide 24: Step 3a - Datapath Assembly
Instruction fetch unit: common operations
  Fetch the instruction: mem[PC]
  Update the program counter
    Sequential code: PC <- PC + 4
    Branch and Jump: PC <- “Something else”
Notes: Now let take a look at the first major component of the datapath: the instruction fetch unit.
The common RTL operations for all instructions are:
(a) Fetch the instruction using the Program Counter (PC) at the beginning of an
instruction execution (PC -> Instruction Memory -> Instruction Word).
(b) Then at the end of the instruction execution, you need to update the
Program Counter (PC -> Next Address Logic -> PC).
More specifically, you need to increment the PC by 4 if you are executing sequential code.
For Branch and Jump instructions, you need to update the program counter to omething else?other than plus 4.
I will show you what is inside this Next Address Logic block when we talked about the Branch and Jump instructions.
For now, let focus our attention to the Add and Subtract instructions.
+2 = 37 min. (Y:17)

## Slide 25: Step 3b - Add and Subtract
R[rd] <- R[rs] op R[rt] Ex: add rd, rs, rt
  Ra, Rb, Rw come from instruction’s rs, rt, and rd fields
  ALU and RegWrite: control logic after decode
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
rs
rt
rd
4
I
n
s
t
r
u
c
t
i
o
n
R
e
g
i
s
t
e
r
s
W
r
i
t
e
r
e
g
i
s
t
e
r
R
e
a
d
d
a
t
a
1
R
e
a
d
d
a
t
a
2
R
e
a
d
r
e
g
i
s
t
e
r
1
R
e
a
d
r
e
g
i
s
t
e
r
2
W
r
i
t
e
d
a
t
a
A
L
U
r
e
s
u
l
t
A
L
U
Z
e
r
o
R
e
g
W
r
i
t
e
A
L
U
o
p
e
r
a
t
i
o
n
(funct)
Notes: And here is the datapath that can do the trick.
First of all, we connect the register file Ra, Rb, and Rw input to the Rd, Rs, and Rt fields of the instruction bus (points to the format diagram).
Then we need to connect busA and busB of the register file to the ALU.
Finally, we need to connect the output of the ALU to the input bus of the register file.
Conceptually, this is how it works.
The instruction bus coming out of the Instruction memory will set the Ra and Rb to the register specifiers Rs and Rt.
This causes the register file to put the value of register Rs onto busA and the value of register Rt onto busB, respectively.
By setting the ALUctr appropriately, the ALU will perform either the Add and Subtract for us.
The result is then fed back to the register file where the register specifier Rw should already be set to the instruction bus Rd field.
Since the control, which we will design in our next lecture, should have already set the RegWr signal to 1, the result will be written back to the register file at the next clock tick (points to the Clk input).
+3 = 42 min. (Y:22)

## Slide 26: Step 3c - Load/Store Operations
R[rt]<-Mem[R[rs]+SignExt[imm16]] Ex: lw rt,rs,imm16
rs
rt
11
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
4
rt
Notes: Once again we cannot use the instruction Rd field for the Register File Rw input because load is a I-type instruction and there is no such thing as the Rd field in the I format.
So instead of Rd, the Rt field is used to specify the destination register through this two to one multiplexor.
The first operand of the ALU comes from busA of the register file which contains the value of Register Rs (points to the Ra input of the register file).
The second operand, on the other hand, comes from the immediate field of the instruction.
Instead of using the Zero Extender I used in datapath for the or immediate datapath, I have to use a more general purpose Extender that can do both Sign Extend and Zero Extend.
The ALU then adds these two operands together to form the memory address.
Consequently, the output of the ALU has to go to two places:
(a) First the address input of the data memory.
(b) And secondly, also to the input of this two-to-one multiplexer.
The other input of this multiplexer comes from the output of the data memory so we can place the output of the data memory onto the register file input bus for the load instruction.
For Add, Subtract, and the Or immediate instructions, the output of the ALU will be selected to be placed on the input bus of the register file.
In either case, the control signal RegWr should be asserted so the register file will be written at the end of the cycle.
+3 = 60 min. (Y:40)

## Slide 27: R-Type/Load/Store Datapath

## Slide 28: Step 3d - Branch Operations
beq rs, rt, imm16
  mem[PC] /*Fetch inst. from memory */
  Equal <- R[rs] == R[rt] /* Calculate branch condition */
  if (COND == 0) /* Calculate next inst. Address */
    PC <- PC + 4 + ( SignExt(imm16) x 4 )
  else
    PC <- PC + 4
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: How does the branch on equal instruction work?
Well it calculates the branch condition by subtracting the register selected by the Rt field from the register selected by the Rs field.
If the result of the subtraction is zero, then these two registers are equal and we take a branch. Otherwise, we keep going down the sequential path (PC <- PC +4).
+1 = 65 min. (Y:45)

## Slide 29: Datapath for Branch Operations
beq rs, rt, imm16
4
Notes: The datapath for calculating the branch condition is rather simple.
All we have to do is feed the Rs and Rt fields of the instruction into the Ra and Rb inputs of the register file.
Bus A will then contain the value from the register selected by Rs.
And bus B will contain the value from the register selected by Rt.
The next thing to do is to ask the ALU to perform a subtract operation and feed the output Zero to the next address logic.
How does the next address logic block look like?
Well, before I show you that, let take a look at the binary arithmetics behind the program counter (PC).
+2 = 67 min. (Y:47)

## Slide 30: Outline
Introduction to design a processor
Analyze the instruction set
Build the datapath
A single-cycle implementation
Control for the single-cycle CPU
  Control of CPU operations
  ALU controller
  Main controller
Add jump instruction

## Slide 31: A Single Cycle Datapath

## Slide 32: Data Flow during add
Clocking
Data flows in other paths
100..0100

4

## Slide 33: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element
  Longest delay determines clock period

## Slide 34: Clocking Methodology
Define when signals are read and written
Assume edge-triggered
  Values in storage (state) elements updated only on a clock edge => clock edge should arrive only after input signals stable
  Any combinational circuit must have inputs from and outputs to storage elements
  Clock cycle: Time for signals to propagate from one storage element, through combinational circuit, to reach the second storage element
  A register can be read, its value propagated through some combinational circuit, new value is written back to the same register, all in same cycle => no feedback within a single cycle

## Slide 35: Register-Register Timing
32
Result
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rd
ALU
Clk
PC
Rs, Rt, Rd,
Op, Func
Clk-to-Q
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA, B
Register File Access Time
Old Value
New Value
busW
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write
Occurs Here
Ideal
Instruction
Memory
PC
32
Clk
35
Notes: Let take a more quantitative picture of what is happening.
At each clock tick, the Program Counter will present its latest value to the Instruction memory after Clk-to-Q time.
After a delay of the Instruction Memory Access time, the Opcode, Rd, Rs, Rt, and Function fields will become valid on the instruction bus.
Once we have the new instruction, that is the Add or Subtract instruction, on the instruction bus, two things happen in parallel.
First of all, the control unit will decode the Opcode and Func field and set the control signals ALUctr and RegWr accordingly. We will cover this in the next lecture.
While this is happening (points to Control Delay), we will also be reading the register file (Register File Access Time).
Once the data is valid on busA and busB, the ALU will perform the Add or Subtract operation based on the ALUctr signal.
Hopefully, the ALU is fast enough that it will finish the operation (ALU Delay) before the next clock tick.
At the next clock tick, the output of the ALU will be written into the register file because the RegWr signal will be equal to 1.
+3 = 45 min. (Y:25)

## Slide 36: The Critical Path
Critical Path (Load Operation) =
PC’s Clk-to-Q +
Instruction memory’s Access Time +
Register file’s Access Time +
ALU to Perform a 32-bit Add +
Data Memory Access Time +
Setup Time for Register File Write +
Clock Skew
Clk
5
Rw
Ra
Rb
32 32-bit
Registers
Rd
ALU
Clk
Data In
Data
Address
Ideal
Data
Memory
Instruction
Instruction
Address
Ideal
Instruction
Memory
Clk
PC
5
Rs
5
Rt
16
Imm
32
32
32
32
A
B
Next Address
Register file and ideal memory
  During read, behave as combinational logic
    Address valid => Output valid after access time
Notes: Now with the clocking methodology back in your mind, we can think about how the critical path of our bstract?datapath may look like.
One thing to keep in mind about the Register File and Ideal Memory (points to both Instruction and Data) is that the Clock input is a factor ONLY during the write operation.
For read operation, the CLK input is not a factor. The register file and the ideal memory behave as if they are combinational logic.
That is you apply an address to the input, then after certain delay, which we called access time, the output is valid.
We will come back to these points (point to the ehave?bullets) later in this lecture.
But for now, let look at this bstract?datapath critical path which occurs when the datapath tries to execute the Load instruction.
The time it takes to execute the load instruction are the sum of:
(a) The PC clock-to-Q time.
(b) The instruction memory access time.
(c) The time it takes to read the register file.
(d) The ALU delay in calculating the Data Memory Address.
(e) The time it takes to read the Data Memory.
(f) And finally, the setup time for the register file and clock skew.
+3 = 21 (Y:01)

## Slide 37: Worst Case Timing (Load)
Clk
PC
Rs, Rt, Rd,
Op, Func
Clk-to-Q
ALUctr
Instruction Memoey Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA
Register File Access Time
Old Value
New Value
busB
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
ExtOp
Old Value
New Value
ALUSrc
Old Value
New Value
MemtoReg
Old Value
New Value
Address
Old Value
New Value
busW
Old Value
New
Delay through Extender & Mux
Register
Write Occurs
Data Memory Access Time
Notes: This timing diagram shows the worst case timing of our single cycle datapath which occurs at the load instruction.
Clock to Q time after the clock tick, PC will present its new value to the Instruction memory.
After a delay of instruction access time, the instruction bus (Rs, Rt, ...) becomes valid.
Then three things happens in parallel:
(a) First the Control generates the control signals (Delay through Control Logic).
(b) Secondly, the regiser file is access to put Rs onto busA.
(c) And we have to sign extended the immediate field to get the second operand (busB).
Here I asuume register file access takes longer time than doing the sign extension so we have to wait until busA valid before the ALU can start the address calculation (ALU delay).
With the address ready, we access the data memory and after a delay of the Data Memory Access time, busW will be valid.
And by this time, the control unit whould have set the RegWr signal to one so at the next clock tick, we will write the new data coming from memory (busW) into the register file.
+3 = 77 min. (Y:57)

## Slide 38: Outline
Introduction to design a processor
Analyze the instruction set
Build the datapath
A single-cycle implementation
Control for the single-cycle CPU
  Control of CPU operations (step 4)
  ALU controller ( step 5a)
  Main controller (step 5b)
Add jump instruction

## Slide 39: Step 4 - Control Points and Signals
ALUctr
RegDst
ALUSrc
MemRd
MemtoReg
MemWr
Equal
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rs
Rt
PCsrc
Addr
Inst.
Memory
Datapath
Control
Op
<21:25>
Funct
RegWr

## Slide 40: Datapath with Mux and Control
Control point

## Slide 41: Design Main Control
Some observations
  opcode (Op[5-0]) is always in bits 31-26

## Slide 42: Datapath with Control Unit

## Slide 43: Instruction Fetch at Start of Add
instruction <- mem[PC]; PC + 4

## Slide 44: Instruction Decode of Add
Fetch the two operands and decode instruction:

## Slide 45: ALU Operation during Add
R[rs] + R[rt]

## Slide 46: Write Back at the End of Add
R[rd] <- ALU; PC <- PC + 4

## Slide 47: Datapath Operation for lw
R[rt] <- Memory {R[rs] + SignExt[imm16]}

## Slide 48: Datapath Operation for beq
if (R[rs]-R[rt]==0) then Zero<-1 else Zero<-0
if (Zero==1) then PC=PC+4+signExt[imm16]*4; else PC = PC + 4

## Slide 49: Outline
Introduction to design a processor
Analyze the instruction set
Build the datapath
A single-cycle implementation
Control for the single-cycle CPU
  Control of CPU operations (step 4)
  ALU controller (step 5a)
  Main controller (step 5b)
Add jump instruction

## Slide 50: Step 5a - ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on funct field
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 51: Our Plan for the Controller
ALUop is 2-bit wide to represent
  Load/store requires the ALU to perform add (00)
  Beq requires the ALU to perform sub (01)
  “R-type” needs to reference func field (10)
R-type
lw
sw
beq
jump
ALUop (Symbolic)
“R-type”
Add
Add
Subtract
xxx
ALUop<1:0>
10
00
00
01
xxx
Main
Control
Op code
6
ALU
Control
(Local)
func
2
6
ALUop
ALUctr
4
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
R-type
ALU
7
Notes: Well the answer is 2 because we only need to represent 4 things: -type,?the Or operation, the Add operation, and the Subtract operation.
If you are implementing the entire MIPS instruction set, then ALUop has to be 3 bits wide because we will need to repreent 5 things: R-type, Or, Add, Subtract, and AND.
Here I show you the bit assignment I made for the 3-bit ALUop.
With this bit assignment in mind, let figure out what the local control ALU Control has to do.
+1 = 26 min. (Y:26)

## Slide 52: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw | 00 | load word | XXXXXX | add | 0010
sw | 00 | store word | XXXXXX | add | 0010
beq | 01 | branch equal | XXXXXX | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111

## Slide 53: Logic Equation for ALUctr
x
ALUop
func
bit<1>
bit<0>
bit<2>
bit<1>
bit<0>
bit<3>
0
0
x
ALUctr
1
0
bit<2>
bit<1>
bit<0>
x
1
0
1
x
0
1
x
0
1
x
0
1
x
x
x
0
0
0
0
x
x
0
1
0
0
x
0
0
0
1
0
1
0
1
0
0
1
1
1
0
0
1
1
x
1
x
x
0
0
1
1
0
1
0
1
1
1
bit<4>
bit<5>
x
x
x
x
x
x
x
x
x
x
x
x
x
bit<3>
0
0
0
0
0
0
0

## Slide 54: Logic Equation for ALUctr2
ALUctr2 = ALUop0 + ALUop1‧func2’‧func1‧func0’
ALUop
func
bit<1>
bit<0>
ALUctr<2>
x
1
1
1
x
1
1
x
bit<2>
x
0
0
bit<1>
x
1
1
bit<0>
x
0
0
1
bit<3>
x
0
1
This makes func<3> a don’t care
bit<4>
x
x
x
bit<5>
x
x
x
Notes: From the truth table we had before the break, we can derive the logic equation for ALUctr bit 2 but collecting all the rows that has ALUCtr bit 2 equals to 1 and this table is the result.
Each row becomes a product term and we need to OR the prodcut terms together.
Notice that the last row are identical except the bit<3> of the func fields. One is zero and the other is one. Together, they make bit<3> a don care term.
With all these don care terms, the logic equation is rather simple.
The first prodcut term is: not ALUOp<2> and ALUOp<0>.
The second product term, after we making Func<3> a don care becomes ...
+2 = 57 min. (Y:37)

## Slide 55: Logic Equation for ALUctr1
ALUctr1 = ALUop1’+ ALUop1‧func2’‧func0’
ALUop
func
bit<1>
bit<0>
0
0
ALUctr<1>
x
1
1
x
1
x
1
x
bit<2>
x
x
0
0
0
bit<0>
x
x
0
0
0
1
1
1
1
1
bit<3>
x
x
0
0
1
bit<1>
x
x
0
1
1
bit<4>
x
x
x
x
x
bit<5>
x
x
x
x
x
Notes: Here is the truth table when we collect all the rows whereALCctr bit<1> equals to 1.
Once again, we can simplify the table by noticing that the first two rows are different only at the ALUop bit<0> position. We can make ALUop bit<0> into a don care.
Similarly, the last three rows can be combined to make Func bit<3> and bit<1> into don cares.
Consequently, the logic equation for ALUctr bit<1> becomes ...
+2 = 59 min. (Y:39)

## Slide 56: Logic Equation for ALUctr0
ALUctr0 = ALUop1‧func3’‧func2‧func1’‧func0 + ALUop1‧func3‧func2’‧func1‧func0’
ALUop
func
bit<1>
bit<0>
ALUctr<0>
1
x
1
1
x
bit<3>
0
1
bit<2>
1
0
bit<1>
0
1
bit<0>
1
0
1
bit<4>
x
x
bit<5>
x
x
Notes: Finally, after we gather all the rows where ALUctr bit 0 are 1, we have this truth table.
Well, we are out of luck here. I don see any simple way to simplify these product terms by just looking at them.
There may be some if you draw out the 7 dimension K map but I am not going to try it.
So I just write down the logic equations as it is.
+2 = 61 min. (Y:41)

## Slide 57: The Resultant ALU Control Block
0
Operation3

## Slide 58: Outline
Introduction to design a processor
Analyze the instruction set
Build the datapath
A single-cycle implementation
Control for the single-cycle CPU
  Control of CPU operations
  ALU controller
  Main controller (step 5b)
Add jump instruction

## Slide 59: Step 5b - The Main Control Unit
Control signals derived from instruction
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
Branch
opcode
always read
read, except for load
write for R-type and load
sign-extend and add

## Slide 60: Truth Table of Control Signals (6 inputs and 9 outputs)
add
sub
lw
sw
beq
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
Branch
ALUop1
ALUop0
1
0
0
1
0
0
1
0
1
0
0
1
0
0
1
0
0
1
1
1
0
0
0
0
x
1
x
0
1
0
0
0
x
0
x
0
0
1
0
1
func
op
00 0000
00 0000
10 0011
10 1011
00 0100
Appendix A
10 0000
See
10 0010
Don’t Care
MemRead
0
0
1
0
0
Main
Control
Op code
6
ALU
Control
(Local)
func
2
6
ALUop
ALUctr
4
RegDst
ALUSrc
:
Notes: Here is a table summarizing the control signals setting for the seven (add, sub, ...) instructions we have looked at.
Instead of showing you the exact bit values for the ALU control (ALUctr), I have used the symbolic values here.
The first two columns are unique in the sense that they are R-type instrucions and in order to uniquely identify them, we need to look at BOTH the op field as well as the func fiels.
Ori, lw, sw, and branch on equal are I-type instructions and Jump is J-type. They all can be uniquely idetified by looking at the opcode field alone.
Now let take a more careful look at the first two columns. Notice that they are identical except the last row.
So we can combine these two rows here if we can elay?the generation of ALUctr signals.
This lead us to something call ocal decoding.
+3 = 42 min. (Y:22)

## Slide 61: Truth Table for RegWrite
R-type
lw
sw
beq
RegWrite
1
1
0
0
Op code
00 0000
10 0011
10 1011
00 0100
RegWrite = R-type + lw
  = op5’‧op4’‧op3’‧op2’‧op1’‧op0’ (R-type)
  + op5‧op4’‧op3’‧op2’‧op1‧ op0 (lw)
op<0>
op<5>
.
.
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
R-type
lw
sw
beq
jump
RegWrite
X
Notes: For example, consider the control signal RegWrite.
If we treat all the don’t cares as zeros, this row here means RegDest has to be equal to one whenever we have a R-type, or an OR immediate, or a load instruction.
Since we can determine whether we have any of these instructions (point to the column headers) by looking at the bits in the P?field, we can transform this symbolic equation to this binary logic equation.
For example, the first product term here say we have a R-type instruction whenever all the bits in the OP field are zeros.
So each of these big AND gates implements one of the columns (R-type, ori, ...) in our table. Or in more technical terms, each AND gate implements a product term.
In order to finish implementing this logic equation, we have to OR the proper terms together.
In the case of the RegWrite signal, we need to OR the R-type, ORi, and load terms together.
+2 = 67 min. (Y:47)

## Slide 62: Programmable Logic Array Implementation of Main Control

## Slide 63: Outline
Introduction to design a processor
Analyze the instruction set (step 1)
Build the datapath (steps 2, 3)
A single-cycle implementation
Control for the single-cycle CPU
  Control of CPU operations
  ALU controller
  Main controller
Add jump instruction

## Slide 64: Implement Jump
Jump uses word address
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
  00
Need an extra control signal decoded from opcode
000010
address
31:26
25:0
Jump

## Slide 65: Put it Altogether (+ jump instruction)

## Slide 66: Drawback of Single-Cycle Design
Long cycle time
  Cycle time must be long enough for the load instruction
    PC’s Clock-to-Q +
    Instruction Memory Access Time +
    Register File Access Time +
    ALU Delay (address calculation) +
    Data Memory Access Time +
    Register File Setup Time +
    Clock Skew
Cycle time for load is much longer than needed for all other instructions
Notes: Well, the last slide pretty much illustrate one of the biggest disadvantage of the single cycle implementation: it has a long cycle time.
More specifically, the cycle time must be long enough for the load instruction which has the following components: Clock to Q time of the PC, ....
Having a long cycle time is a big problem but not the the only problem.
Another problem of this single cycle implementation is that this cycle time, which is long enough for the load instruction, is too long for all other instructions.
We will show you why this is bad and what we can do about it in the next few lectures.
That all for today.
+2 = 79 min (Y:59)

## Slide 67: Summary
Single cycle datapath => CPI=1, Clock cycle time long
MIPS makes control easier
  Instructions same size
  Source registers always in same place
  Immediates same size, location
  Operations always on registers/immediates