## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Single-Cycle Advantages & Disadvantages
Uses the clock cycle inefficiently – the clock cycle must be timed to accommodate the slowest instruction
  Especially problematic for more complex instructions, e.g., floating-point multiplication
May be wasteful of area since some functional units (e.g., adders) must be duplicated since they can not be shared during a clock cycle
But it is simple and easy to understand
lw
sw
Cycle 1
waste
Cycle 2
Clk

## Slide 3: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
  4-load speedup = 8/3.5 = 2.3
  20-load speedup = 40/11.5 = 3.478
Under ideal conditions
  The speedup from pipelining ≈ The number of pipe stages

## Slide 4: Five Stages of Load Instruction
Five stages, one step per stage
IF: Instruction fetch from (instruction) memory
ID: Instruction decode & register read
EX: Execute operation or calculate address
MEM: Access (data) memory operand
WB: Write result back to register

## Slide 5: Pipeline Performance (1)
Assume time for stages is
  100 ns for register read or write
  200 ns for other stages
Compare pipelined datapath with single-cycle datapath
Instruction | IF | Reg Read | ALU Op | Mem Access | Reg Write | Total
lw | 200 | 100 | 200 | 200 | 100 | 800
sw | 200 | 100 | 200 | 200 |  | 700
R-format | 200 | 100 | 200 |  | 100 | 600
beq | 200 | 100 | 200 |  |  | 500

## Slide 6: Pipeline Performance (2)

## Slide 7: Pipeline Speedup
If all stages are balanced, i.e., all take the same time
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease
Time between instructionspipelined = | Time between instructionsnonpipelined
 | Number of pipeline stages

## Slide 8: Pipelining and ISA Design
MIPS ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in the 3rd stage, access memory in the 4th stage
  Alignment of memory operands
    Memory access takes only one cycle

## Slide 9: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  The decision on control action depends on previous instruction

## Slide 10: Structure Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 11: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3
We may need to insert a pipeline stall (or bubble)

## Slide 12: Forwarding (or Bypassing)
Use result when it is computed
  Do not wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 13: Load-Use Data Hazard
Cannot always avoid stalls by forwarding
  If value not computed when needed
  Can not forward in time!

## Slide 14: Reorder Code to Avoid Pipeline Stalls
Reorder code to avoid the use of load result in the next instruction
Consider the C-code
  a = b + e; c = b + f;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall

## Slide 15: Control Hazards
Branch determines flow of control
  Fetch next instruction depends on branch outcome
  Pipeline cannot always fetch correct instruction
    Still working on ID stage of branch
In MIPS pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage

## Slide 16: Stall on Branch
Wait until branch outcome determined before fetching the next instruction
  Conservative approach: Stall immediately after fetching a branch, wait until outcome of branch is known and fetch branch address

## Slide 17: Branch Prediction
Longer pipelines cannot readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In MIPS pipeline
  Can predict branches not taken
  Fetch instruction after branch, with no delay

## Slide 18: Predict Branches Are Not Taken
Prediction Correct
No penalty
Prediction Incorrect
Stall

## Slide 19: More-Realistic Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 20: Pipeline Big-Picture Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation

## Slide 21: MIPS Pipelined Datapath
WB
Data hazard
MEM
Control hazard

## Slide 22: Pipeline Registers
Need registers between stages
  To hold information produced in previous cycle
[64]
[128]
[97]
[64]

## Slide 23: Timeline of Instruction Execution

## Slide 24: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  “Single-clock-cycle” pipeline diagram
    Shows pipeline usage in a single cycle
    Highlight resources used
We will look at “single-clock-cycle” diagrams for load & store

## Slide 25: IF for Load

## Slide 26: ID for Load

## Slide 27: EX for Load

## Slide 28: MEM for Load

## Slide 29: WB for Load (with bug)
Incorrect destination register

## Slide 30: Corrected Datapath for Load

## Slide 31: EX for Store

## Slide 32: MEM for Store

## Slide 33: WB for Store

## Slide 34: Multi-Cycle Pipeline Diagram (1)
Traditional diagram

## Slide 35: Multi-Cycle Pipeline Diagram (2)
Resources usage is shown

## Slide 36: Single-Cycle Pipeline Diagram
State of the pipeline at a specific cycle

## Slide 37: Pipelined Datapath with Control Signals

## Slide 38: Control Signals (1)

## Slide 39: Control Signals (2)

## Slide 40: Pipeline Control
Control signals derived from instruction
  As in single-cycle implementation

## Slide 41: Pipeline Datapath with Control

## Slide 42: Data Hazards in ALU Instructions
Consider this sequence
sub $2, $1,$3 # Register $2 written by sub
and $12,$2,$5 # 1st operand($2) depends on sub
or $13,$6,$2 # 2nd operand($2) depends on sub
add $14,$2,$2 # 1st($2) & 2nd($2) depend on sub
sw $15,100($2) # Base ($2) depends on sub
We can resolve hazards with forwarding
  How do we detect when to forward?

## Slide 43: Dependencies and Forwarding

## Slide 44: Detect the Need to Forward (1)
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs = register number for Rs sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs, ID/EX.RegisterRt
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRt
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRt
Forward from EX/MEM pipeline registers
Forward from MEM/WB pipeline registers

## Slide 45: Detect the Need to Forward (2)
But only if forwarding instruction will write to a register
  EX/MEM.RegWrite
  MEM/WB.RegWrite
And only if Rd for that instruction is not $zero
  EX/MEM.RegisterRd ≠ 0
  MEM/WB.RegisterRd ≠ 0

## Slide 46: Forwarding Paths

## Slide 47: Forwarding Control

## Slide 48: Forwarding Conditions
EX hazard
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs))
  ForwardA = 10
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt))
  ForwardB = 10
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs))
  ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRt))
  ForwardB = 01

## Slide 49: Double Data Hazard
Consider the sequence:
  add $1,$1,$2
  add $1,$1,$3
  add $1,$1,$4
Both hazards occur
  Want to use the most recent
Revise MEM hazard condition
  Only forward if EX hazard condition is not true

## Slide 50: Revised Forwarding Conditions
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) and (MEM/WB.RegisterRd = ID/EX.RegisterRs))
  ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) and (MEM/WB.RegisterRd = ID/EX.RegisterRt))
  ForwardB = 01

## Slide 51: Datapath with Forwarding

## Slide 52: Load-Use Data Hazard
Need to stall for one cycle

## Slide 53: Load-Use Hazard Detection
Check when using instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs
  IF/ID.RegisterRt
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRt = IF/ID.RegisterRs) or (ID/EX.RegisterRt = IF/ID.RegisterRt))
If detected, stall and insert bubble

## Slide 54: How to Stall the Pipeline
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  Using instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for lw
    Can subsequently forward to EX stage

## Slide 55: Without Stalling

## Slide 56: Stall/Bubble in the Pipeline

## Slide 57: Datapath with Hazard Detection

## Slide 58: Stalls and Performance
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure

## Slide 59: Branch Hazards
If branch outcome determined in MEM
Flush these instructions (Set control values to 0)

## Slide 60: Control Hazards
When the flow of instruction addresses is not sequential (i.e., PC = PC + 4); incurred by change of flow instructions
  Unconditional branches (j, jal, jr)
  Conditional branches (beq, bne)
  Exceptions
Possible approaches
  Stall (impacts CPI)
  Move decision point as early in the pipeline as possible, thereby reducing the number of stall cycles
  Delay decision (requires compiler support)
  Predict and hope for the best!
Control hazards occur less frequently than data hazards, but there is nothing as effective against control hazards as forwarding is for data hazards

## Slide 61: Reducing Branch Delay
Move hardware to determine outcome to ID stage to reduce cost of the taken branch
  Target address adder
  Register comparator
Example: branch taken
36: sub $10, $4, $8 40: beq $1, $3, 7 44: and $12, $2, $5 48: or $13, $2, $6 52: add $14, $4, $2 56: slt $15, $6, $7 ... 72: lw $4, 50($7)

## Slide 62: Example - Branch Taken (1)

## Slide 63: Example - Branch Taken (2)

## Slide 64: Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction
  Branch prediction buffer (aka branch history table)
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 65: 1-Bit Predictor - Shortcoming
A 1-bit predictor will be incorrect twice when not taken
  Assume predict_bit = 0 to start (indicating branch not taken) and loop control is at the bottom of the loop code
  First time through the loop, the predictor mispredicts the branch since the branch is taken back to the top of the loop; invert prediction bit (predict_bit = 1)
  As long as branch is taken (looping), prediction is correct
  Exiting the loop, the predictor again mispredicts the branch since this time the branch is not taken falling out of the loop; invert prediction bit (predict_bit = 0)
For 10 times through the loop we have a 80% prediction accuracy for a branch that is taken 90% of the time

## Slide 66: 2-Bit Predictor
A 2-bit scheme can give 90% accuracy since a prediction must be wrong twice before the prediction bit is changed

## Slide 67: Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 68: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU
    e.g., undefined opcode, overflow, syscall, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard

## Slide 69: Handling Exceptions
In MIPS, exceptions managed by a System Control Coprocessor (CP0)
Save PC of offending (or interrupted) instruction
  In MIPS: Exception Program Counter (EPC)
Save indication of the problem
  In MIPS: Cause register
Jump to handler at 0x8000 0180

## Slide 70: Summary
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards
  Structural
    designing the pipeline correctly
  Data
    Stall (impacts CPI)
    Forward (requires hardware support)
  Control
    Stall (impacts CPI)
    Delay decision (requires compiler support)
    Static and dynamic prediction (requires hardware support)
Pipelining complicates exception handling