## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Outline
An overview of pipelining
A pipelined datapath
Pipelined control
Hazards: types of hazard
Handling data hazards
  Inserting NOP（software）
  Forwarding, R-Type-use（hardware)
  Stalls, load-use (hardware)
Handling branch hazards
Exceptions
Superscalar and dynamic pipelining

## Slide 3: Single-Cycle Advantages & Disadvantages
Uses the clock cycle inefficiently – the clock cycle must be timed to accommodate the slowest instruction
  Especially problematic for more complex instructions, e.g., floating-point multiplication
May be wasteful of area since some functional units (e.g., adders) must be duplicated since they can not be shared during a clock cycle
But it is simple and easy to understand
lw
sw
Cycle 1
waste
Cycle 2
Clk

## Slide 4: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
  4-load speedup = 8/3.5 = 2.3
  20-load speedup = 40/11.5 = 3.478
Under ideal conditions
  The speedup from pipelining ≈ The number of pipe stages

## Slide 5: Five Stages of Load Instruction
Five stages, one step per stage
IF: Instruction fetch from (instruction) memory
ID: Instruction decode & register read
EX: Execute operation or calculate address
MEM: Access (data) memory operand
WB: Write result back to register

## Slide 6: Single Cycle VS Pipeline
Clk
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Load
Pipeline Implementation
Clk
Single Cycle Implementation:
Load
Store
Waste
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Store
IF
ID
EX
MEM
WB
R-type
Cycle 1
Cycle 2
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.
In the multiple clock cycle implementation, however, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.
But may be more importantly, since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.
+2 = 77 min. (X:57)

## Slide 7: Pipeline Performance (1)
Assume time for stages is
  100 ns for register read or write
  200 ns for other stages
Compare pipelined datapath with single-cycle datapath
Instruction | IF | Reg Read | ALU Op | Mem Access | Reg Write | Total
lw | 200 | 100 | 200 | 200 | 100 | 800
sw | 200 | 100 | 200 | 200 |  | 700
R-format | 200 | 100 | 200 |  | 100 | 600
beq | 200 | 100 | 200 |  |  | 500

## Slide 8: Pipeline Performance (2)

## Slide 9: Pipeline Speedup
If all stages are balanced, i.e., all take the same time
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease
Time between instructionspipelined = | Time between instructionsnonpipelined
 | Number of pipeline stages

## Slide 10: Pipeline and ISA Design
MIPS ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in the 3rd stage, access memory in the 4th stage
  Alignment of memory operands
    Memory access takes only one cycle

## Slide 11: Pipeline Lessons
Does not help latency of single task, but throughput of entire
Pipeline rate limited by slowest stage
Multiple tasks working at the same time using different resources
Potential speedup = Number pipeline stages
Unbalanced stage length; time to “fill” & “drain” the pipeline reduce speedup
Stall for dependences

## Slide 12: Outline
An overview of pipelining
A pipelined datapath
Pipelined control
Hazards: types of hazard
Handling data hazards
  Inserting NOP（software）
  Forwarding, R-Type-use（hardware)
  Stalls, load-use (hardware)
Handling branch hazards
Exceptions
Superscalar and dynamic pipelining

## Slide 13: Design a Pipelined Processor
Examine the datapath and control diagram
  Starting with single cycle datapath
  Single cycle control?
Partition datapath into stages:
  IF (instruction fetch), ID (instruction decode and register file read), EX (execution or address calculation), MEM (data memory access), WB (write back)
Associate resources with stages
Ensure that flows do not conflict, or figure out how to resolve
Assert control in appropriate stage

## Slide 14: Multi-Execution Steps
But, use single-cycle datapath ...

## Slide 15: Split Single-cycle Datapath
What to add to split the datapath into stages?
Feedback
Path

## Slide 16: Add Pipeline Registers
Pipeline registers (latches)
Use registers between stages to carry data and control

## Slide 17: Consider load
IF: Instruction Fetch
  Fetch the instruction from the Instruction Memory
ID: Instruction Decode
  Registers fetch and instruction decode
EX: Calculate the memory address
MEM: Read the data from the Data Memory
WB: Write the data back to the register file
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Notes: As shown here, each of these five steps will take one clock cycle to complete.
And in pipeline terminology, each step is referred to as one stage of the pipeline.
+1 = 8 min. (X:48)

## Slide 18: Pipelining load
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Ifetch
Reg/Dec
Exec
Mem
Wr
1st lw
Ifetch
Reg/Dec
Exec
Mem
Wr
2nd lw
Ifetch
Reg/Dec
Exec
Mem
Wr
3rd lw
5 functional units in the pipeline datapath are
  Instruction Memory for the Ifetch stage
  Register File’s Read ports (busA and busB) for the Reg/Dec stage
  ALU for the Exec stage
  Data Memory for the MEM stage
  Register File’s Write port (busW) for the WB stage
Notes: For the load instructions, the five independent functional units in the pipeline datapath are:
(a) Instruction Memory for the Ifetch stage.
(b) Register File Read ports for the Reg/Decode stage.
(c) ALU for the Exec stage. (d) Data memory for the Mem stage.
(e) And finally Register File write port for the Write Back stage.
Notice that I have treat Register File read and write ports as separate functional units because the register file we have allows us to read and write at the same time.
Notice that as soon as the 1st load finishes its Ifetch stage, it no longer needs the Instruction Memory. Consequently, the 2nd load can start using the Instruction Memory (2nd Ifetch).
Furthermore, since each functional unit is only used ONCE per instruction, we will not have any conflict down the pipeline (Exec-Ifet, Mem-Exec, Wr-Mem) either.
I will show you the interaction between instructions in the pipelined datapath later. But for now, I want to point out the performance advantages of pipelining.
If these 3 load instructions are to be executed by the multiple cycle processor, it will take 15 cycles. But with pipelining, it only takes 7 cycles. This (7 cycles), however, is not the best way to look at the performance advantages of pipelining.
A better way to look at this is that we have one instruction enters the pipeline every cycle so we will have one instruction coming out of the pipeline (Wr stages) every cycle.
Consequently, the ffective?(or average) number of cycles per instruction is now ONE even though it takes a total of 5 cycles to complete each instruction.
+3 = 14 min. (X:54)

## Slide 19: IF Stage of load
IR = mem[PC]; PC = PC + 4
IR, PC+4

## Slide 20: ID Stage of load
A = Reg[IR[25-21]]; B = Reg[IR[20-16]];

## Slide 21: EX Stage of load
ALUout = A + sign-ext(IR[15-0])

## Slide 22: MEM State of load
MDR = mem[ALUout]

## Slide 23: WB Stage of load
Reg[IR[20-16]] = MDR
Who will supply this address?

## Slide 24: The Four Stages of R-type
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Ifetch
Reg/Dec
Exec
Wr
R-type
IF: fetch the instruction from the Instruction Memory
ID: registers fetch and instruction decode
EX: ALU operates on the two register operands
WB: write ALU output back to the register file
Notes: Well, so far so good. Let take a look at the R-type instructions.
The R-type instruction does NOT access data memory so it only takes four clock cycles, or in our new pipeline terminology, four stages to complete.
The Ifetch and Reg/Dec stages are identical to the Load instructions. Well they have to be because at this point, we do not know we have a R-type instruction yet.
Instead of calculating the effective address during the Exec stage, the R-type instruction will use the ALU to operate on the register operands.
The result of this ALU operation is written back to the register file during the Wr back stage.
+1 = 15 min. (55)

## Slide 25: Pipelining R-type and load
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type
Ops! We have a problem!
Notes: What happened if we try to pipeline the R-type instructions with the Load instructions?
Well, we have a problem here!!!
We end up having two instructions trying to write to the register file at the same time!
Why do we have this problem (the write ubble??
Well, the reason for this problem is that there is something I have not yet told you.
+1 = 16 min. (X:56)

## Slide 26: Important Observation
Each functional unit can only be used once per instruction
Each functional unit must be used at the same stage for all instructions
  Load uses Register File’s write port during its 5th stage
  R-type uses Register File’s write port during its 4th stage
Several ways to solve: forwarding, adding pipeline bubble, making instructions same length
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
1
2
3
4
5
Ifetch
Reg/Dec
Exec
Wr
R-type
1
2
3
4
Notes: I already told you that in order for pipeline to work perfectly, each functional unit can ONLY be used once per instruction.
What I have not told you is that this (1st bullet) is a necessary but NOT sufficient condition for pipeline to work.
The other condition to prevent pipeline hiccup is that each functional unit must be used at the same stage for all instructions.
For example here, the load instruction uses the Register File Wr port during its 5th stage but the R-type instruction right now will use the Register File port during its 4th stage.
This (5 versus 4) is what caused our problem. How do we solve it? We have 2 solutions.
+1 = 17 min. (X:57)

## Slide 27: Solution - Delay R-type’s Write
Delay R-type’s register write by one cycle
  R-type also use Reg File’s write port at Stage 5
  MEM is a NOP stage: nothing is being done.
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type
Mem
Exec
Exec
Exec
Exec
1
2
3
4
5
R-type also has 5 stages
Notes: Well one thing we can do is to add a op?stage to the R-type instruction pipeline to delay its register file write by one cycle.
Now the R-type instruction ALSO uses the register file witer port at its 5th stage so we eliminate the write conflict with the load instruction.
This is a much simpler solution as far as the control logic is concerned. As far as performance is concerned, we also gets back to having one instruction completes per cycle.
This is kind of like promoting socialism: by making each individual R-type instruction takes 5 cycles instead of 4 cycles to finish, our overall performance is actually better off.
The reason for this higher performance is that we end up having a more efficient pipeline.
+1 = 20 min. (Y:00)

## Slide 28: The Four Stages of store
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Ifetch
Reg/Dec
Exec
Mem
Store
WB
IF: fetch the instruction from the Instruction Memory
ID: registers fetch and instruction decode
EX: calculate the memory address
MEM: write the data into the Data Memory
Add an extra stage:
WB: NOP
Notes: Let continue our lecture by looking at the store instruction.
Once again, the Ifetch and Reg/Decode stages are the same as all other instructions.
The Exec stage of the store instruction calculates the memory address.
Once the address is calculated, the store instruction will write the data it read from the register file back at the Reg/Decode stage into the data memory during the Mem stage.
Notice that unlike the load instruction which takes five cycles to accomplish its task, the Store instruction only takes four cycles or four pipe stages.
In order to keep our pipeline diagram looks more uniform, however, we will keep the Wr stage for the store instruction in the pipeline diagram.
But keep in mind that as far as the pipelined control and pipelined datapath are concerned, the store instruction requires NOTHING to be done once it finishes its Mem stage.
+2 = 27 min. (Y:07)

## Slide 29: The Three Stages of beq
IF: fetch the instruction from the Instruction Memory
ID: registers fetch and instruction decode
EX:
  Compares the two register operand
  Select correct branch target address
  Latch into PC
Add two extra stages:
MEM: NOP
WB: NOP
Beq
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Ifetch
Reg/Dec
Exec
Mem
WB
Notes: Well similar to the store instruction, the branch instruction only consists of four pipe stages.
Ifetch and Reg/decode are the same as all other instructions because we do not know what instruction we have at this point. We have not finish decoding the instruction yet.
During the Execute stage of the pipeline, the BEQ instruction will use the ALU to compare the two register operands it fetched during the Reg/Dec stage.
At the same time, a separate adder is used to calculate the branch target address.
If the registers we compared during the Execute stage (point to the last bullet) have the same value, the branch is taken.
That is, the branch target address we calculated earlier (last bullet) will be written into the Program Counter.
Once again, similar to the Store instruction, the BEQ instruction will require NEITHER the pipelined control nor the pipelined datapath to do ANY thing once it finishes its Mem stage.
With all these talk about pipelined datapath and pipelined control, let take a look at how the pipelined datapath looks like.
+2 = 29 min. (Y:09)

## Slide 30: Graphically Representing Pipelines
Can help with answering questions like
  How many cycles to execute this code?
  What is the ALU doing during cycle 4?
  Help understand datapaths

## Slide 31: Example 1 - Cycle 1

## Slide 32: Example 1 - Cycle 2

## Slide 33: Example 1 - Cycle 3

## Slide 34: Example 1 - Cycle 4

## Slide 35: Example 1 - Cycle 5

## Slide 36: Example 1 - Cycle 6

## Slide 37: Outline
An overview of pipelining
A pipelined datapath
Pipelined control
Hazards: types of hazard
Handling data hazards
  Inserting NOP（software）
  Forwarding, R-Type-use（hardware)
  Stalls, load-use (hardware)
Handling branch hazards
Exceptions
Superscalar and dynamic pipelining

## Slide 38: Pipeline Control - Control Signals

## Slide 39: Group Signals According to Stages
Can use control signals of single-cycle CPU

## Slide 40: Data Stationary Control (1)
Pass control signals along just like the data
  Main control generates control signals during ID

## Slide 41: Data Stationary Control (2)
IF/ID Register
ID/Ex Register
Ex/MEM Register
MEM/WB Register
ID
EX
MEM
ExtOp
ALUOp
RegDst
ALUSrc
Branch
MemWr
MemtoReg
RegWr
Main
Control
ExtOp
ALUOp
RegDst
ALUSrc
MemtoReg
RegWr
MemtoReg
RegWr
MemtoReg
RegWr
Branch
MemWr
Branch
MemW
WB
Signals for EX (ExtOp, ALUSrc, ...) are used 1 cycle later
Signals for MEM (MemWr, Branch) are used 2 cycles later
Signals for WB (MemtoReg, MemWr) are used 3 cycles later
Notes: The main control here is identical to the one in the single cycle processor. It generate all the control signals necessary for a given instruction during that instruction Reg/Decode stage.
All these control signals will be saved in the ID/Exec pipeline register at the end of the Reg/Decode cycle.
The control signals for the Exec stage (ALUSrc, ... etc.) come from the output of the ID/Exec register. That is they are delayed ONE cycle from the cycle they are generated.
The rest of the control signals that are not used during the Exec stage is passed down the pipeline and saved in the Exec/Mem register.
The control signals for the Mem stage (MemWr, Branch) come from the output of the Exec/Mem register. That is they are delayed two cycles from the cycle they are generated.
Finally, the control signals for the Wr stage (MemtoReg & RegWr) come from the output of the Exec/Wr register: they are delayed three cycles from the cycle they are generated.
+2 = 45 min. (Y:45)

## Slide 42: WB Stage of load
Reg[IR[20-16]] = MDR
Who will supply this address?

## Slide 43: Datapath with Control

## Slide 44: Let’s Try it Out
lw $10, 20($1)
sub $11, $2, $3
and $12, $4, $5
or $13, $6, $7
add $14, $8, $9

## Slide 45: Example 2 - Cycle 1

## Slide 46: Example 2 - Cycle 2

## Slide 47: Example 2 - Cycle 3

## Slide 48: Example 2 - Cycle 4

## Slide 49: Example 2 - Cycle 5

## Slide 50: Example 2 - Cycle 6

## Slide 51: Example 2 - Cycle 7
Fig. 6.34

## Slide 52: Example 2 - Cycle 8

## Slide 53: Example 2 - Cycle 9

## Slide 54: Summary of Pipeline Basics
Pipelining is a fundamental concept
  Multiple steps using distinct resources
  Utilize capabilities of datapath by pipelined instruction processing
    Start next instruction while working on the current one
    Limited by length of longest stage (plus fill/flush)
    Need to detect and resolve hazards
What makes it easy in MIPS?
  All instructions are of the same length
  Just a few instruction formats
  Memory operands only in loads and stores
What makes pipelining hard? hazards

## Slide 55: Outline
An overview of pipelining
A pipelined datapath
Pipelined control
Hazards: types of hazard
Handling data hazards
  Inserting NOP（software）
  Forwarding, R-Type-use（hardware)
  Stalls, load-use (hardware)
Handling branch hazards
Exceptions
Superscalar and dynamic pipelining

## Slide 56: Pipeline Hazards
Situations that prevent starting the next instruction in the next cycle
  Structure hazards
    A required resource is busy
  Data hazard
    Need to wait for previous instruction to complete its data read/write
  Control hazard
    The decision on control action depends on previous instruction
    Branch instructions
Can always resolve hazards by waiting
  Pipeline control must detect the hazard
  Take action (or delay action) to resolve hazards

## Slide 57: Structure Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 58: Structural Hazard - Single Memory (1)
Mem
I
n
s
t
r.
O
r
d
e
r
Time
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg

## Slide 59: Structural Hazard - Single Memory (2)
Mem
I
n
s
t
r.
O
r
d
e
r
Time
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Use 2 memory: data memory and instruction memory

## Slide 60: Data Hazards (1)
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3
We may need to insert a pipeline stall (or bubble)

## Slide 61: Data Hazards (2)
I
M
R
e
g
I
M
R
e
g
C
C
1
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
s
u
b
$
2
,
$
1
,
$
3
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
a
n
d
$
1
2
,
$
2
,
$
5
I
M
R
e
g
D
M
R
e
g
I
M
D
M
R
e
g
I
M
D
M
R
e
g
C
C
7
C
C
8
C
C
9
1
0
1
0
1
0
1
0
1
0
/
-2
0
-20
-2
0
-2
0
-2
0
o
r
$
1
3
,
$
6
,
$
2
a
d
d
$
1
4
,
$
2
,
$
2
s
w
$
1
5
,
1
0
0
(
$
2
)
V
a
l
u
e
o
f
r
e
g
i
s
t
e
r
$
2
:
D
M
R
e
g
R
e
g
R
e
g
R
e
g
D
M

## Slide 62: Types of Data Hazards
RAW (read after write) - i2 tries to read operand before i1 writes it
WAR (write after read) - i2 tries to write operand before i1 reads it
  Can not happen in MIPS 5-stage pipeline because
    All instructions take 5 stages, and reads are always in stage 2, and writes are always in stage 5
WAW (write after write) - i2 tries to write operand before i1 writes it
  Leaves wrong result ( i1’s not i2’s); occur only in pipelines that write in more than one stage
  Can not happen in MIPS 5-stage pipeline because
    All instructions take 5 stages, and writes are always in stage 5

## Slide 63: Pipeline Data Hazards Illustrated
IF ID EX MEM WB
IF ID EX Mem
RAW (read after write) Data Hazard
WAW Data Hazard (write after write)
IF ID EX MEM WB
WAR Data Hazard (write after read)
IF ID EX MEM WB
IF ID EX MEM WB
time

## Slide 64: Outline
An overview of pipelining
A pipelined datapath
Pipelined control
Hazards: types of hazard
Handling data hazards
  Inserting NOP（software）
  Forwarding, R-Type-use (hardware)
  Stalls, load-use (hardware)
Handling branch hazards
Exceptions
Superscalar and dynamic pipelining

## Slide 65: Handling Data Hazards
Use simple, fixed design
  Eliminate WAR by always fetching operands early (ID) in pipeline
  Eliminate WAW by doing all write backs in order (last stage, static)
  These features have a lot to do with ISA design
Internal forwarding in register file
  Write in first half of clock and read in second half
  Read delivers what is written, resolve hazard between sub and add
Detect and resolve remaining ones
  Compiler inserts NOP (software solution)
  Forward (hardware solution)
  Stall (hardware solution)

## Slide 66: Software Solution
Have compiler guarantee no hazards
Where do we insert the NOPs sub $2, $1, $3 and $12, $2, $5 or $13, $6, $2 add $14, $2, $2 sw $15, 100($2)
Problem: this really slows us down

## Slide 67: Data Hazards
I
M
R
e
g
I
M
R
e
g
C
C
1
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
s
u
b
$
2
,
$
1
,
$
3
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
a
n
d
$
1
2
,
$
2
,
$
5
C
C
7
C
C
8
C
C
9
0
V
a
l
u
e
o
f
I
M
R
e
g
D
M
R
e
g
I
M
D
M
R
e
g
I
M
D
M
R
e
g
1
0
1
0
1
0
1
0
1
0
/
-2
0
-20
-2
0
-2
0
-2
o
r
$
1
3
,
$
6
,
$
2
a
d
d
$
1
4
,
$
2
,
$
2
s
w
$
1
5
,
1
0
0
(
$
2
)
r
e
g
i
s
t
e
r
$
2
:
D
M
R
e
g
R
e
g
R
e
g
R
e
g
D
M
Insert two nops

## Slide 68: Outline
An overview of pipelining
A pipelined datapath
Pipelined control
Hazards: types of hazard
Handling data hazards
  Inserting NOP（software）
  Forwarding, R-Type-use（hardware)
  Stalls, load-use (hardware)
Handling branch hazards
Exceptions
Superscalar and dynamic pipelining

## Slide 69: Resolve Data Hazards - Forwarding
Use result when it is computed
  Do not wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 70: Detect Data Hazards (1)
Hazard conditions
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRt
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRt
Two optimizations
  Do not forward if instruction does not write register => check if RegWrite is asserted
  Do not forward if destination register is $0 => check if RegisterRd = 0
Forward from EX/MEM pipeline registers
Forward from MEM/WB pipeline registers

## Slide 71: Detect Data Hazards (2)
Hazard conditions using control signals
  At EX stage EX/MEM.RegWrite and (EX/MEM.RegRd0) and (EX/MEM.RegRd=ID/EX.RegRs)
  At MEM stage MEM/WB.RegWrite and (MEM/WB.RegRd0) and (MEM/WB.RegRd=ID/EX.RegRs)
  (replace ID/EX.RegRt for ID/EX.RegRs for the other two conditions)

## Slide 72: Datapath with Forwarding (MEM and WB Stages Forwards)

## Slide 73: Forwarding Logic
Forwarding: input to ALU from any pipe register
  Add multiplexors to ALU input 
  Control forwarding in EX => carry Rs in ID/EX
Control signals for forwarding
  If both WB and MEM forward, e.g., add $1,$1,$2; add $1,$1,$3; add $1,$1,$4; => let MEM forward
  EX hazard
    if (EX/MEM.RegWrite and (EX/MEM.RegRd0) and (EX/MEM.RegRd=ID/EX.RegRs)) ForwardA=10
  MEM hazard
    if (MEM/WB.RegWrite and (MEM/WB.RegRd0) and (EX/MEM.RegRd  ID/EX.Reg.Rs) and (MEM/WB.RegRd=ID/EX.RegRs)) ForwardA=01

## Slide 74: Example 3 - Cycle 3

## Slide 75: Example 3 - Cycle 4

## Slide 76
Example 3 - Cycle 5

## Slide 77: Example 3 - Cycle 6
Fig. 6.42

## Slide 78: Outline
An overview of pipelining
A pipelined datapath
Pipelined control
Hazards: types of hazard
Handling data hazards
  Inserting NOP（software）
  Forwarding, R-Type-use（hardware)
  Stalls, load-use (hardware)
Handling branch hazards
Exceptions
Superscalar and dynamic pipelining

## Slide 79: Cannot Always Forwarding
lw can still cause a hazard
  if is followed by an instruction to read the loaded register
Use stalling or compiler to resolve

## Slide 80: Stalling
Stall pipeline by keeping instructions in same stage and inserting an NOP instead

## Slide 81: Datapath with Stalling Unit
Forwarding controls ALU inputs, hazard detection controls PC, IF/ID, control signals

## Slide 82: Control - Handling Stalls
Hazard detection unit in ID to insert stall between a load instruction and its use if (ID/EX.MemRead and ((ID/EX.RegisterRt = IF/ID.RegisterRs) or (ID/EX.RegisterRt = IF/ID.registerRt)) stall the pipeline for one cycle (ID/EX.MemRead=1 indicates a load instruction)
How to stall?
  Stall instruction in IF and ID: not change PC and IF/ID => the stages re-execute the instructions
  What to move into EX: insert an NOP by changing EX, MEM, WB control fields of ID/EX pipeline register to 0
    All control signals to EX, MEM, WB are deasserted and no registers or memories are written

## Slide 83: Example 4 - Cycle 2

## Slide 84: Example 4 - Cycle 3

## Slide 85: Example 4 - Cycle 4

## Slide 86: Example 4 - Cycle 5

## Slide 87: Example 4 - Cycle 6

## Slide 88: Example 4 - Cycle 7

## Slide 89: Outline
An overview of pipelining
A pipelined datapath
Pipelined control
Hazards: types of hazard
Handling data hazards
  Inserting NOP（software）
  Forwarding, R-Type-use（hardware)
  Stalls, load-use (hardware)
Handling branch hazards
Exceptions
Superscalar and dynamic pipelining

## Slide 90: Pipeline Datapath with Control Signals

## Slide 91: Branch Hazards
When decide to branch, other inst. are in pipeline!

## Slide 92: Handle Branch Hazard
Predict branch always not taken
  Need to add hardware for flushing instruction if wrong
  Branch decision made at MEM => need to flush instruction in IF/ID, ID/EX by changing control values to 0
Reduce delay of taken branch by moving branch execution earlier in the pipeline
  Move up branch address calculation to ID
  Check branch equality at ID (using XOR) by comparing the two registers read during ID
  Branch decision made at ID => one instruction to flush
  Add a control signal, IF.Flush, to zero instruction field of IF/ID => making the instruction an NOP
Dynamic branch prediction
Compiler rescheduling, delay branch

## Slide 93: Pipeline with Flushing

## Slide 94: Example 5 - Cycle 3

## Slide 95: Example 5 - Cycle 4

## Slide 96: Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction (e.g. loop)
  Branch prediction buffer (i.e., branch history table)
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 97: Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 98: Delayed Branch
Predict-not-taken + branch decision at ID => the following instruction is always executed => branches take effect 1 cycle later
0 clock cycle penalty per branch instruction if can find instruction to put in slot (50% of time)
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
add
beq
misc
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Mem
ALU
Reg
Mem
Reg
lw
Mem
ALU
Reg
Mem
Reg

## Slide 99: Outline
An overview of pipelining
A pipelined datapath
Pipelined control
Hazards: types of hazard
Handling data hazards
  Inserting NOP（software）
  Forwarding, R-Type-use（hardware)
  Stalls, load-use (hardware)
Handling branch hazards
Exceptions
Superscalar and dynamic pipelining

## Slide 100: Exceptions and Interrupts
Unexpected events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU
  e.g., undefined opcode, overflow, syscall, …
Interrupt
  From an external I/O controller
In MIPS, exceptions managed by a System Control Coprocessor (CP0)
Dealing with them without sacrificing performance is hard

## Slide 101: Handling Exceptions
Before jump to OS
Save PC of offending (or interrupted) instruction
  In MIPS: Exception Program Counter (EPC)
Save indication of the problem
  In MIPS: Cause register
  We will assume 1-bit
    0 for undefined opcode, 1 for overflow
Jump to handler at 8000 00180

## Slide 102: An Alternate Mechanism
Vectored Interrupts
  Handler address determined by the cause
Example:
  Undefined opcode: C000 0000
  Overflow: C000 0020
  …: C000 0040
Instructions either
  Deal with the interrupt, or
  Jump to real handler

## Slide 103: Handler Actions
In OS
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  Use EPC to return to program
Otherwise
  Terminate program
  Report error using EPC, cause, …

## Slide 104: Exceptions in a Pipeline
Another form of control hazard
Consider overflow on add in EX stage
  add $1, $2, $1
  Prevent $1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Set Cause and EPC register values
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware

## Slide 105: Pipeline with Exceptions

## Slide 106: Exception Example (1)
Exception on add in
  40 sub $11, $2, $4 44 and $12, $2, $5 48 or $13, $2, $6 4C add $1, $2, $1 50 slt $15, $6, $7 54 lw $16, 50($7) …
Handler
  80000180 sw $25, 1000($0) 80000184 sw $26, 1004($0) …

## Slide 107: Exception Example (2)

## Slide 108: Exception Example（3）

## Slide 109: Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once
Simple approach: deal with exception from the earliest instruction
  Flush subsequent instructions
  “Precise” exceptions
In complex pipelines
  Multiple instructions issued per cycle
  Out-of-order completion
  Maintaining precise exceptions is difficult!

## Slide 110: Imprecise Exceptions
Just stop pipeline and save state
  Including exception cause(s)
Let the handler work out
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion
Simplifies hardware, but more complex handler software
Feasible for complex multiple-issue out-of-order pipelines

## Slide 111: Outline
An overview of pipelining
A pipelined datapath
Pipelined control
Hazards: types of hazard
Handling data hazards
  Inserting NOP（software）
  Forwarding, R-Type-use（hardware)
  Stalls, load-use (hardware)
Handling branch hazards
Exceptions
Superscalar and dynamic pipelining

## Slide 112: Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
    Clock cycle Per Instruction (CPI) < 1, so use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue (Assume 1 instruction completed in 1 cycle)
      16 billion instruction per second (BIPS), peak CPI = 0.25, peak IPC = 4
      But dependencies reduce this in practice

## Slide 113: Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 114: Speculation
Guess what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load
    A store that proceeds a load does not refer to the same address (load first)
    Roll back if location is updated

## Slide 115: Compiler/Hardware Speculation
Compiler can reorder instructions
  e.g., move load before store
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until determining they are actually needed
  Flush buffers on incorrect speculation

## Slide 116: Multiple Issue
Static multiple issue (compiler approach)
Dynamic multiple issue (hardware approach)

## Slide 117: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)

## Slide 118: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary

## Slide 119: MIPS with Static Dual Issue (1)
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 120: MIPS with Static Dual Issue (2)
Notes: Hardware required: (beyond hazard detection)
Register file with 4 read ports and two write ports (one r-type and one load instructions)
One more ALU to compute load/store address

## Slide 121: Hazards in the Dual-Issue MIPS
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add $t0, $s0, $s1 load $s2, 0($t0)
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required

## Slide 122: Scheduling Example
Schedule this for dual-issue MIPS
Loop: lw $t0, 0($s1) # $t0=array element addu $t0, $t0, $s2 # add scalar in $s2 sw $t0, 4($s1) # store result addi $s1, $s1,–4 # decrement pointer bne $s1, $zero, Loop # branch $s1!=0
 | ALU/branch | Load/store | cycle
Loop: | nop | lw $t0, 0($s1) | 1
 | addi $s1, $s1,–4 | nop | 2
 | addu $t0, $t0, $s2 | nop | 3
 | bne $s1, $zero, Loop | sw $t0, 4($s1) | 4
  IPC = 5/4 = 1.25 (c.f. peak IPC = 2)

## Slide 123: Loop Unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Called “register renaming”
  Avoid loop-carried “anti-dependencies”
    Store followed by a load of the same register (the value in the register is differrent)
    Aka “name dependence”
      Reuse of a register name

## Slide 124: Scheduling Example
Schedule this for dual-issue MIPS
Loop: lw $t0, 0($s1) # $t0=array element addu $t0, $t0, $s2 # add scalar in $s2 sw $t0, 4($s1) # store result addi $s1, $s1,–4 # decrement pointer bne $s1, $zero, Loop # branch $s1!=0
Replicate loop body 4 times to expose more parallelism

## Slide 125: Unrolling Two Iterations
Schedule this for dual-issue MIPS
Loop: lw $t0, 0($s1) # $t0=array element addu $t0, $t0, $s2 # add scalar in $s2 sw $t0, 4($s1) # store result addi $s1, $s1,–4 # decrement pointer bne $s1, $zero, Loop # branch $s1!=0
lw $t0, 0($s1) # $t0=array element addu $t0, $t0, $s2 # add scalar in $s2 sw $t0, 4($s1) # store result addi $s1, $s1,–4 # decrement pointer bne $s1, $zero, Loop # branch $s1!=0

## Slide 126: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at cost of registers and code size
 | ALU/branch | Load/store | cycle
Loop: | addi $s1, $s1,–16 | lw $t0, 0($s1) | 1
 | nop | lw $t1, 4($s1) | 2
 | addu $t0, $t0, $s2 | lw $t2, 8($s1) | 3
 | addu $t1, $t1, $s2 | lw $t3, 12($s1) | 4
 | addu $t2, $t2, $s2 | sw $t0, 4($s1) | 5
 | addu $t3, $t4, $s2 | sw $t1, 8($s1) | 6
 | nop | sw $t2, 12($s1) | 7
 | bne $s1, $zero, Loop | sw $t3, 16($s1) | 8

## Slide 127: Multiple Issue
Static multiple issue (compiler approach)
Dynamic multiple issue (hardware approach)

## Slide 128: Dynamic Multiple Issue
Simplest version of “Superscalar”processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoid the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 129: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s4, $s4, $t3 slti $t5, $s4, 20
  Can start sub while addu is waiting for lw

## Slide 130: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 131: Speculation
Predict branch and continue issuing
  Do not commit until branch outcome determined
Load speculation
  Avoid load and cache miss delay
    Predict the effective address
    Predict loaded value
    Load before completing outstanding stores
    Bypass stored values to load unit
  Do not commit load until speculation cleared

## Slide 132: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
  Not all stalls are predicable
    e.g., cache misses
  Can not always schedule around branches
    Branch outcome is dynamically determined
  Different implementations of an ISA have different latencies and hazards

## Slide 133: Does Multiple Issue Work?
Yes, but not as much as we would like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well

## Slide 134: Power Efficiency
Complexity of dynamic scheduling and speculations requires power
Multiple simpler cores may be better
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
UltraSparc T1 | 2005 | 1200MHz | 6 | 1 | No | 8 | 70W

## Slide 135: Fallacies
Pipelining is easy
  The basic idea is easy
  The devil is in the details
    e.g., detecting data hazards
Pipelining is independent of technology
  So why haven’t we always done pipelining?
  More transistors make more advanced techniques feasible
  Pipeline-related ISA design needs to take the technology trends into account
    e.g., predicted instructions

## Slide 136: Pitfalls
Poor ISA design can make pipelining harder
  e.g., complex instruction sets (VAX, IA-32)
    Significant overhead to make pipelining work
    IA-32 micro-op approach
  e.g., complex addressing modes
    Register update side effects, memory indirection
  e.g., delayed branches
    Advanced pipelines have long delay slots

## Slide 137: Concluding Remarks
ISA influences design of datapath and control
Datapath and control influence the design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Multiple issue and dynamic scheduling (ILP)
  Dependencies limit achievable parallelism
  Complexity leads to the power wall