## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $500 – $1000 per GB (2012)
Dynamic RAM (DRAM)
  50ns – 70ns, $10 – $20 per GB (2012)
Flash Memory
  5µs – 50µs, $0.75 – $1.00 per GB (2012)
Magnetic disk
  5ms – 20ms, $0.05 – $0.10 per GB (2012)
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk

## Slide 3: SRAM vs. DRAM
DRAM
SRAM

## Slide 4: A Typical Memory Hierarchy
Take advantage of the principle of locality to present the user with as much memory as is available in the cheapest technology at the speed offered by the fastest technology

## Slide 5: Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  e.g., sequential instruction access, array data

## Slide 6: Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU

## Slide 7: Memory Hierarchy Levels
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
  Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
  Miss penalty: extra time taken
  Miss ratio: misses/accesses = (1 – hit ratio)
Then accessed data supplied from upper level
Hit time << Miss penalty

## Slide 8: Cache Memory
The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
How do we know if the data is present?
Where do we look?

## Slide 9: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits

## Slide 10: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 11: Cache Example (1)
8-blocks, 1 word/block, direct mapped
Initial state of cache
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 12: Cache Example (2)
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Memory[101102]
111 | N |  | 
Address (decimal) | Address (binary) | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 13: Cache Example (3)
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Memory[110102]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Memory[101102]
111 | N |  | 
Address (decimal) | Address (binary) | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 14: Cache Example (4)
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Memory[110102]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Memory[101102]
111 | N |  | 
Address (decimal) | Address (binary) | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 15: Cache Example (5)
Index | V | Tag | Data
000 | Y | 10 | Memory[100002]
001 | N |  | 
010 | Y | 11 | Memory[110102]
011 | Y | 00 | Memory[000112]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Memory[101102]
111 | N |  | 
Address (decimal) | Address (binary) | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 16: Cache Example (6)
Index | V | Tag | Data
000 | Y | 10 | Memory[100002]
001 | N |  | 
010 | Y | 10 | Memory[100102]
011 | Y | 00 | Memory[000112]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Memory[101102]
111 | N |  | 
Address (decimal) | Address (binary) | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 17: Address Subdivision

## Slide 18: Example: Larger Block Size
64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address = [1200/16] = 75
Block number = 75 modulo 64 = 11
  This block maps all addresses between 1200 and 1215
Tag
Index
Offset
31 10 9 4 3 0
22 bits
6 bits
4 bits

## Slide 19: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
  Larger blocks  spatial locality decreases
Larger miss penalty
  Can override benefit of reduced miss rate
  Early restart and critical-word-first can help

## Slide 20: Miss Rate vs. Block Size vs. Cache Size
Miss rate goes up if the block size becomes a significant fraction of the cache size because the number of blocks that can be held in the same size cache is smaller (increasing capacity misses)

## Slide 21: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 22: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write-through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 23: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 24: Write Allocation
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: write allocate
  Don’t update cache: no write allocate
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually write allocate, but need to check if the block being replaced is dirty or not (and write-back if dirty).

## Slide 25: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
With simplifying assumptions:

## Slide 26: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
Miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 = 2.72 times faster

## Slide 27: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    In average 2 cycles per instruction

## Slide 28: Performance Summary
When CPU performance increased
  Miss penalty becomes more significant
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
Can not neglect cache behavior when evaluating system performance

## Slide 29: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)

## Slide 30: Associative Cache Example

## Slide 31: Spectrum of Associativity
For a cache with 8 entries

## Slide 32: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped

## Slide 33: Associativity Example
2-way set associative
Fully associative

## Slide 34: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 35: Set Associative Cache Organization

## Slide 36: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 37: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 38: Multilevel Cache Example (1)
Given
  CPU base CPI = 1, clock rate = 4GHz (1 cycle = 0.25ns)
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 39: Multilevel Cache Example (2)
Now add L-2 cache
  Access time = 5ns
  Miss rate/instruction = 2% (same)
  Global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  Penalty = 5ns/0.25ns = 20 cycles
Primary miss with L-2 miss
  Extra penalty = 400 + 20 cycles
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6

## Slide 40: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single cache
  L-1 block size smaller than L-2 block size

## Slide 41: Interactions with Advanced CPUs
Out-of-order CPUs can execute instructions during cache miss
  Pending store stays in load/store unit
  Dependent instructions wait in reservation stations
  Independent instructions continue
Effect of miss depends on program data flow
  Much harder to analyze
  Use system simulation