## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache

## Slide 3: Memory Technology
Random access
  Access time same for all locations
  SRAM (Static Random Access Memory)
    Low density, high power, expensive, fast
    Static: content will last forever until lose power
    Address not divided
    Use for caches
  DRAM (Dynamic Random Access Memory)
    High density, low power, cheap, slow
    Dynamic: need to be refreshed regularly
    Addresses in 2 halves (memory as a 2D matrix)
      RAS/CAS (Row/Column Access Strobe)
    Use for main memory
Magnetic disk
Notes: The technology we used to build our memory hierarchy can be divided into two categories: Random Access and Non-so-Random Access.
Unlike all other aspects of life where the word random usually associates with bad things, random, when associates with memory access, for the lack of a better word, is good!
Because random access means you can access any random location at any time and the access time will be the same as any other random locations.
Which is NOT the case for disks or tape where the access time for a given location at any time can be quite different from some other random locations at some other random time.
As far as Random Access technology is concerned, we will concentrate on two specific technologies: Dynamic RAM and Static RAM.
The advantages of Dynamic RAMs are high density, low cost, and low power so we can have a lot of them without burning a hole in our budget or our desktop.
The disadvantages of DRAM are they are slow. Also they will forget what you tell them if you don remind them constantly (Refresh). We will talk more about refresh later today.
SRAM only has one redeeming feature: it is fast. Other than that, they have low density, expensive, and burn a lot of power. Oh, SRAM actually has another redeeming feature. They will not forget what you tell them. They will keep whatever you write to them forever.
Well orever?is a long time. So lets just say it will keep your data as long as you don pull the plug on your computer.
In the next two lectures, we will be focusing on DRAMs and SRAMs.
We will not get into disk until the Virtual Memory lecture a week from now.
+3 = 19 min. (X:59)

## Slide 4: Comparisons of Various Technologies
Memory
technology
$ per GB
in 2008
SRAM
$2000 – $5,000
DRAM
Magnetic
disk
$0.20 – $2
Typical access
time
0.5 – 2.5 ns
50 – 70 ns
5,000,000 –
20,000,000 ns
$20 – $75
Idea memory
  Access time of DRAM
  Capacity and cost/GB
Notes: From the truth table we had before the break, we can derive the logic equation for ALUctr bit 2 but collecting all the rows that has ALUCtr bit 2 equals to 1 and this table is the result.
Each row becomes a product term and we need to OR the prodcut terms together.
Notice that the last row are identical except the bit<3> of the func fields. One is zero and the other is one. Together, they make bit<3> a don care term.
With all these don care terms, the logic equation is rather simple.
The first prodcut term is: not ALUOp<2> and ALUOp<0>.
The second product term, after we making Func<3> a don care becomes ...
+2 = 57 min. (Y:37)

## Slide 5: Solution - Memory Hierarchy
Control
Datapath
Memory
Processor
Memory
Memory
Memory
Memory
Fastest
Slowest
Smallest
Biggest
Highest
Lowest
Speed:
Size:
Cost:
An Illusion of a large, fast, cheap memory
  Fact: Large memories slow, fast memories small
  How to achieve: hierarchy, parallelism
An expanded view of memory system

## Slide 6: Memory Hierarchy - Principle
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Block X
Block Y
At any given time, data is copied between only two adjacent levels
  Upper level: The one closer to the processor
    Smaller, faster, uses more expensive technology
  Lower level: The one away from the processor
    Bigger, slower, uses less expensive technology
Block: Basic unit of information transfer
  Minimum unit of information that can either be present or not present in a level of the hierarchy

## Slide 7: Why Hierarchy Works
Principle of Locality
  Program access a relatively small portion of the address space at any instant of time
  90-10 rule: 10% of code executed 90% of time
Two types of locality
  Temporal locality: If an item is referenced, it will tend to be referenced again soon, e.g., loop
  Spatial locality: If an item is referenced, items whose addresses are close by tend to be referenced soon., e.g., instruction access, array data structure
Probability
of reference
address space
0
2n - 1
Notes: The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
This is kind of like in real life, we all have a lot of friends. But at any given time most of us can only keep in touch with a small group of them.
There are two different types of locality: Temporal and Spatial. Temporal locality is the locality in time which says if an item is referenced, it will tend to be referenced again soon.
This is like saying if you just talk to one of your friends, it is likely that you will talk to him or her again soon.
This makes sense. For example, if you just have lunch with a friend, you may say, let go to the ball game this Sunday. So you will talk to him again soon.
Spatial locality is the locality in space. It says if an item is referenced, items whose addresses are close by tend to be referenced soon.
Once again, using our analogy. We can usually divide our friends into groups. Like friends from high school, friends from work, friends from home.
Let say you just talk to one of your friends from high school and she may say something like: o did you hear so and so just won the lottery.
You probably will say NO, I better give him a call and find out more.
So this is an example of spatial locality. You just talked to a friend from your high school days. As a result, you end up talking to another high school friend. Or at least in this case, you hope he still remember you are his friend.
+3 = 10 min. (X:50)
Temporal locality: loop
Spatial locality: instruction executed sequentially, access of array element.

## Slide 8: Levels of Memory Hierarchy
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Transfer Unit
prog./compiler
cache controller
OS
user/operator
Upper Level
Lower Level
faster
Larger

## Slide 9: How Is the Hierarchy Managed
Registers <-> Memory
  By compiler (programmer?)
Cache <-> Memory
  By the hardware
Memory <-> Disks
  By the hardware and operating system (virtual memory)
  By the programmer (files)

## Slide 10: Memory Hierarchy - Terminology
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Block X
Block Y
Hit: Data appears in upper level (Block X)
  Hit rate: Fraction of memory access found in the upper level
  Hit time: Time to access the upper level
    RAM access time + Time to determine hit/miss
Miss: Data needs to be retrieved from a block in the lower level (Block Y)
  Miss Rate = 1 - (Hit Rate)
  Miss Penalty: Time to replace a block in the upper level + time to deliver the block to the processor (latency + transmit time)
Hit Time << Miss Penalty
Notes: A HIT is when the data the processor wants to access is found in the upper level (Blk X).
The fraction of the memory access that are HIT is defined as HIT rate.
HIT Time is the time to access the Upper Level where the data is found (X). It consists of:
(a) Time to access this level.
(b) AND the time to determine if this is a Hit or Miss.
If the data the processor wants cannot be found in the Upper level. Then we have a miss and we need to retrieve the data (Blk Y) from the lower level.
By definition (definition of Hit: Fraction), the miss rate is just 1 minus the hit rate.
This miss penalty also consists of two parts:
(a) The time it takes to replace a block (Blk Y to BlkX) in the upper level.
(b) And then the time it takes to deliver this new block to the processor.
It is very important that your Hit Time to be much much smaller than your miss penalty. Otherwise, there will be no reason to build a memory hierarchy.
+2 = 14 min. (X:54)

## Slide 11: Four Questions for Hierarchy Design
Q1: Where can a block be placed in the upper level? => Block placement
Q2: How is a block found if it is in the upper level? => Block finding
Q3: Which block should be replaced on a miss? => Block replacement
Q4: What happens on a write? => Write strategy

## Slide 12: Summary of Memory Hierarchy
DRAM is slow but cheap and dense
  Good for presenting users with a BIG memory system
SRAM is fast but expensive, not very dense
  Good choice for providing users FAST accesses
Two different types of locality
  Temporal Locality (Locality in Time)
  Spatial Locality (Locality in Space)
Use the principle of locality
  Present the user with as much memory as is available in the cheapest technology
  Provide access at the speed offered by the fastest technology
Notes: Let summarize today lecture. The first thing we covered is the principle of locality.
There are two types of locality: temporal, or locality of time and spatial, locality of space.
We talked about memory system design.
The key idea of memory system design is to present the user with as much memory as possible in the cheapest technology while by taking advantage of the principle of locality, create an illusion that the average access time is close to that of the fastest technology.
As far as Random Access technology is concerned, we concentrate on 2: DRAM and SRAM.
DRAM is slow but cheap and dense so is a good choice for presenting the use with a BIG memory system.
SRAM, on the other hand, is fast but it is also expensive both in terms of cost and power, so it is a good choice for providing the user with a fast access time.
I have already showed you how DRAMs are used to construct the main memory for the SPARCstation 20.
On Friday, we will talk about caches.
+2 = 78 min. (Y:58)

## Slide 13: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache

## Slide 14: Processor Memory Latency Gap
Proc
60%/yr.
(2X/1.5 yr)
DRAM
9%/yr.
(2X/10 yrs)
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
1982
Processor-memory
performance gap: (grows 50% / year)
Performance
Year
Moore’s Law
Notes: Y-axis is performance
X-axis is time
Latency
Clich?
Not e that x86 didn have cache on chip until 1989

## Slide 15: Levels of Memory Hierarchy
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Transfer Unit
prog./compiler
cache controller
OS
user/operator
Upper Level
Lower Level
faster
Larger

## Slide 16: Inside the Processor
AMD Barcelona: 4 processor cores

## Slide 17: Basics of Cache
Our first example: Direct-mapped cache
Block Placement
  For each item of data at the lower level, there is exactly one location in cache where it might be
  Address mapping: modulo number of blocks
M
r
y
0
0
0
0
1
0
0
1
0
1
0
1
0
0
1
0
1
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
0
0
0
0
1
0
1
0
0
1
1
1
0
0
1
0
1
1
1
0
1
1
1

## Slide 18: Tags and Valid Bits - Block Finding
How do we know which particular block is stored in a cache location
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 19: Cache Example (1)
8-blocks, 1 word/block, direct mapped
Initial state of cache
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 20: Cache Example (2)
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Memory[101102]
111 | N |  | 
Address (decimal) | Address (binary) | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 21: Cache Example (3)
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Memory[110102]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Memory[101102]
111 | N |  | 
Address (decimal) | Address (binary) | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 22: Cache Example (4)
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Memory[110102]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Memory[101102]
111 | N |  | 
Address (decimal) | Address (binary) | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 23: Cache Example (5)
Index | V | Tag | Data
000 | Y | 10 | Memory[100002]
001 | N |  | 
010 | Y | 11 | Memory[110102]
011 | Y | 00 | Memory[000112]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Memory[101102]
111 | N |  | 
Address (decimal) | Address (binary) | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 24: Cache Example (6)
Index | V | Tag | Data
000 | Y | 10 | Memory[100002]
001 | N |  | 
010 | Y | 10 | Memory[100102]
011 | Y | 00 | Memory[000112]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Memory[101102]
111 | N |  | 
Address (decimal) | Address (binary) | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 25: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache

## Slide 26: Memory Address
100000
101000
100100
100001
100010
100011
100101
100111
100110

## Slide 27
1K words, 1-word block
  Cache index: lower 10 bits
  Cache tag: upper 20 bits
  Valid bit (When start up, valid is 0)
Address Subdivision

## Slide 28: Example - Larger Block Size
64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address = 1200/16 = 75
Block number = 75 modulo 64 = 11
1200=00…00100101100002 /100002 =>00…0010010112
10010112 =>0010112
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits

## Slide 29: Example - Intrinsity FastMATH (1)
Embedded MIPS processor
  12-stage pipeline
  Instruction and data access on each cycle
Split cache: Separate I-cache and D-cache
  Each 16KB: 256 blocks × 16 words/block

## Slide 30: Example - Intrinsity FastMATH (2)
  Cache: 16KB
  256 blocks × 16 words/block

## Slide 31: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer number of blocks
    More competition  increased miss rate
Larger miss penalty
  Larger blocks  pollution
  Can override benefit of reduced miss rate
  Early restart and critical-word-first can help
Notes: Eearly restart: to resume the execution as soon as the requested word of block is returned rather than wait for the entire block. Work good for instruction.
critical word first: the requested word is transferred first. Then the remaining transfer start from the word next to the requested word and wrapping around to the beginning.

## Slide 32: Block Size on Performance
Increase block size tends to decrease miss rate
Notes: Each line represents a cache of different size.

## Slide 33: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache

## Slide 34: Cache Hit and Miss
Cache read
  Read hit
  Read miss
Cache write
  Write hit
    Write-through
    Write-back
  Write miss

## Slide 35: Read Cache
Read Hit
On cache hit, CPU proceeds normally
Read Miss
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 36: Write Hit - Write-Through
There are two copies of data, one in cache and one in memory
Write Hit
Write through: also update memory
Increase the traffic to memory
Also makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 37: Avoid Waiting for Memory in Write Through
Use a write buffer (WB)
  Processor: Writes data into cache and WB
  Memory controller: Write WB data to memory
Write buffer is just a FIFO
  Typical number of entries: 4
Memory system designer’s nightmare
  Store frequency > 1 / DRAM write cycle
  Write buffer saturation => CPU stalled
Processor
Cache
Write Buffer
DRAM
Notes: You are right, memory is too slow. We really didn't writ e to the memory directly. We are writing to a write buffer.
Once the data is written into the write buffer and assuming a cache hit, the CPU is done with the write. The memory controller will then move the write buffer contents to the real memory behind the scene.
The write buffer works as long as the frequency of store is not too high. Notice here, I am referring to the frequency with respect to time, not with respect to number of instructions.
Remember the DRAM cycle time we talked about last time. It sets the upper limit on how frequent you can write to the main memory.
If the store are too close together or the CPU time is so much faster than the DRAM cycle time, you can end up overflowing the write buffer and the CPU must stop and wait.
+2 = 60 min. (Y:40)

## Slide 38: Write Hit - Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow a replacing block to be read first
Data in cache and memory is inconsistent

## Slide 39: Write Miss - Write Allocation
Write Miss
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: Fetch the block
  Write around: Do not fetch the block
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually fetch the block

## Slide 40: Example - Intrinsity FastMATH
Embedded MIPS processor
  12-stage pipeline
  Instruction and data access on each cycle
Split cache: Separate I-cache and D-cache
  Each 16KB: 256 blocks × 16 words/block
  D-cache: Write-through or write-back
SPEC2000 miss rates
  I-cache: 0.4%
  D-cache: 11.4%
  Weighted average: 3.2%

## Slide 41: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache

## Slide 42: Memory Design to Support Cache
How to increase memory bandwidth to reduce miss penalty?

## Slide 43: Interleaving for Bandwidth
Access pattern without interleaving
Access Bank 0 again
Access
Transfer time
Data ready
Cycle time
D1 available
Start access for D1
Start access for D2
Access time
Access pattern with interleaving
Access Bank 0
Access Bank 1
Access Bank 2
Access Bank 3

## Slide 44: Miss Penalty for Different Memory Organizations
Assume
1 memory bus clock to send the address
15 memory bus clocks for each DRAM access initiated
1 memory bus clock to send a word of data
A cache block = 4 words
Three memory organizations :
  A one-word-wide bank of DRAMs
    Miss penalty = 1 + 4 x 15 + 4 x 1 = 65
  A four-word-wide bank of DRAMs
    Miss penalty = 1 + 15 + 1 = 17
  A four-bank, one-word-wide bus of DRAMs
    Miss penalty = 1 + 1 x 15 + 4 x 1 = 20

## Slide 45: Access of DRAM
21-0
2048 x 2048
array

## Slide 46: DRAM Generations
Year | Capacity | $/GB
1980 | 64Kbit | $1500000
1983 | 256Kbit | $500000
1985 | 1Mbit | $200000
1989 | 4Mbit | $50000
1992 | 16Mbit | $15000
1996 | 64Mbit | $10000
1998 | 128Mbit | $4000
2000 | 256Mbit | $1000
2004 | 512Mbit | $250
2007 | 1Gbit | $50
Trac:access time to a new row
Tcac:column access time to existing row

## Slide 47: DDR SDRAM
Double Data Rate Synchronous DRAMs
Burst access from a sequential locations
Starting address, burst length
Data transferred under control of clock
(300 MHz, 2004)
Clock is used to eliminate the need of synchronization and the need of supplying successive address
Data transfer on both leading an falling edge of clock

## Slide 48: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache

## Slide 49: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
With simplified assumptions

## Slide 50: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
  Compute the actual CPI?
Miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster

## Slide 51: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 52: Performance Summary
When CPU performance increased
  Miss penalty becomes more significant
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
Cannot neglect cache behavior when evaluating system performance

## Slide 53: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache

## Slide 54: Improving Cache Performance
Reduce the time to hit in the cache
Decrease the miss ratio
Decrease the miss penalty

## Slide 55: Direct Mapped
Block Placement
  For each item of data at the lower level, there is exactly one location in cache where it might be
  Address mapping: modulo number of blocks
M
e
m
o
r
y
0
0
0
0
1
0
0
1
0
1
0
1
0
0
1
0
1
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
0
0
0
0
1
0
1
0
0
1
1
1
0
0
1
0
1
1
1
0
1
1
1

## Slide 56: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)

## Slide 57: Associative Cache Example
Placement of a block whose address is 12

## Slide 58: Possible Associativity Structures
An 8-block cache

## Slide 59: Associativity Example (1)
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 
time

## Slide 60: Associativity Example (2)
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative (0, 8, 0, 6, 8)
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | M[em8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 
time
2-way set associative (0, 8, 0, 6, 8)
time

## Slide 61: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 62: A 4-Way Set-Associative Cache
Increasing associativity shrinks index, expands tag

## Slide 63: Comparing Data Available Time
Direct mapped cache
  Cache block is available BEFORE Hit/Miss
    Possible to assume a hit and continue, recover later if miss
N-way set-associative cache
  Data comes AFTER Hit/Miss decision
  Extra MUX delay for the data

## Slide 64: Data Placement Policy
Direct mapped cache
  Each memory block mapped to one location
  No need to make any decision
  Current item replaces previous one in location
N-way set associative cache
  Each memory block has choice of N locations
Fully associative cache
  Each memory block can be placed in ANY cache location
Misses in N-way set-associative or fully associative cache
  Bring in new block from memory
  Throw out a block to make room for new block
  Need to decide on which block to throw out

## Slide 65: Cache Block Replacement
Direct mapped: No choice
Set associative or fully associative
  Random
  LRU (Least Recently Used)
    Hardware keeps track of the access history and replace the block that has not been used for the longest time
  An example of a pseudo LRU (for a two-way set associative)
    Use a pointer pointing at each block in turn
    Whenever an access to the block the pointer is pointing at, move the pointer to the next block
    When need to replace, replace the block currently pointed at

## Slide 66: Comparison of the Structures
N-way set-associative cache
  N comparators vs. 1
  Extra MUX delay for the data
  Data comes AFTER Hit/Miss decision and set selection
Direct mapped cache
  Cache block is available BEFORE Hit/Miss
    Possible to assume a hit and continue, recover later if miss

## Slide 67: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache

## Slide 68: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 69: Multilevel Cache Example (1)
Given
  CPU base CPI = 1, clock rate = 4GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 70: Multilevel Cache Example (2)
Now add L-2 cache
  L-1 miss rate to L-2 = 2% (with one cache: to M)
  L-2 access time = 5ns (to M: 100ns)
  L-2 miss rate to main memory = 0.5%
Primary miss with L-2 hit (2%)
  Penalty to access L-2 = 5ns/0.25ns = 20 cycles
Primary miss with L-2 miss (0.5%)
  Penalty to access memory = 400 cycles
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6

## Slide 71: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single-level cache
  L-1 block size smaller than L-2 block size

## Slide 72: Interactions with Advanced CPUs
Out-of-order CPUs can execute instructions during cache miss
  Pending store stays in load/store unit
  Dependent instructions wait in reservation stations
    Independent instructions continue
Effect of miss depends on program data flow
  Much harder to analyze
  Use system simulation

## Slide 73: Interactions with Software
Misses depend on memory access patterns
  Algorithm behavior
  Compiler optimization for memory access