## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Virtual Memory
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)
Programs share main memory
  Each gets a private virtual address space holding its frequently used code and data
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a page
  VM translation “miss” is called a page fault

## Slide 3: Two Programs Sharing Physical Memory
A program’s address space is divided into pages (all one fixed size) or segments (variable sizes)
Program 1
virtual address space
Main memory
Program 2
virtual address space

## Slide 4: Address Translation
A virtual address is translated to a physical address by a combination of hardware and software
So each memory request first requires an address translation from the virtual space to the physical space
  A virtual memory miss (i.e., when the page is not in physical memory) is called a page fault.
Virtual page number
Page offset
31 12 11 0
Physical page number
Page offset
29 12 11 0
Translation
Virtual Address (VA)
Physical Address (PA)

## Slide 5: Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS code
Try to minimize page fault rate
  Fully associative placement in memory
  Smart replacement algorithms

## Slide 6: Page Tables
Stores placement information
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  Page table entry (PTE) stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk

## Slide 7: Address Translation Mechanisms

## Slide 8: Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written

## Slide 9: Fast Translation Using a TLB
Address translation would appear to require extra memory references
  One to access the PTE
  Then the actual memory access
But access to page tables has good locality
  So use a fast cache of PTEs within the CPU
  Called a Translation Look-aside Buffer (TLB)
  Typical: 16–512 PTEs, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate
  Misses could be handled by hardware or software

## Slide 10: Fast Translation Using a TLB

## Slide 11: TLB Misses
If page is in memory
  Load the PTE from memory and retry
  Could be handled in hardware or in software
If page is not in memory (page fault)
  OS handles fetching the page and updating the page table
  Then restart the faulting instruction

## Slide 12: TLB and Cache

## Slide 13: TLB Event Combinations
TLB miss: PTE not in TLB
Page Table miss: page not in memory
Cache miss: block not in cache
TLB | Page Table | Cache | Possible? Under what circumstances?
Hit | Hit | Miss | Yes. Although page table is never checked if TLB hits.
Miss | Hit | Hit | Yes. TLB misses, PA in page table, data in cache.
Miss | Hit | Miss | Yes. TLB misses, PA in page table, data not in cache.
Miss | Miss | Miss | Yes. Page fault.
Hit | Miss | Miss/Hit | Impossible. Cannot have TLB translation if page is not in memory.
Miss | Miss | Hit | Impossible. Data cannot be allowed in cache if the page is not in memory

## Slide 14: The Hardware / Software Boundary
Which part of address translation is done by hardware?
TLB that caches recent translations:
  TLB access time is part of cache hit time
  May allot extra stage in pipeline
Page Table storage, fault detection and updating
  Dirty & Reference bits
  Page faults result in interrupts
Disk Placement:
(Hardware)
(Hardware)
(Software)
(Software)

## Slide 15: The Memory Hierarchy
Common principles apply at all levels of the memory hierarchy
  Based on notions of caching
At each level in the hierarchy
  Block placement
  Finding a block
  Replacement on a miss
  Write policy

## Slide 16: Block Placement
Determined by associativity
  Direct mapped (1-way associative)
    One choice for placement
  n-way set associative
    n choices within a set
  Fully associative
    Any location
Higher associativity reduces miss rate
  Increases complexity, cost, and access time

## Slide 17: Finding a Block
Hardware caches
  Reduce comparisons to reduce cost
Virtual memory
  Full table lookup makes full associativity feasible
  Benefit in reduced miss rate

## Slide 18: Replacement
Choice of entry to replace on a miss
  Least recently used (LRU)
    Complex and costly hardware for high associativity
  Random
    Close to LRU, easier to implement
Virtual memory
  LRU approximation with hardware support

## Slide 19: Write Policy
Write-through
  Update both upper and lower levels
  Simplifies replacement, but may require write buffer
Write-back
  Update upper level only
  Update lower level when block is replaced
  Need to keep more state (e.g., dirty bit)
Virtual memory
  Only write-back is feasible, given disk write latency

## Slide 20: Sources of Misses
Compulsory misses (aka cold start misses)
  First access to a block
Capacity misses
  Due to finite cache size
  A replaced block is later accessed again
Conflict misses (aka collision misses)
  In a non-fully associative cache
  Due to competition for entries in a set
  Would not occur in a fully associative cache of the same total size

## Slide 21: Cache Design Trade-offs