## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Outline
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy
Using a Finite State Machine to Control a Simple Cache
Parallelism and Memory Hierarchies: Cache Coherence

## Slide 3: Levels of Memory Hierarchy
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Transfer Unit
prog./compiler
cache controller
OS
user/operator
Upper Level
Lower Level
faster
Larger

## Slide 4: Virtual Memory
pages
register
cache
memory
disk
frame
4

## Slide 5: Diagram of Process State
new
ready
running
terminated
waiting
admitted
interrupt
exit
scheduler dispatch
I/O or event wait
I/O or
event completion

## Slide 6: CPU Scheduler
Select one of the ready processes, and allocates the CPU to it.
ready queue
I/O queue(s)
I/O
CPU

## Slide 7: Virtual Memory (1)
Programs share main memory (Multi-programming and I/O)
  Program executed in a name space (virtual address space) different from memory space (physical address space)
  Each gets a private virtual address space holding its frequently used code and data, starting at address 0, only accessible to itself
    Yet, any can run anywhere in physical memory
    Virtual memory implements the translation from virtual space to physical space
  Every program has lots of memory (> physical memory)
  Protected from other programs

## Slide 8: Virtual Memory (2)
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called page
  VM translation “miss” is called page fault

## Slide 9: Virtual Memory (3)

Notes: 9

## Slide 10: Outline
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy
Using a Finite State Machine to Control a Simple Cache
Parallelism and Memory Hierarchies: Cache Coherence

## Slide 11: Basic Issues in Virtual Memory
Size of data blocks that are transferred from disk to main memory
Which region of memory to hold new block => Placement policy (how to the page?)
When memory is full, then some region of memory must be released to make room for the new block => replacement policy
When to fetch missing items from disk?
  Fetch only on a fault => demand load policy
pages
register
cache
memory
disk
frame

## Slide 12: Block Size and Placement Policy
Huge miss penalty
  A page fault may take millions of cycles to process
  Pages should be fairly large (e.g., 4KB) to amortize the high access time
    Reducing page faults is important
      Fully associative placement => use page table (in memory) to locate pages

## Slide 13: Address Translation
Fixed-size pages (e.g., 4K)

## Slide 14: Paging
Virtual and physical address space partitioned into blocks of equal size
Key operation: address mapping
MAP: V  M  {} address mapping function
MAP(a) = a' if data at virtual address a is present in physical address a' and a' in M
=  if data at virtual address a is not present in M
page frames
pages
Processor
Name Space V
Addr Trans
Mechanism
fault
handler
Main
Memory
Secondary
Memory
a
a
a'

missing item fault
physical address
OS does this transfer

## Slide 15: Page Tables
Stores placement information
  Page table stored in main memory
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  Page table entry (PTE) stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk

## Slide 16: Page Tables
All addresses generated by the program are virtual addresses
Table located in physical memory
How many memory references for each address translation?

## Slide 17: Page Fault
Page hit, proceed normally
Page fault means that page is not in memory
Huge miss penalty
  A page fault may take millions of cycles to process
Hardware must detect situation but it cannot remedy the situation
Can handle the faults in software instead of hardware, because handling time is small compared to disk access
  The software can be very smart or complex
  The faulting process can be context-switched

## Slide 18: OS Handling Page Faults
Hardware must trap to the operating system so that it can remedy the situation
  Pick a page to discard (may write it to disk)
  Load the page in from disk
  Update the page table
  Resume to program so HW will retry and succeed!
In addition, OS must know where to find the page
  Create space on disk for all pages of process (swap space)
  Use a data structure to record where each valid page is on disk (may be part of page table)
  Use another data structure to track which process and virtual addresses use each physical page => for replacement purpose

## Slide 19: When to Fetch Missing Items From Disk
Fetch only on a fault
  => Demand load policy

## Slide 20: Page Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written

## Slide 21: Problems of Page Table
Page table is too big
Access to page table is too slow (needs one memory read)

## Slide 22: Outline
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy
Using a Finite State Machine to Control a Simple Cache
Parallelism and Memory Hierarchies: Cache Coherence

## Slide 23: Impact of Paging - Huge Page Table
Page table occupies storage 32-bit VA, 4KB page, 4bytes/entry => 220 PTE, 4MB table
Possible solutions
  Use bounds register to limit table size; add more if exceed
  Let pages to grow in both directions => 2 tables, 2 limit registers, one for hash, one for stack
  Use hashing => page table same size as physical pages
  Multiple levels of page tables
  Paged page table (page table resides in virtual space)

## Slide 24: Hashing - Inverted Page Tables
28-bit virtual address,4 KB per page, and 4 bytes per page-table entry
The number of pages: 64K
The number of physical frames: 16K
  Page table size : 64 K (pages #) x 4 = 256 KB
  Inverted page table : 16 K (frame #) x (4+?) = 64 KB
  => TLBs or virtually addressed caches are critical
V.Page P. Frame
Hash
Virtual
Page
=
Notes: Page 520

## Slide 25: Two-level Page Tables
32-bit address:
P1 index
P2 index
page offset
4 bytes
4 bytes
4KB
10
10
12
1K
PTEs
4 GB virtual address space
4 KB of PTE1
(Each entry indicate if any page in the segment is allocated)
4 MB of PTE2
  paged, holes
What about a 48-64 bit address space?

## Slide 26: Outline
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy
Using a Finite State Machine to Control a Simple Cache
Parallelism and Memory Hierarchies: Cache Coherence

## Slide 27: Impact of Paging - More Memory Access
Each memory operation (instruction fetch, load, store) requires a page-table access
  Basically double number of memory operations
  One to access the PTE
  Then the actual memory access

## Slide 28: Translation Lookaside Buffer (TLB)
Access to page tables has good locality
  Fast cache of PTEs within the CPU
  Called a Translation Look-aside Buffer (TLB)
Typical RISC processors have memory management unit (MMU) which includes TLB that does page table lookup
  TLB can be organized as fully associative, set associative, or direct mapped
  TLBs are small, typically 16–512 PTEs, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate
  Misses could be handled by hardware or software

## Slide 29: Fast Translation Using TLB (Translation Lookaside Buffer)
TLB

## Slide 30: TLB Hit
TLB hit on read
TLB hit on write
  Toggle dirty bit (write back to page table on replacement)

## Slide 31: TLB Miss
If page is in memory
  Load the PTE from memory and retry
  Could be handled in hardware
    Can get complex for more complicated page table structures
  Or in software
    Raise a special exception, with optimized handler
If page is not in memory (page fault)
  OS fetches the page and updates the page table (software)
  Then restarts the faulting instruction

## Slide 32: Outline
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy
Using a Finite State Machine to Control a Simple Cache
Parallelism and Memory Hierarchies: Cache Coherence

## Slide 33: Making Address Translation Practical
In VM, memory acts like a cache for disk
  Page table maps virtual page numbers to physical frames
  Use a page table cache for recent translation => Translation Lookaside Buffer (TLB)
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
20 t
t
1/2 t
Translation
with a TLB

## Slide 34: Integrate TLB and Cache

## Slide 35: TLBs and Caches

## Slide 36: Possible Combinations of Events
Cache
TLB
Page
table
Possible? Conditions?
Miss
Hit
Hit
Yes; but page table never checked if
TLB hits
Hit
Miss
Hit
TLB miss, but entry found in page
table;after retry, data in cache
Miss
Miss
Hit
TLB miss, but entry found in page
table; after retry, data miss in cache
Miss
Miss
Miss
TLB miss and is followed by a page
fault; after retry, data miss in cache
Miss
Hit
Miss
impossible;
not in TLB if page not in memory
Hit
Hit
Miss
impossible;
not in TLB if page not in memory
Hit
Miss
Miss
impossible;
not in cache if page not in memory

## Slide 37: Virtual Address and Cache
TLB access is serial with cache access
  Cache is physically indexed and tagged
Alternative: Virtually addressed cache
  Cache is virtually indexed and virtually tagged
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data
CPU
data
Trans-
lation
Cache
Main
Memory
VA
hit
PA
CPU

## Slide 38: Virtually Addressed Cache
Require address translation only on miss!
Problem
  Same virtual addresses (different processes) map to different physical addresses
  Synonym/alias problem: two different virtual addresses map to same physical address
    Two different cache entries holding data for the same physical address!
    For update: must update all cache entries with same physical address or memory becomes inconsistent
    Determining this requires significant hardware, essentially an associative lookup on the physical address tags to see if you have multiple hits;
    Or software enforced alias boundary: same least-significant bits of VA &PA > cache size
tag + process id

## Slide 39: Integrating TLB and Cache

## Slide 40: An Alternative:Virtually Indexed but Physically Tagged
TLB
Cache
10
2
00
4 bytes
index
1 K
page #
displace
20
12
associative
lookup
32
PA
Hit/
Miss
PA
Data
Hit/
Miss
=
IF cache hit AND (cache tag = PA) then deliver data to CPU
ELSE IF [cache invalid OR (cache tag ! = PA)] and TLB hit THEN
access memory with the PA from the TLB
ELSE do standard VA translation

## Slide 41: Problem with Overlapped Access
11
2
00
virt page #
disp
20
12
cache
index
This bit is changed by VA translation, but is needed for cache lookup
Solutions:
go to 8K byte page sizes;
go to 2 way set associative cache
SW guarantee VA[13]=PA[13]
1K
4
4
10
2-way set associative cache
Address bits to index into cache must not change as a result of VA translation
  Limits to small caches, large page sizes, or high n-way set associativity if want a large cache
  Ex.: cache is 8K bytes instead of 4K

## Slide 42: Outline
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy
Using a Finite State Machine to Control a Simple Cache
Parallelism and Memory Hierarchies: Cache Coherence

## Slide 43: The Memory Hierarchy
Common principles apply at all levels of the memory hierarchy
  Based on notions of caching
At each level in the hierarchy
  Block placement
  Finding a block
  Replacement on a miss
  Write policy
The BIG Picture

## Slide 44: Block Placement
Determined by associativity
  Direct mapped (1-way associative)
    One choice for placement
  n-way set associative
    n choices within a set
  Fully associative
    Any location
Higher associativity reduces miss rate
  Increases complexity, cost, and access time

## Slide 45: Find a Block
Hardware caches
  Reduce comparisons to reduce cost
Virtual memory
  Full table lookup makes full associativity feasible
  Benefit in reduced miss rate
Associativity | Location method | Tag comparisons
Direct mapped | Index | 1
n-way set associative | Set index, then search entries within the set | n
Fully associative | Search all entries | #entries
 | Full lookup table | 0

## Slide 46: Replacement
Choice of entry to replace on a miss
  Least recently used (LRU)
    Complex and costly hardware for high associativity
  Random
    Close to LRU, easier to implement
Virtual memory
  LRU approximation with hardware support

## Slide 47: Write Policy
Write-through
  Update both upper and lower levels
  Simplifies replacement, but may require write buffer
Write-back
  Update upper level only
  Update lower level when block is replaced
  Need to keep more state
Virtual memory
  Only write-back is feasible, given disk write latency

## Slide 48: Sources of Misses
Compulsory misses (aka cold start misses)
  First access to a block
Capacity misses
  Due to finite cache size
  A replaced block is later accessed again
Conflict misses (aka collision misses)
  In a non-fully associative cache
  Due to competition for entries in a set
  Would not occur in a fully associative cache of the same total size

## Slide 49: Challenge in Memory Hierarchy
Every change that potentially improves miss rate can negatively affect overall performance
Design change Effects on miss rate Possible effects
size  capacity miss  access time 
associativity  conflict miss  access time 
block size  spatial locality  miss penalty 
Trends
  Synchronous SRAMs (provide a burst of data)
  Redesign DRAM chips to provide higher bandwidth or processing
  Restructure code to increase locality
  Use prefetching (make cache visible to ISA)

## Slide 50: Outline
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy
Using a Finite State Machine to Control a Simple Cache
Parallelism and Memory Hierarchies: Cache Coherence

## Slide 51: Cache Control
Example cache characteristics
  Direct-mapped, write-back, write allocate
  Block size: 4 words (16 bytes)
  Cache size: 16 KB (1024 blocks)
  32-bit byte addresses
  Valid bit and dirty bit per block
  Blocking cache
    CPU waits until access is complete
Tag
Index
Offset
0
3
4
13
14
31
4 bits
10 bits
18 bits

## Slide 52: Interface Signals
Cache
CPU
Memory
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
32
32
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
128
128
Multiple cycles per access

## Slide 53: Cache Controller FSM
Could partition into separate states to reduce clock cycle time

## Slide 54: Finite State Machines
Use an FSM to sequence control steps
Set of states, transition on each clock edge
  State values are binary encoded
  Current state stored in a register
  Next state = fn (current state, current inputs)
Control output signals = fo (current state)

## Slide 55: Outline
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy
Using a Finite State Machine to Control a Simple Cache
Parallelism and Memory Hierarchies: Cache Coherence

## Slide 56: Cache Coherence Problem
Suppose two CPU cores share a physical address space
  Write-through caches
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
2 | CPU B reads X | 0 | 0 | 0
3 | CPU A writes 1 to X | 1 | 0 | 1
Two different processors have two different values for the same location

## Slide 57: Coherence Defined
Informally: Reads return most recently written value
Formally:
  P writes X; P reads X (no intervening writes)  read returns written value
  P1 writes X; P2 reads X (sufficiently later)  read returns written value
    c.f. CPU B reading X after step 3 in example
  P1 writes X, P2 writes X  all processors see writes in the same order
    End up with the same final value for X

## Slide 58: Cache Coherence Protocols
Operations performed by caches in multiprocessors
  Migration of data to local caches
    Reduces bandwidth for shared memory
  Replication of read-shared data
    Reduces contention for access
Snooping protocols
  Each cache monitors bus reads/writes
Directory-based protocols
  Caches and memory record sharing status of blocks in a directory

## Slide 59: Invalidating Snooping Protocols
Cache gets exclusive access to a block when it is to be written
  Broadcasts an invalidate message on the bus
  A subsequent read results in another cache miss
CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
 |  |  |  | 0
CPU A reads X | Cache miss for X | 0 |  | 0
CPU B reads X | Cache miss for X | 0 | 0 | 0
CPU A writes 1 to X | Invalidate for X | 1 |  | 0
CPU B read X | Cache miss for X | 1 | 1 | 1

## Slide 60: Multilevel On-Chip Caches
Intel Nehalem 4-core processor
  Per core: 32KB L1 I-cache, 32KB L1 D-cache, 512KB L2 cache

## Slide 61: 2-Level TLB Organization
 | Intel Nehalem | AMD Opteron X4
Virtual addr | 48 bits | 48 bits
Physical addr | 44 bits | 48 bits
Page size | 4KB, 2/4MB | 4KB, 2/4MB
L1 TLB (per core) | L1 I-TLB: 128 entries for small pages, 7 per thread (2×) for large pages L1 D-TLB: 64 entries for small pages, 32 for large pages Both 4-way, LRU replacement | L1 I-TLB: 48 entries L1 D-TLB: 48 entries Both fully associative, LRU replacement
L2 TLB (per core) | Single L2 TLB: 512 entries 4-way, LRU replacement | L2 I-TLB: 512 entries L2 D-TLB: 512 entries Both 4-way, round-robin LRU
TLB misses | Handled in hardware | Handled in hardware

## Slide 62: 3-Level Cache Organization
 | Intel Nehalem | AMD Opteron X4
L1 caches (per core) | L1 I-cache: 32KB, 64-byte blocks, 4-way, approx LRU replacement, hit time n/a L1 D-cache: 32KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | L1 I-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, hit time 3 cycles L1 D-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, write-back/allocate, hit time 9 cycles
L2 unified cache (per core) | 256KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | 512KB, 64-byte blocks, 16-way, approx LRU replacement, write-back/allocate, hit time n/a
L3 unified cache (shared) | 8MB, 64-byte blocks, 16-way, replacement n/a, write-back/allocate, hit time n/a | 2MB, 64-byte blocks, 32-way, replace block shared by fewest cores, write-back/allocate, hit time 32 cycles
n/a: data not available |  | 

## Slide 63: Pitfalls (1)
Byte vs. word addressing
  Example: 32-byte direct-mapped cache, 4-byte blocks
    Byte 36 maps to block 1
    Word 36 maps to block 4
Ignore memory system effects when writing or generating code
  Example: iterating over rows vs. columns of arrays
  Large strides result in poor locality

## Slide 64: Pitfalls (2)
In multiprocessor with shared L2 or L3 cache
  Less associativity than cores results in conflict misses
  More cores  need to increase associativity
Using AMAT (Average Memory Access Time) to evaluate performance of out-of-order processors
  Ignore effect of non-blocked accesses
  Instead, evaluate performance by simulation

## Slide 65: Concluding Remarks
Fast memories are small, large memories are slow
  We really want fast, large memories 
  Caching gives this illusion 
Principle of locality
  Programs use a small part of their memory space frequently
Memory hierarchy
  L1 cache  L2 cache  …  DRAM memory  disk
Memory system design is critical for multiprocessors