## Slide 1: CSC3050 – Computer Architecture
Prof. Yeh-Ching Chung
School of Science and Engineering
Chinese University of Hong Kong, Shenzhen

## Slide 2: Introduction
I/O devices can be characterized by
  Behaviour: input, output, storage
  Partner: human or machine
  Data rate: bytes/sec, transfers/sec
I/O bus connections

## Slide 3: I/O System Characteristic
Dependability is important
  Particularly for storage devices
Performance measures
  Latency (response time)
  Throughput (bandwidth)
  Desktops & embedded systems
    Mainly interested in response time & diversity of devices
  Servers
    Mainly interested in throughput & expandability of devices

## Slide 4: Dependability Measures
Reliability: mean time to failure (MTTF)
Service interruption: mean time to repair (MTTR)
Mean time between failures
  MTBF = MTTF + MTTR
Availability = MTTF / (MTTF + MTTR)
Improving Availability
  Increase MTTF: fault avoidance, fault tolerance, fault forecasting
  Reduce MTTR: improved tools and processes for diagnosis and repair

## Slide 5: Interconnecting Components
Need interconnections between
  CPU, memory, I/O controllers
Bus: shared communication channel
  Parallel set of wires for data and synchronization of data transfer
  Can become a bottleneck
Performance limited by physical factors
  Wire length, number of connections
More recent alternative: high-speed serial connections with switches
  Like networks

## Slide 6: Bus Types
Processor-Memory buses
  Short, high speed
  Design is matched to memory organization
I/O buses
  Longer, allowing multiple connections
  Specified by standards for interoperability
  Connect to processor-memory bus through a bridge

## Slide 7: Bus Signals and Synchronization
Data lines
  Carry address and data
  Multiplexed or separate
Control lines
  Indicate data type, synchronize transactions
Synchronous
  Uses a bus clock
Asynchronous
  Uses request/acknowledge control lines for handshaking

## Slide 8: I/O Bus Examples
 | Firewire | USB 2.0 | PCI Express | Serial ATA | Serial Attached SCSI
Intended use | External | External | Internal | Internal | Internal
Devices per channel | 63 | 127 | 1 | 1 | 4
Data width | 4 | 2 | 2/lane | 4 | 4
Peak bandwidth | 50MB/s or 100MB/s | 0.2MB/s, 1.5MB/s, or 60MB/s | 250MB/s/lane 1×, 2×, 4×, 8×, 16×, 32× | 300MB/s | 300MB/s
Hot pluggable | Yes | Yes | Depends | Yes | Yes
Max length | 4.5m | 5m | 0.5m | 1m | 8m
Standard | IEEE 1394 | USB Implementers Forum | PCI-SIG | SATA-IO | INCITS TC T10

## Slide 9: Typical x86 PC I/O System

## Slide 10: I/O Management
I/O is mediated by the OS
  Multiple programs share I/O resources
    Need protection and scheduling
  I/O causes asynchronous interrupts
    Same mechanism as exceptions
  I/O programming is complicated
    OS provides abstractions to programs

## Slide 11: I/O Commands
I/O devices are managed by I/O controller hardware
  Transfers data to/from device
  Synchronizes operations with software
Command registers
  Cause device to do something
Status registers
  Indicate what the device is doing and occurrence of errors
Data registers
  Write: transfer data to a device
  Read: transfer data from a device

## Slide 12: I/O Register Mapping
Memory-mapped I/O
  Registers are addressed in same space as memory
  Address decoder distinguishes between them
  OS uses address translation mechanism to make them only accessible to kernel
I/O instructions (or port-mapped I/O)
  Separate instructions to access I/O registers
  Can only be executed in kernel mode
  Example: x86 (in and out)

## Slide 13: Polling
Periodically check I/O status register
  If device ready, do operation
  If error, take action
Common in small or low-performance real-time embedded systems
  Predictable timing
  Low hardware cost
In other systems, wastes CPU time

## Slide 14: Interrupts
When a device is ready or error occurs
  Controller interrupts CPU
Interrupt is like an exception
  But not synchronized to instruction execution
  Can invoke handler between instructions
  Cause information often identifies the interrupting device
Priority interrupts
  Devices needing more urgent attention get higher priority
  Can interrupt handler for a lower priority interrupt

## Slide 15: I/O Data Transfer
Polling and interrupt-driven I/O
  CPU transfers data between memory and I/O data registers
  Time consuming for high-speed devices
Direct memory access (DMA)
  OS provides starting address in memory
  I/O controller transfers to/from memory autonomously
  Controller interrupts on completion or error

## Slide 16: DMA/Cache Interaction
If DMA writes to a memory block that is cached
  Cached copy becomes stale
If write-back cache has dirty block, and DMA reads memory block
  Reads stale data
Need to ensure cache coherence
  Flush blocks from cache if they will be used for DMA
  Or use non-cacheable memory locations for I/O

## Slide 17: DMA/VM Interaction
OS uses virtual addresses for memory
  DMA blocks may not be contiguous in physical memory
Should DMA use virtual addresses?
  Would require controller to do translation
If DMA uses physical addresses
  May need to break transfers into page-sized chunks
  Or chain multiple transfers
  Or allocate contiguous physical pages for DMA
Whichever is used, the OS must cooperate by not remapping pages while a DMA transfer involving that page is in progress

## Slide 18: The DMA Stale Data Problem
In systems with caches, there can be two copies of a data item, one in the cache and one in the main memory
  For a DMA input (from disk to memory) – the processor will be using stale data if that location is also in the cache
  For a DMA output (from memory to disk) and a write-back cache –the I/O device will receive stale data if the data is in the cache and has not yet been written back to the memory
The coherency problem can be solved by
  Routing all I/O activity through the cache – expensive and a large negative performance impact
  Having the OS invalidate all the entries in the cache for an I/O input or force write-backs for an I/O output (called a cache flush)
  Providing hardware to selectively invalidate cache entries – i.e., need a snooping cache controller