## Slide 1: CSC6032 – Advanced Operating Systems
Prof. Yeh-Ching Chung
School of Data Science
Chinese University of Hong Kong, Shenzhen

## Slide 2: 虛擬化技術 Virtualization Techniques
Hardware Support Virtualization
SR-IOV

## Slide 3: Agenda
Overview
  Introduction
    Memory Virtualization
    Storage Virtualization
    Servers Virtualization
    I/O Virtualization
PCIe Virtualization
  Motivation
  Directed I/O
  PCIe Architecture
SR-IOV
  Architecture Supporting SR-IOV Capability
  ARI – Alternative Routing ID Interpretation
  ACS Access Control Services
  ATS - Address Translation Service
  Theory of Operations

## Slide 4: Overview
Memory Virtualization
Storage Virtualization
Servers Virtualization
I/O Virtualization

## Slide 5: Overview
Memory Virtualization
  Uses memory more effectively
  Was revolutionary, but now is assumed
Storage Virtualization
  Presents storage resources in ways not bound to the underlying hardware characteristics
  Fairly common now
Servers Virtualization
  Increases typically under-utilized CPU resources
  Becoming more common

## Slide 6: Overview
I/O Virtualization
  Virtualizing the I/O path between a server and an external device
  Can apply to anything that uses an adapter in a server, such as:
    Ethernet Network Interface Cards (NICs)
    Disk Controllers (including RAID controllers)
    Fibre Channel Host Bus Adapters (HBAs)
    Graphics/Video cards or co-processors
    SSDs mounted on internal cards

## Slide 7: PCIe I/O Virtualization
Motivation
Directed I/O
PCIe Architecuture

## Slide 8: Motivation
I/O Virtualization Solutions
  A - Software only
  B - Directed I/O (enhance performance)
  C – Directed I/O and Device Sharing (resource saving)
Virtual Machine
Virtual Machine
I/O Driver
Virtual Machine
I/O Driver
Virtual Machine Monitor
Virtual Machine
I/O Driver
Virtual Machine
I/O Driver
Virtual Machine Monitor
Virtual Machine
I/O Driver
Virtual Machine
I/O Driver
Virtual Machine Monitor
Virtual Function
Physical Function
A – Software only
B – Directed I/O
C – Directed I/O & Device Sharing

## Slide 9: PCIe I/O Virtualization
Motivation
Directed I/O
PCIe Architecture

## Slide 10: Directed I/O
Software-based sharing adds overhead to each I/O due to emulation layer
  This indirection has the additional affect of eliminating the use of hardware acceleration that may be available in the physical device.
Directed I/O has added enhancements to facilitate memory translation and ensure protection of memory that enables a device to directly DMA to/form host memory.
  Bypass the VMM’s I/O emulation layer
  Throughput improvement for the VMs

## Slide 11: Drawbacks to Directed I/O
One concern with direct assignment is that it has limited scalability
  A physical device can only be assigned to one VM.
  For example, a dual port NIC allows for direct assignment to two VMs. (one port per VM)
  Consider for a moment a fairly substantial server of the very near future
    4 physical CPU’s
    12 cores per CPU
    If we use the rule that one VM per core, it would need 48 physical ports.

## Slide 12: Terminology relating to Directed I/O
Acronym | Expansion | Defined By | What is it?
I/O MMU | I/O Memory Management Unit | Common parlance | Translation mechanism in the system memory controller (North Bridge) that allows a device or set of devices to use translated addresses when accessing main memory. In many cases, it also translates interrupts coming from the devices as messages.
ATPT | Address Translation and Protection Table | PCI SIG | I/O MMU
VT-d, VT-d2 | Virtualization Technology for Directed I/O | Intel | I/O MMU
DMAr | DMA Remapping | Intel, Microsoft | I/O MMU
IOMMU | I/O Memory Management Unit | AMD | I/O MMU

## Slide 13: PCIe I/O Virtualization
Motivation
Directed I/O
PCIe Architecture

## Slide 14: Generic Platform
System Image(SI)
  SW, e.g., a guest OS, to which virtual and physical devices can be assigned
System Image (SI)
Processor
Memory
Root Complex (RC)
Root
Port (RP)
Root
Port (RP)
PCIe Device
Switch
PCIe Device
PCIe Device
PCIe Device
System Image (SI)
System Image (SI)
System Image (SI)
Virtualization Intermediary

## Slide 15: PCIe components
Root Complex
  A root complex connects the processor and memory subsystem to the PCIe switch fabric composed of one or more switch devices
  Similar to a host bridge in a PCI system
    Generate transaction requests on
    behalf of the processor, which is
    interconnected through a local bus.
    May contain more than one PCIe port
    and multiple switch devices.

## Slide 16: PCIe components
Root Port (RP)
  The portion of the motherboard that contains the host bridge. The host bridge allows the PCIe ports to talk to the rest of the computer

## Slide 17: PCIe Device
PCIe Device
  Unique PCI Function Address
    Bus / Dev / Function
    Command, lspci -v, can get PCI device information on linux
Device
Function1
Function2

## Slide 18: Example: Multi-Function Device
The link and PCIe functionality shared by all functions is managed through Function 0
All functions use a single Bus Number captured through the PCI enumeration process
Each function can be assigned to an SI
Function 0
ATC1
Physical Resources1
Function 1
ATC2
Physical Resources2
Function 2
ATC3
Physical Resources3
Internal Routing
Configuration Resources
PCIe
Port
PCIe
Port
PCIe
Port
PCIe Device

## Slide 19: Components in PCIe Device
Configuration Space
  Devices will allocate resource such as memory and record the address into this configuration space
  Reference:
    PCI Local Bus Specification ver.2.3 Chap 6
Configuration Resources

## Slide 20: Components in PCIe Device
ARI – Alternative Routing Id Interpretation
  Alternative Routing ID Interpretation as per the PCIe Base Specification
Physical Resources
  Memory which allocated from physical memory
ATC - Address Translation Cache
  A hardware stores recently
  used address translations.
  This term is used instead of
  TLB buffer
  To differentiate the TLB used
  for I/O from the TLB used by
  the CPU
Function 0
ATC1
Physical Resources1
Function 1
ATC2
Physical Resources2
Function 2
ATC3
Physical Resources3
Internal Routing

## Slide 21: Physical V.S. Virtual
Function 0
ATC1
Physical Resources1
Function 1
ATC2
Physical Resources2
Function 2
ATC3
Physical Resources3
Internal Routing
Configuration Resources
PCIe
Port
PCIe
Port
PCIe
Port
PCIe Device
PF 0
ATC1
Physical Resources
VF 0,1
Physical Resources
VF 0,2
Physical Resources
Internal Routing
PCIe
Port
PCIe SR-IOV
Capable Device
Configuration Resources
Physical
Virtual

## Slide 22: PCIe SR-IOV Capable Device
SR-IOV
  A technique performs and manages PCIe Virtualization.
PF – physical Function
  Provide full PCIe functionality, including the SR-IOV capabilities
  Discover the page sizes supported by a PF and its associated VF
VF – virtual Function
  A “light-weight” PCIe function that
  is directly accessible by an SI,
  including an isolated memory
  space, a work queue, interrupts
  and command processing.
  For data movement
  Can be optionally migrated form
  one PF to another PF
  Can be serially shared by different
  SI
PF 0
ATC1
Physical Resources
VF 0,1
Physical Resources
VF 0,2
Physical Resources
Internal Routing
PCIe
Port
PCIe SR-IOV
Capable Device
Configuration Resources

## Slide 23: Directly and Software Shared
Figure from Inter PCI-SIG SR-IOV Primer

## Slide 24: Extended Capabilities

## Slide 25: SR-IOV Extended Capabilities

## Slide 26: SR-IOV
Architecture Supporting SR-IOV Capability
ARI – Alternative Routing ID Interpretation
ACS – Access Control Services
ATS – Address Translation Service
Data Path for Incoming Packets

## Slide 27: Platform with SR-IOV
SR-PCIM
  Configure SR-IOV Capability
  Management of PFs and VFs
  Processing of error events
  Device controls
    Power management
    Hot-plug
System Image (SI)
Processor
Memory
Root Complex (RC)
Root
Port (RP)
Root
Port (RP)
PCIe Device
Switch
PCIe Device
PCIe Device
PCIe Device
System Image (SI)
System Image (SI)
System Image (SI)
Virtualization Intermediary
Translation Agent (TA)
Address Translation and Protection Table (ATPT)
SR-PCIM
SR-PCIM

## Slide 28: Components of SR-IOV
TA – Translation Agent
  Translate address within a PCIe transaction into the associated platform physical address.
  Hardware or combination of hardware and software
  A TA may also support to enable a PCIe function to obtain address translations a priori to DMA access to the associated memory.
Translation Agent (TA)
Address Translation and Protection Table (ATPT)

## Slide 29: Components of SR-IOV
ATPT – Address Translation and Protection Table
  Contain the set of address translations accessed by a TA to Process PCEe requests
    DMA Read/Write
    Interrupt requests
  DMA Read/Write requests are translated through a combination of the Routing ID and the address contained within a PCIe transaction
  In PCIe, interrupts are treated as memory write operations.
    Though the combination of the Routing ID and the address contained within a PCIe transaction as well
Translation Agent (TA)
Address Translation and Protection Table (ATPT)

## Slide 30: SR-IOV
Architecture Supporting SR-IOV Capability
ARI – Alternative Routing ID Interpretation
ACS – Access Control Services
ATS – Address Translation Service
Data Path for Incoming Packets

## Slide 31: ARI – Alternative Routing ID Interpretation
Routing ID is used to forward requests to the corresponding PFs and VFs
All VFs and PFs must have distinct Routing IDs
ARI provides a mechanism to allow single PCIe component to support up to 256 functions.
  Originally there are 8 functions at most in a PCIe.
Figure from Intel PCI-SIG SR_IOV prim

## Slide 32: ARI – Alternative Routing ID Interpretation
Figure from SR-IOV Specification revision 1.1
Figure from Intel PCI-SIG SR_IOV prim

## Slide 33: SR-IOV
Architecture Supporting SR-IOV Capability
ARI – Alternative Routing ID Interpretation
ACS – Access Control Services
ATS – Address Translation Service
Data Path for Incoming Packets

## Slide 34: ACS – Access Control Services
The PCIe specification allows for P2P transactions.
  This means that it is possible and even desirable in some cases for one PCIe endpoint to send data directly to another endpoint without having to go through the Root Complex.
However, in a virtualized environment it is generally not desirable to have P2P transactions.
  With both direct assignment and SR-IOV, the PCIe transactions should go through the Root Complex in order for the ATS to be utilized.
ACS provides a mechanism by
which a P2P PCIe transaction
can be forced to go up through
the RC
Figure from Intel PCI-SIG SR_IOV prim

## Slide 35: SR-IOV
Architecture Supporting SR-IOV Capability
ARI – Alternative Routing ID Interpretation
ACS – Access Control Services
ATS – Address Translation Service
Data Path for Incoming Packets

## Slide 36: ATS – Address Translation Services
ATS provides a mechanism allowing a virtual machine to perform DMA transaction directly to and from a PCIe endpoint.

## Slide 37: ATS – Address Translation Services
ATS uses a request-completion protocol between a Device and a Root Complex (RC)

## Slide 38: ATS – Address Translation Services
Upon receipt of an ATS Translation Request, the TA performs the following Requests
  Validates that the Function has been configured to issue ATS Translation Requests.
  Determines whether the Function may access the memory indicated by the ATS Translation Request and has the associated access rights.
  Determines whether a translation can be provided to the Function. If yes, the TA issues a translation to the Function.
  The TA communicates the success or failure of the request to the RC which generates an ATS Translation Completion and transmits via a Response TLP through a RP to the Function.
Path
  Function(Request)=>TA=>RC(Completion)=>Function

## Slide 39: ATS – Address Translation Services
When the Function receives the ATS Translation Completion
  Either updates its ATC to reflect the translation
  Or notes that a translation does not exist.
The Function generates subsequent requests using
  either a translated address
  or an un-translated address based on the results of the Completion.

## Slide 40: SR-IOV
Architecture Supporting SR-IOV Capability
ARI – Alternative Routing ID Interpretation
ACS – Access Control Services
ATS – Address Translation Service
Data Path for Incoming Packets

## Slide 41: Data Path for incoming packets
The Ethernet packet arrives at the Ethernet NIC
The packet is sent to the Layer 2 sorter/switch/classifier
  This Layer 2 sorter is configured by the Master Driver. When either the MD or the VF Driver configure a MAC address or VLAN, this Layer 2 sorter is configured.

## Slide 42: Data Path for incoming packets
3. After being sorted by the
Layer 2 Switch, the packet is
placed into a receive queue
dedicated to the target VF.
4. The DMA operation is
initiated. The target memory
address for the DMA operation
is defined within the
descriptors in the VF, which
have been configured by the VF
driver within the VM.

## Slide 43: Data Path for incoming packets
5. The DMA Operation has
reached the chipset. Intel VT-d,
which has been configured by
the VMM then remaps the target
DMA address from a virtual host
address to a physical host address.
The DMA operation is completed;
the Ethernet packet is now in the
memory space of the VM
6. The NIC fires interrupt,
indicating a packet has
arrived. This interrupt
is handled by the VMM

## Slide 44: Data Path for incoming packets
7. The VMM fires a virtual
interrupt to the VM, so
that it is informed that
the packet has arrived

## Slide 45: Summary
SR-IOV creates Virtual Function, which records the information of the virtual PCIe device and be directly mapped to a system image.
Virtual Function is a “light weight” function just for data movement. The management is controlled by Physical Function.
ATC, a hardware stores recently used address translations
ARI, a mechanism to allow single PCIe component to support up to 256 functions. And Routing ID is used to forward requests to the corresponding PFs and VFs.
ATS, a mechanism allowing a virtual machine to perform DMA transaction directly to and from a PCIe endpoint
In the end, a example show up the data path for the incoming packets.

## Slide 46: Reference
Intel PCI-SIG SR-IOV Primer
“SR-IOV Networking in Xen: Architecture, Design and Implementation” Yaozu Dong, Zhao Yu and Greg Rose
Single Root I/O Virtualization and Sharing Specification Revision 1.1
Address Translation Services Revision 1.1
“Implementing PCI I/O Virtualization Standards”, Mike Krause and Renato Recio
PCI SIG IOV Work Group Co-chairs
http://www.mindshare.com/files/ebooks/PCI%20System%20Architecture%20(4th%20Edition).pdf
http://www.pcisig.com/developers/main/training_materials/get_document?doc_id=4717c70ea2fe2f92dcbc4560a39cba8129af32c1
http://www.intel.com/content/dam/doc/application-note/pci-sig-sr-iov-primer-sr-iov-technology-paper.pdf
http://ieeexplore.ieee.org/xpls/abs_all.jsp?arnumber=5416637&tag=1