## Slide 1: 雲端計算 Cloud Computing
Network Virtualization
Open vSwitch

## Slide 2: Open vSwitch
Virtual Switch
Open vSwitch architecture
OpenFlow

## Slide 3: Virtual Switch
SOFTWARE-BASED VIRTAUL SWITCH
HARDWARE-BASED VIRTAUL SWITCH
VN-Tag

## Slide 4: INTRODUCTION
Owing to the emergence of cloud computing service, the number of virtual switches begins to dramatically expand
  Management complexity, security issues and even performance degradation
Software/hardware based virtual switch as well as integration of open-source hypervisor with virtual switch technology is exhibited

## Slide 5: SOFTWARE-BASED VIRTAUL SWITCH
The 80x86 hypervisors implemented vSwitch
Each VM has at least one virtual network interface cards (vNICs) that are sharing physical network interface cards (pNICs) on the physical host through vSwitch
Administrator don’t have effective solution to separate packets from different VM users
For VMs reside in the same physical machine, their traffic visibility is a big issue

## Slide 6: Problems of original vSwitch
The original vSwitchs lack of advanced networking features such as VLAN, port mirror and port channel etc.
Nowadays, some hypervisor vSwitch vendors provide technologies to fix the above problems
  OpenvSwitch may be superior in quality for the reasons

## Slide 7: Virtual Switch
SOFTWARE-BASED VIRTAUL SWITCH
HARDWARE-BASED VIRTAUL SWITCH
VN-Tag

## Slide 8: HARDWARE-BASED VIRTAUL SWITCH
Why hardware-based?
  Software virtual switches consume CPU and memory usage
  Possible inconsistence of network and server configurations may cause errors and is very hard to troubleshooting and maintenance
Hardware-based virtual switch solution emerges for better resource utilization and configuration consistence

## Slide 9: Virtual Ethernet Port Aggregator (1/2)
A standardization led by HP, Extreme, IBM, Brocade and Juniper etc.
An emerging technology as part of IEEE 802.1Qbg Edge Virtual Bridge (EVB) standard
The main goal of VEPA is to allow traffic of VM to exit and re-enter the same server physical port to enable switching among VMs

## Slide 10: Virtual Ethernet Port Aggregator (2/2)
VEPA software update is required for host servers in order to force packets to be transmitted to external switches
An external VEPA enabled switch is required for communications between VMs in the same server
VEPA supports “hairpin” mode which allows traffic to “hairpin” back out the same port it just received it from--- requires firmware update to existing switches

## Slide 11: Pros. and Cons. for VEPA
Pros
  Minor software/firmware update , network configuration maintained by external switches
Cons
  VEPA still consumes server resources in order to perform forwarding table lookup

## Slide 12: Virtual Switch
SOFTWARE-BASED VIRTAUL SWITCH
HARDWARE-BASED VIRTAUL SWITCH
VN-Tag

## Slide 13: VN-Tag(1/3)
Proposed by Cisco, adopted by the IEEE as the basis for 802.1Qbh ‘Bridge Port Extension’
A VN-Tag between Layer2 and 802.1Q header is inserted to indicate what path the frame should travel on its way to another VM
The VN-Tag contains two essential fields: the source virtual interface identifier (SVIF_ID) of the sending host and the destination virtual interface identifier (DVIF_ID) of the receiving host

## Slide 14: VN-Tag(2/3)
Ethertype | Identifies the VN tag
D | Direction, 1 indicates that the frame is traveling from the bridge to the interface virtualizer (IV.)
P | Pointer, 1 indicates that a vif_list_id is included in the tag.
vif_list_id | A list of downlink ports to which this frame is to be forwarded (replicated). (multicast/broadcast operation)
Dvif_id | Destination vif_id of the port to which this frame is to be forwarded.
L | Looped, 1 indicates that this is a multicast frame that was forwarded out the bridge port on which it was received. In this case, the IV must check the Svif_id and filter the frame from the corresponding port.
R | Reserved
VER | Version of the tag
SVIF_ID | The vif_id of the source of the frame

## Slide 15: VN-Tag(3/3)
The VN-Tag capable NIC and the VN-Tag aware switch are the necessary
VN-Tag capable physical NIC
  Insert Tag at layer2 of the data frame that identify a network packet as part of a specified VM
VN-Tag aware switch
  Strip the tag from the frame header at the stage of forwarding to normal switch
  Convert a stripped or untagged frame, if the packet is to be transmitted to a VM destination via a VIF port

## Slide 16: Pros. and Cons. for VN-Tag
Pros
  With VN-Tag technique, the switching will be totally performed by external VN-Tag aware switches
  No forwarding decision table will be left in host servers
Cons
  The Ethernet frame format is modified
  We have to invest new host NICs and external switches in order to recognize VN-Tag

## Slide 17: Open vSwitch
Virtual Switch
Open vSwitch architecture
OpenFlow

## Slide 18: Open vSwitch architecture
Introduction to Open vSwitch
Main components of Open vSwitch
Open vSwitch Testing Case

## Slide 19: Open vSwitch
A software-based solution
  Resolve the problems of network separation and traffic visibility, so the cloud users can be assigned VMs with elastic and secure network configurations
Flexible Controller in User-Space
Fast Datapath in Kernel
Server
Open vSwitch Datapath
Open vSwitch Controller

## Slide 20: Open vSwitch Concepts(1/2)
Multiple ports to physical switches
  A port may have one or more interfaces
    Bonding allows more than once interface per port
Packets are forwarded by flow
Visibility
  NetFlow
  sFlow
  Mirroring (SPAN/RSPAN/ERSPAN)
IEEE 802.1Q Support
  Enable virtual LAN function
  By attaching VLAN ID to Linux virtual interfaces, each user will have its own LAN environment separated from other users

## Slide 21: Open vSwitch Concepts(2/2)
Fine-grained ACLs and QoS policies
  L2-­‐L4 matching
  Actions to forward, drop, modify, and queue
  HTB and HFSC queuing disciplines
Centralized control through OpenFlow
Works on Linux-based hypervisors:
  Xen
  XenServer
  KVM
  VirtualBox

## Slide 22: Open vSwitch Contributors(Partial)

## Slide 23: Packets are Managed as Flows(1/2)
A flow may be identied by any combination of
  Input port
  VLAN ID (802.1Q)
  Ethernet Source MAC address
  Ethernet Destination MAC address
  IP Source MAC address
  IP Destination MAC address
  TCP/UDP/... Source Port
  TCP/UDP/... Destination Port

## Slide 24: Packets are Managed as Flows(2/2)
The 1rst packet of a flow is sent to the controller
The controller programs the datapath's actions for a flow
  Usually one, but may be a list
  Actions include:
    Forward to a port or ports, mirror
    Encapsulate and forward to controller
    Drop
And returns the packet to the datapath
Subsequent packets are handled directly by the datapath

## Slide 25: Open vSwitch architecture
Introduction to Open vSwitch
Main components of Open vSwitch
Open vSwitch Testing Case

## Slide 26: Main Components

## Slide 27: ovsdb-­‐server
Database that holds switch--‐level configuration
Custom database with nice properties:
  Value constraints
  Weak references
  Garbage collection
Log--‐based
Speaks management protocol(JSON--‐RPC) to manager and ovs--‐vswitchd

## Slide 28: ovs-­‐vswitchd(1/2)
Core component in the system:
  Communicates with outside world using OpenFlow
  Communicates with ovsdb-­‐server using management protocol
  Communicates with kernel module over netlink
  Communicates with the system through netdev abstract interface
Supports multiple independent datapaths (bridges)
Packet classiﬁer supports eﬃcient ﬂow lookup with wildcards and “explodes” these (possibly) wildcard rules for fast processing by the datapath

## Slide 29: ovs-­‐vswitchd(2/2)
Implements mirroring, bonding, and VLANs through modiﬁcations of the same ﬂow table exposed through OpenFlow
Checks datapath ﬂow counters to handle ﬂow expiration and stats requests

## Slide 30: openvswitch_mod.ko
Kernel module that handles switching and tunneling
Exact-­‐match cache of ﬂows
Designed to be fast and simple
  Packet comes in, if found, associated actions executed and counters updated. Otherwise, sent to userspace
  Does no ﬂow expiration
  Knows nothing of OpenFlow
Implements tunnels

## Slide 31: Tunneling
Required to provide “true” virtual networks
Focus on performance
  Header caching
  Hardware oﬄoading
Supported tunneling modes
  GRE
  GRE-­‐over-­‐IPsec
  CAPWAP

## Slide 32: Migration
KVM and Xen provide Live Migration
With bridging, IP address migration must occur with in the same L2 network
Open vSwitch avoids this problem using GRE tunnels

## Slide 33: Distributed Virtual Switch

## Slide 34: Open vSwitch architecture
Introduction to Open vSwitch
Main components of Open vSwitch
Open vSwitch Testing Case

## Slide 35: Virtual LAN
Per-Customer VLANs are desirable for security reasons
But there is a limit of 4094 VLANs

## Slide 36: Open vSwitch Testing(1/2)
VM1 and VM3 belong to a user assigned with VLAN ID 1 through tap0 virtual interface; VM2 and VM4 belong to a user assigned with VLAN ID 2 through tap1 virtual interface
Data Network is used for VMs to transmit data packets; Management Network is used for out-of-band management and packet mirroring
On both hosts, we have to install an OVS bridge interface (br0) for performing virtual switch function and attach it with physical Data Network interface eth1

## Slide 37: Open vSwitch Testing(2/2)
Attach virtual interfaces of each VM (tap0 and tap1) to the OVS bridge interface (br0) with proper VLAN ID as follows:
Assign VM1~VM4 within the same IP range. Basically, VM1 and VM3 can ping each other and VM2 and VM4 can ping each other successfully
VM1 cannot access VM2 and VM3 cannot access VM4 even they exist on the same host machine

## Slide 38: Open vSwitch
Virtual Switch
Open vSwitch architecture
OpenFlow

## Slide 39: OpenFlow
Introduction to OpenFlow
OpenFlow Switching
Usage models
Virtualizing OpenFlow
FlowVisor-based Virtualization
OpenFlow references

## Slide 40: OpenFlow
Idealized view of a switch’s datapath
Centralized controller conﬁgures ﬂow table
  Lookup based on L2-­‐L4
  Supports full wildcarding and priorities
  Flows associated with actions: forward, drop, modify
  Missed ﬂows go to controller
Remote visibility
  Description of switch (supported actions, ﬂow tables’ sizes, etc.)
  Statistics (ﬂows, tables, ports)

## Slide 41: Nicira Extensions to OpenFlow
Resubmit
NXM (Extensible Match)
  Tunnels
  Registers
  IPv6
  Labels used by new actions
Flexible tunnel tagging
Multiple controllers
Separate setting a QoS queue from transmitting
Multipathing

## Slide 42: Dynamic Flow Aggregation on an OpenFlow Network(1/2)
Scope
  Different Networks want different flow granularity (ISP, Backbone,…)
  Switch resources are limited (flow entries, memory)
  Network management is hard
  Current Solutions : MPLS, IP aggregation

## Slide 43: Dynamic Flow Aggregation on an OpenFlow Network(2/2)
How do OpenFlow Help?
  Dynamically define flow granularity by wildcarding arbitrary header fields
  Granularity is on the switch flow entries, no packet rewrite or encapsulation
  Create meaningful bundles and manage them using your own software (reroute, monitor)

## Slide 44: OpenFlow
Introduction to OpenFlow
OpenFlow Switching
Usage models
Virtualizing OpenFlow
FlowVisor-based Virtualization
OpenFlow references

## Slide 45: OpenFlow Switching
A way to run experiments in the networks
Bring GENI to college campuses
A “pragmatic” compromise
  Allow researchers to run experiments in their network without requiring vendors to expose internal workings
Basic requirements
  An Ethernet switch (e.g. 128-ports of 1GE)
  An open protocol to remotely add/remove flow entries

## Slide 46: Experimenter’s Dream (Vendor’s Nightmare)
Standard
Network
Processing
hw
sw
Experimenter writes experimental code on switch/router
User-
defined
Processing

## Slide 47: No obvious way
Commercial vendor won’t open software and hardware development environment
  Complexity of support
  Market protection and barrier to entry
Hard to build my own
  Prototypes are flakey
  Software only: Too slow
  Hardware/software: Fanout too small (need >100 ports for wiring closet)

## Slide 48: Furthermore, we need…
Isolation
  Regular production traffic untouched
Virtualized and programmable
  Different flows processed in different ways
Equipment we can trust in our wiring closet
Open development environment for all researchers (e.g. Linux, Verilog, etc).
Flexible definitions of a flow
  Individual application traffic
  Aggregated flows
  Alternatives to IP running side-by-side
  …

## Slide 49: OpenFlow Switching
Controller
OpenFlow Switch
Flow
Table
Secure
Channel
PC
OpenFlow
Protocol
SSL
hw
sw
OpenFlow Switch specification

## Slide 50: Flow Table Entry “Type 0” OpenFlow Switch
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
+ mask
Packet + byte counters

## Slide 51: Examples(1/2)
Switching
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
00:1f:..
*
*
*
*
*
*
*
port6
Flow Switching
port3
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
00:20..
00:1f..
0800
vlan1
1.2.3.4
5.6.7.8
4
17264
80
port6
Firewall
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
22
drop

## Slide 52: Examples(2/2)
Routing
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
5.6.7.8
*
*
*
port6
VLAN Switching
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
vlan1
*
*
*
*
*
port6,
port7,
port9
00:1f..

## Slide 53: OpenFlow “Type 1”
Additional actions
  Rewrite headers
  Map to queue/class
  Encrypt
More flexible header
  Allow arbitrary matching of first few bytes
Support multiple controllers
  Load-balancing and reliability

## Slide 54: Secure Channel
SSL Connection, site-specific key
Controller discovery protocol
Encapsulate packets for controller
Send link/port state to controller

## Slide 55
Controller
PC
OpenFlow
Access Point
Server room
OpenFlow
OpenFlow
OpenFlow
OpenFlow-enabled
Commercial Switch
Flow
Table
Secure
Channel
Normal
Software
Normal
Datapath

## Slide 56: OpenFlow
Introduction to OpenFlow
OpenFlow Switching
Usage models
Virtualizing OpenFlow
FlowVisor-based Virtualization
OpenFlow references

## Slide 57: OpenFlow Usage Models(1/2)
Experiments at the flow level
  User-defined routing protocols
  Admission control
  Network access control
  Network management
  Energy management
  VOIP mobility and handoff
  …
Experiments at the packet level
  Slow: Controller handles packet processing
  Fast: Redirect flows through programmable hardware
  Modified routers, firewalls, NAT, congestion control…
Alternatives to IP
Experiment-specific controllers
Static or dynamic flow-entries

## Slide 58: Example Experiment at the flow level Mobility
Lots of interesting questions
Management of flows
Control of switches
Access control of users and devices
Tracking user location and motion

## Slide 59: Experiments at the packet level
Controller
PC
NetFPGA
Laboratory
OpenFlow-enabled
Commercial Switch
Flow
Table
Secure
Channel
Normal
Software
Normal
Datapath

## Slide 60: OpenFlow Usage Models(2/2)
Experiments at the flow level
Experiments at the packet level
Alternatives to IP
  Flow-table is Layer-2 based
  e.g. new naming and addressing schemes
  …

## Slide 61: OpenFlow
Introduction to OpenFlow
OpenFlow Switching
Usage models
Virtualizing OpenFlow
FlowVisor-based Virtualization
OpenFlow references

## Slide 62: Network Virtualization
Network Operators “Delegate” control of subsets of network hardware and/or traffic to other Network Operators or Users
Multiple Controllers can talk to same set of switches
Imagine a Hypervisor for network equipment
Allows experiments to be run on the network in isolation of each other and production traffic

## Slide 63: Trend
Windows
(OS)
Windows
(OS)
Linux
Mac
OS
x86
(Computer)
Windows
(OS)
App
App
Linux
Linux
Mac
OS
Mac
OS
Virtualization layer
App
Controller 1
App
App
Controller
2
Virtualization or “Slicing”
App
OpenFlow
Controller 1
NOX
(Network OS)
Controller
2
Network OS
Computer Industry
Network Industry
Notes: Hidden slide (just for backup reasons)
Shows how far along we can go in opening up the network
63

## Slide 64
Simple Packet Forwarding Hardware
Network Operating System 1
Open interface to hardware
Virtualization or “Slicing” Layer
Network Operating System 2
Network Operating System 3
Network Operating System 4
App
App
App
App
App
App
App
App
Many operating systems, or
Many versions
Open interface to hardware
Isolated “slices”
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware

## Slide 65: Switch Based Virtualization Exists for NEC, HP switches but not flexible enough
Normal L2/L3 Processing
Flow Table
Production VLANs
Research VLAN 1
Controller
Research VLAN 2
Flow Table
Controller
Notes: Experiments running on PRODUCTION infrastructure
Key to get scale, key to get traffic on the network
(e.g. can’t just do a reset...)

## Slide 66: OpenFlow
Introduction to OpenFlow
OpenFlow Switching
Usage models
Virtualizing OpenFlow
FlowVisor-based Virtualization
OpenFlow references

## Slide 67: FlowVisor
Network Hypervisor developed by Stanford
A software proxy between the forwarding and control planes of network devices

## Slide 68: FlowVisor-based Virtualization(1/2)
OpenFlow
Switch
OpenFlow
Protocol
OpenFlow FlowVisor & Policy Control
Craig’s
Controller
Heidi’s
Controller
Aaron’s
Controller
OpenFlow
Protocol
OpenFlow
Switch
OpenFlow
Switch
68
Topology discovery is per slice

## Slide 69
OpenFlow
Protocol
OpenFlow
FlowVisor & Policy Control
Broadcast
Multicast
OpenFlow
Protocol
http
Load-balancer
FlowVisor-based Virtualization(2/2)
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
Separation not only
by VLANs, but any
L1-L4 pattern
dl_dst=FFFFFFFFFFFF
tp_src=80, or tp_dst=80

## Slide 70: FlowVisor Slicing
Slices are defined using a slice definition policy
  The policy language specifies the slice’s resource limits, flowspace, and controller’s location in terms of IP and TCP port-pair
  FlowVisor enforces transparency and isolation between slices by inspecting, rewriting, and policing OpenFlow messages as they pass

## Slide 71: FlowVisor Resource Limits
FV assigns hardware resources to “Slices”
  Topology
    Network Device or Openflow Instance (DPID)
    Physical Ports
  Bandwidth
    Each slice can be assigned a per port queue with a fraction of the total bandwidth
  CPU
    Employs Course Rate Limiting techniques to keep new flow events from one slice from overrunning the CPU
  Forwarding Tables
    Each slice has a finite quota of forwarding rules per device

## Slide 72: Slicing
Notes:     Carves Network into “Slices” and Assigns hardware resources to each slice. Switch DPID, Port.

## Slide 73: FlowVisor FlowSpace
FlowSpace is defined by a collection of packet headers and assigned to “Slices”
  Src/Dst MAC Address
  VLAN ID
  Ethertype
  IP Protocol
  Src/Dst IP Address
  ToS/DSCP
  Src/Dst Port Number

## Slide 74: FlowSpace: Maps Packets to Slices

## Slide 75: FlowVisor Slicing Policy(1/2)
FV intercepts OF messages from devices
  FV only sends control plane messages to the Slice controller if the src device is in the Slice Topology.
  Rewrites OF feature negotiation messages so the slice controller only sees the ports in it’s slice
  Port up/down messages are pruned and only forwarded to affected slices

## Slide 76: FlowVisor Slicing Policy(2/2)
FV intercepts OF messages from controllers
  Rewrites Flow Insertion, Deletion & Modifications so they don’t violate the slice definition
    Flow definition – ex. Limit Control to HTTP traffic only
    Actions – ex. Limit forwarding to only ports in the slice
  Expand Flow rules into multiple rules to fit policy
    Flow definition – ex. If there is a policy for John’s HTTP traffic and another for Uwe’s HTTP traffic, FV would expand a single rule intended to control all HTTP traffic into 2 rules.
    Actions – ex. Rule action is send out all ports. FV will create one rule for each port in the slice.
  Returns “action is invalid” error if trying to control a port outside of the slice

## Slide 77: FlowVisor Message Handling
OpenFlow
Firmware
Data Path
Alice
Controller
Bob
Controller
Cathy
Controller
FlowVisor
OpenFlow
OpenFlow
Packet
Exception
Policy Check:
Is this rule allowed?
Policy Check:
Who controls this packet?
Full Line Rate
Forwarding
Rule
Packet

## Slide 78: OpenFlow
Introduction to OpenFlow
OpenFlow Switching
Usage models
Virtualizing OpenFlow
FlowVisor-based Virtualization
OpenFlow references

## Slide 79: OpenFlow Consortium
http://OpenFlowSwitch.org
Goal
  Evangelize OpenFlow to vendors
  Free membership for all researchers
  Whitepaper, OpenFlow Switch Specification, Reference Designs
  Licensing: Free for research and commercial use

## Slide 80: OpenFlow building blocks
Controller
NOX
Slicing
Software
FlowVisor
FlowVisor
Console
80
Applications
LAVI
ENVI (GUI)
Expedient
n-Casting
NetFPGA
Software
Ref. Switch
Broadcom
Ref. Switch
OpenWRT
PCEngine WiFi AP
Commercial Switches
Stanford Provided
OpenFlow
Switches
ONIX
Stanford Provided
Monitoring/ debugging tools
oflops
oftrace
openseer
Open vSwitch
HP, NEC, Pronto, Juniper.. and many more
Beacon
Trema
Maestro
Notes: There are components at different levels that work together in making it work
The commercial switch details will follow in next slide
There are a plethora of applications possible. I only list those available at Stanford

## Slide 81: Current SDN hardware
Ciena Coredirector
NEC IP8800
Ask your vendors
Juniper MX-series
HP Procurve 5400
Pronto 3240/3290
WiMax (NEC)
PC Engines
Netgear 7324
81

## Slide 82: Commercial Switch Vendors
Model | Virtualize | Notes | 
HP Procurve 5400zl or 6600 | 1 OF instance per VLAN | LACP, VLAN and STP processing before OpenFlow Wildcard rules or non-IP pkts processed in s/w Header rewriting in s/w CPU protects mgmt during loop | 
NEC IP8800 | 1 OF instance per VLAN | OpenFlow takes precedence Most actions processed in hardware MAC header rewriting in h/w | 
Pronto 3240 or 3290 with Pica8 or Indigo firmware | 1 OF instance per switch | No legacy protocols (like VLAN and STP) Most actions processed in hardware MAC header rewriting in h/w | 
82
Notes: All support ver 1.0
All have approx 1500 flow table entry limit

## Slide 83: OpenFlow Controllers
Name | Lang | Platform(s) | License | Original Author | Notes
OpenFlow Reference | C | Linux | OpenFlow License | Stanford/Nicira | not designed for extensibility
NOX | Python, C++ | Linux | GPL | Nicira | actively developed
Beacon | Java | Win, Mac, Linux, Android | GPL (core), FOSS Licenses for your code | David Erickson (Stanford) | runtime modular, web UI framework, regression test framework
Maestro | Java | Win, Mac, Linux | LGPL | Zheng Cai (Rice) | 
Trema | Ruby, C | Linux | GPL | NEC | includes emulator, regression test framework
RouteFlow | ? | Linux | Apache | CPqD (Brazil) | virtual IP routing as a service
Notes: Language open-source Performance cross-platform runtime modular

## Slide 84: Growing Community
Vendors and start-ups
Providers and business-unit
More...
More...
84
Note: Level of interest varies

## Slide 85: Related Research
DIFANE
  Rule partitioning for controller-less flow insertion
UCSD Fat Tree Series: Scalable Commodity Data Center, PortLand, Hedera
  Scale-out data centers that use OpenFlow
Tesseract
  Centralized WAN in the 4D Architecture
ONIX
  Fault-tolerant controller platform from Nicira, Google, NEC
DevoFlow
  Practical scalability limits to OpenFlow and modifications to get around them

## Slide 86: References
Network Virtualization with Cloud Virtual Switch
S. Horman, “An Introduction to Open vSwitch,” LinuxCon Japan, Yokohama, Jun. 2, 2011.
J. Pettit, J. Gross “Open vSwitch Overview,” Linux Collaboration Summit, San Francisco, Apr. 7, 2011.
J. Pettit, “Open vSwitch: A Whirlwind Tour,” Mar. 3, 2011.
Access Layer Network Virtualization: VN-Tag and VEPA
OpenFlow Tutorial