## Slide 1: GPU communication systems: Collective Communication from Libraries to Hardware 2026.1.22
Haoran Kong
School of Data Science
Chinese University of Hong Kong, Shenzhen

## Slide 2: Outline
Introduction (3 min)
Background & Motivation (11 min)
Proposed Methods & Performance Evaluation (24 min)
  MSCCL++ (8 min)
  syCCL (8 min)
  NCCLX (8 min)
Conclusions (2 min)
Q & A (5 min)

## Slide 3: Outline
Introduction (3 min)
Background & Motivation (11 min)
Proposed Methods & Performance Evaluation (24 min)
  MSCCL++ (8 min)
  syCCL (8 min)
  NCCLX (8 min)
Conclusions (2 min)
Q & A (5 min)

## Slide 4: Introduction – CCL (1/3)
What is CCL?
  A Collective Communication Library (CCL) is a specialized set of software tools that allows multiple processors (CPUs or GPUs) to talk to each other efficiently.

## Slide 5: Introduction – CCL (2/3)
Why use CCL?
  ML workloads are going distributed
    Larger and larger training scale (All-reduce, Reduce-scatter, All-gather)
    Massive expert parallelism in MoE (All to All like)
  Collectives are central to scalability in a variety of key applications:
    Parallel FFT (Transposition is all-to-all)
    Molecular Dynamics (All-reduce)
    Graph Analytics (All-to-all)
  While various solutions—including NCCL, MPI, and DeepEP—address different layers of this challenge, this discussion focuses specifically on GPU-directed CCLs.

## Slide 6: Introduction – CCL (3/3)
How CCLs work?
  Core Idea: a battle between algorithmic efficiency and hardware constraints
  At its heart, a CCL must balance two competing goals:
    High Throughput: Maximizing the volume of data moved by saturating every available lane of the network.
    Low Latency: Minimizing the "handshake" time between devices, which is critical for small-message synchronization in modern AI.
  Scaling requires topology-aware implementation.
    While many assume a simple "Fat Tree" network architecture, real-world systems are often much more complex.
    A CCL must adapt its routing to the specific physical layout of the cluster.

## Slide 7: Outline
Introduction (3 min)
Background & Motivation (11 min)
Proposed Methods & Performance Evaluation (24 min)
  MSCCL++ (8 min)
  syCCL (8 min)
  NCCLX (8 min)
Conclusions (2 min)
Q & A (5 min)

## Slide 8: Background & Motivation (1/4)
Challenges of CCL for multi-GPU systems:
While NVIDIA’s NCCL remains the industry benchmark, it encounters several critical bottlenecks as we scale to next-generation workloads:
  Inefficient Initialization: Connection setup is often slow, and the library occasionally fails to identify the mathematically optimal communication topology for complex clusters.
  Small-Message Latency: High overhead per message makes NCCL inefficient for the fine-grained communication patterns.
  Resource Contention: NCCL statically reserves a significant number of Streaming Multiprocessors (SMs), leading to suboptimal GPU resource utilization and 'stealing' compute power from the actual kernels.

## Slide 9: Background & Motivation (2/4)
Solution: The Evolution of NCCL (v2.27 & v2.28)
The latest advancements in NCCL , targeting small-message latency and resource contention, address some fundamental bottlenecks of distributed scaling.
Four Features codesigned with hardware:
  SHARP: In-Network Reduction Offloading
  GPU-Initiated Networking (GIN) & Device-side APIs
  Symmetric Memory Support: Identical virtual address buffers across multiple GPUs
  Copy Engine-Based Collectives: Zero-SM Involvement

## Slide 10: Background & Motivation (3/4)
Solution: The Architectural Evolution of NCCL
  Symmetric Memory enables highly optimized, direct-access memory patterns. This streamlines data routing and serves as the foundation for the observed 9x reduction in small-message latency.
  By bypassing the host-driven control path, GPU Initiated Networking eliminates the costly CPU-to-GPU handshake. This transition to autonomous, device-level orchestration drastically reduces overhead.
  NCCL leverages In-Network Computing (SHARP) and dedicated Copy Engines to offload reduction and data-movement tasks. By migrating these operations from general-purpose SMs to specialized hardware, the system reclaims vital compute cycles and achieves true hardware-level overlap between communication and computation without resource contention.

## Slide 11: Background & Motivation (4/4)
New problem encountered: The "Implementation Gap"
  The Hardware-Software Friction: Cutting-edge AI applications are being developed over fast-evolving, heterogeneous, nascent hardware. Achieving peak communication performance currently mandates writing custom, low-level code from scratch, which is time-consuming and prone to technical debt.
  The Rigidity of Current Standards: Existing open-source CCLs (such as NCCL) rely on fixed schedules and cannot adjust to varying topology and model requirements.
  The 100K-GPU Bottleneck: As LLMs scale to clusters with over 100,000-GPU clusters, traditional collective communication methods encounter fundamental throughput and latency bottlenecks, limiting both efficient training and practical deployment.
How to improve?
  Develop a reusable, high-level communication library that abstracts hardware complexity.
  Implement efficient search strategies to explore the vast space of communication sub-demands.
  Other solutions …

## Slide 12: Outline
Introduction (3 min)
Background & Motivation (11 min)
Proposed Methods & Performance Evaluation (24 min)
  MSCCL++ (8 min)
  syCCL (8 min)
  NCCLX (8 min)
Conclusions (2 min)
Q & A (5 min)

## Slide 13: Outline
Introduction (3 min)
Background & Motivation (11 min)
Proposed Methods & Performance Evaluation (24 min)
  MSCCL++ (8 min)
  syCCL (8 min)
  NCCLX (8 min)
Conclusions (2 min)
Q & A (5 min)

## Slide 14: MSCCL++ (1/6)
There are various communication channels:
  CPU-GPU: PCIe, NVLink-C2C
  Intra-node: NVLink, xGMI,
  Inter-node: RDMA (IB, RoCE)
Portability and Performance: MSCCL++ provides a reusable lib
  a primitive interface provides a minimal hardware abstraction
  higher-level portable interfaces and specialized implementations
MSCCL++ fundamentally rethinks GPU communication abstractions to address the limitations of existing libraries (like NCCL) in the face of rapidly evolving AI hardware and specialized workloads.

## Slide 15: MSCCL++ (2/6)
Architecture Overview
MSCCL++ are building with an abstraction for various communication channels.
  PortChannel: DMA engines on GPUs or RDMA NICs.
  MemoryChannel: peer-to-peer memory access over NVLink / xGMI.
  SwitchChannel: interconnection-switch-enabled multimem memory.

## Slide 16: MSCCL++ (3/6)
Architecture Overview
All MSCCL++ primitives are defined as a method of a channel.
  put: asynchronously transfers data from one GPU to another.
  signal and wait: synchronize data transfer between GPUs.
  flush: ensures the completion of preceded data transfer.

## Slide 17: MSCCL++ (4/6)
Key ideas: ML workloads move fast! Separate high-level abstractions and optimizations from primitive hardware abstractions.
  Application developers optimize and fine-tune by enabling precise control of the hardware
  Library developers support new hardware features by only providing a shallow layer of abstraction over it
Basically, they are building a reusable communication library with an abstraction for various communication channels.

## Slide 18: MSCCL++ (5/6)
Code Example

## Slide 19: MSCCL++ (6/6)
Evaluation

## Slide 20: Outline
Introduction (3 min)
Background & Motivation (11 min)
Proposed Methods & Performance Evaluation (24 min)
  MSCCL++ (8 min)
  syCCL (8 min)
  NCCLX (8 min)
Conclusions (2 min)
Q & A (5 min)

## Slide 21: syCCL (1/7)
SyCCL reduces the exponential search space of large-scale collective scheduling by synergistically exploiting topological and collective symmetries to decompose global communication demands into tractable sub-problems.

## Slide 22: syCCL (2/7)
Three-Step Strategy Overview
  Decompose: By utilizing symmetry, a large-scale communication demand (e.g., AllGather across 1024 GPUs) is broken down into multiple "sub-demands" mapped to smaller topological subsets (e.g., an 8-GPU single node).

## Slide 23: syCCL (3/7)
Three-Step Strategy Overview
  Search: Within the significantly reduced search space, a Mixed Integer Linear Programming (MILP) solver can find the optimal sub-schedules for the sub-topology in just a few minutes.
  Integrate: These sub-schedules are assembled like building blocks. Through symmetry mapping, they are reconfigured into a complete, comprehensive scheduling plan that covers the entire large-scale cluster.

## Slide 24: syCCL (4/7)
Architecture Overview
  Sketch Exploration searches and composes candidate communication structures to generate high-quality sketches.
  Schedule Synthesis generates concrete communication schedules and evaluates their performance given a sketch.

## Slide 25: syCCL (5/7)
Evaluation

## Slide 26: syCCL (6/7)
Evaluation

## Slide 27: syCCL (7/7)
Evaluation

## Slide 28: Outline
Introduction (3 min)
Background & Motivation (11 min)
Proposed Methods & Performance Evaluation (24 min)
  MSCCL++ (8 min)
  syCCL (8 min)
  NCCLX (8 min)
Conclusions (2 min)
Q & A (5 min)

## Slide 29: NCCLX (1/9)
Key Features
  Host-driven customization framework
  SM-free, zero-copy communication
  Tensor registration management for zero-copy
  CTran and network co-design
  Pipeline Parallelism: zero-copy and SM-free send/receive
  Tensor Parallelism: fine-grained overlap via RMA Put
  Hybrid Sharding Data Parallelism: fault-tolerant AllReduce

## Slide 30: NCCLX (2/9)
Key Features
  GPU-resident collectives for imbalance-aware inference
  Low-latency optimizations for small messages
  Scalable initialization for large-scale training
  Efficient resource management
  Fast fault localization and debugging support

## Slide 31: NCCLX (3/9)
Architecture Overview
Host-initiated APIs
  Communication fully orchestrated by CPU
  Removes unnecessary CPU–GPU synchronizations
  Enables easy implementation of custom collectives
Host-initiated APIs with GPU-resident metadata
  Host initiates communication
  Decision-making uses metadata resident on GPUs
  Designed for adaptive collectives, e.g., MoE routing-dependent communication

## Slide 32: NCCLX (4/9)
Core Transport Layer: CTran, a custom-designed transport layer.
Its design is guided by two key principles: promoting zero-copy data transfer and avoiding GPU SM occupation whenever possible.
  provides unified support for multiple execution models
  offers richer communication semantics
  supports multiple network backends, including NVLink, IB / RoCE and socket-based transports
  highly optimized communication critical path

## Slide 33: NCCLX (5/9)
Software tooling stack overview

## Slide 34: NCCLX (6/9)
ncclAllToAllv copies communication metadata (e.g., send counts) during both the initialization and enqueue phases. After the operation is enqueued on the CPU, other GPU kernels (e.g., the MoE router kernel), which may start execution before ncclAllToAllv, can modify the metadata stored in the original data structures.
In the design of GPU-resident collectives, AllToAllvDynamic takes metadata by reference rather than copying it during the enqueue phase.

## Slide 35: NCCLX (7/9)
Evaluation

## Slide 36: NCCLX (7/9)
Evaluation

## Slide 37: NCCLX (9/9)
Evaluation

## Slide 38: Outline
Introduction (3 min)
Background & Motivation (11 min)
Proposed Methods & Performance Evaluation (24 min)
  MSCCL++ (8 min)
  syCCL (8 min)
  NCCLX (8 min)
Conclusions (2 min)
Q & A (5 min)

## Slide 39: Conclusions
Scheduling: From "Fixed Algorithms" to "Topology-Aware Synthesis".
Efficiency: From "Resource Contention" to "Hardware Offloading" .
Abstraction: From "Black-Box Libraries" to "Decoupled Primitives".
Scalability: From "Local Tuning" to "Systemic Self-Healing".
Summary:
Collective communication is evolving from a "monolithic library" into a deep hardware-software co-designed system—driven by mathematical synthesis, executed by dedicated hardware, and empowered by decoupled primitives.

## Slide 40: Outline
Introduction (3 min)
Background & Motivation (11 min)
Proposed Methods & Performance Evaluation (24 min)
  MSCCL++ (8 min)
  syCCL (8 min)
  NCCLX (8 min)
Conclusions (2 min)
Q & A (5 min)