## Slide 1: DDA2001 – Guest Lecture Computer System
Prof. Yeh-Ching Chung
School of Data Science
Chinese University of Hong Kong, Shenzhen

## Slide 2: Outline
Introduction
Computer Hardware
  ISA
Computer Software
  System Software
  Application Software
How Software and Hardware Co-Work
Conclusions

## Slide 3: Introduction

## Slide 4: Computers (1)
Desktop computers
  Designed to deliver good performance to a single user at a low cost.
  Usually executing third-party software.
  Usually incorporating a graphics display, a keyboard and a mouse.

## Slide 5: Computers (2)
Servers
  Used to run larger program for multiple users simultaneously, typically accessed only via a network, with a greater emphasis on dependability and (often) security.
Supercomputers
  A high performance, high-cost class of servers with a large number of processors, huge memory and storage that are used for high-end scientific and engineering applications.
Embedded computers (microprocessors)
  A computer within another system with a dedicated function or application.

## Slide 6: Supercomputers
Sunway TaihuLight
  Fastest supercomputer in the world (as of June 2017)
  Over 10 million CPU cores
  Power: 15 MW
  Speed: 93 PFLOPS
http://www.nsccwx.cn/wxcyw/

## Slide 7: Automotive Embedded Systems
https://dcvizcayno.wordpress.com/2015/08/28/the-future-of-technology-privacy-security-and-risks-part-3-of-5/

## Slide 8: Post-PC Era
Personal Mobile Devices
  Battery-operated devices with wireless connectivity.
Warehouse-Scale Computers
  Datacenter containing hundreds of thousands of servers providing software as a service (SaaS).

## Slide 9: Evolution of Computer Hardware (1)
1st transistor invented by John Bardeen, Walter Brattain, and William Shockley at Bell Labs in 1947.
UNIVAC I (UNIVersal Automatic Computer I): 1st commercial computer sold in US in 1951.

## Slide 10: Evolution of Computer Hardware (2)
1st integrated circuit invented by Jack Kilby of Texas Instruments in 1958.
IBM System/360: 1st family of computers in 1964 with a range of performance but with the same instruction set.

## Slide 11: Evolution of Computer Hardware (3)
Intel 4004: 1st commercially available microprocessor by Intel in 1971.
https://en.wikipedia.org/wiki/Intel_4004

## Slide 12: IC Manufacturing Process
Yield: proportion of working dies per wafer.

## Slide 13: Intel Core i7 Wafer
300-mm wafer, 280 dies at 100% yield (32-nm technology).

## Slide 14: Moore’s Law（1）
Processor
  Logic capacity: increases about 30% per year
  Performance: 2× every 1.5 years
Memory
  DRAM capacity: 4× every 3 years, about 60% per year
  Memory speed: 1.5× every 10 years
  Cost per bit: decreases about 25% per year
Storage
  Capacity: increases about 60% per year

## Slide 15: Moore’s Law（2）
http://www.itrs2.net/

## Slide 16: hardware

## Slide 17: Major Components of a Computer
  (keyboard, mouse)
  (display, printer)
  (cache, SRAM, disk drive, etc.)

## Slide 18: Machine Organization
Capabilities and performance characteristics of the principal functional units (e.g., registers, ALU, shifters, logic units)
Ways in which these components are interconnected
Logic and means by which such information flow is controlled
Instruction Set Architecture (ISA)
Register Transfer Level (RTL) description

## Slide 19: Instruction Set Architecture (ISA)
ISA, or simply architecture – the abstract interface between the hardware and the lowest level software that includes all the information necessary to write a machine language program, including instructions, registers, memory access, I/O, etc.
Enables implementations of varying cost and performance to run identical software.
The combination of the basic instruction set (the ISA) and the operating system interface is called the Application Binary Interface (ABI).
  The user portion of the instruction set plus the operating system interfaces used by application programmers.
  Define a standard for binary portability across computers.

## Slide 20: Related Courses
Digital Logic (switching circuit)
  AND-gate, Or-gate, etc.
Computer architecture
  CPU, memory, etc.
VLSI
  VLSI compiler (from High-level synthesis to RTL code)
  EDA tools

## Slide 21: Software

## Slide 22: Software
System software
  Operating systems
  Compiler/Assembler
  Linker
  Loader
Application software
  Redis
  QEMU
  Programming languages (C, C++, etc.)
  Database management systems (MySQL, etc.)
Application Software
System Software
Hardware

## Slide 23: System Software
Operating System
  Supervise program that interfaces the user’s program with the hardware (e.g., Linux, iOS, Windows)
  Handles basic input and output operations
  Allocates storage and memory
  Provides for protected sharing among multiple applications
Compiler
  Translate high-level language programs (e.g., C, Java) into instructions that the hardware can execute

## Slide 24: Application Software
Application software
  Redis
  Docker
  QEMU
  Programming languages (C, C++, etc.)
  Database management systems (MySQL, etc.)
  …..

## Slide 25: Software and Hardware Co-Work

## Slide 26: Program Compilation

## Slide 27: Code Input to Device
Memory
Processor
Devices
Network
Input
Output
Control
Datapath
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000
Object Code

## Slide 28: Code Stored in Memory
Memory
Processor
Devices
Network
Input
Output
Control
Datapath
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000

## Slide 29: Code Fetch from Memory
Memory
Processor
Devices
Network
Input
Output
Control
Datapath
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000

## Slide 30: Decoding Code
Processor
Devices
Network
Input
Output
Control
Datapath
000000 00100 00010 0001000000100000
Memory

## Slide 31: Executing Code
Control unit decodes the instruction to determine what to execute
Datapath unit executes the instruction as directed by control
Processor
Devices
Network
Input
Output
Control
Datapath
Memory
Add Reg #4 and Reg #2, put result in Reg #2
000000 00100 00010 0001000000100000

## Slide 32: The Cycle
Processor fetches the next instruction from memory
How does it know which location in memory to fetch from next?
Fetch
Decode
Execute

## Slide 33: Data Output to Device
Memory
Processor
Devices
Network
Input
Output
Control
Datapath
00000100010100000000000000000000
00000000010011110000000000000100
00000011111000000000000000001000

## Slide 34: Conclusions
A computer consists of two components - hardware and software
Computer architecture course discuss the main components of hardware
OS, compiler, linker, and loader form the main components of system software

## Slide 35
Q & A